## Slide 1: Levelized Cost of Wind
J. McCalley
EE 459/559
Notes: Check Ackermann’s “Wind power in power systems,” chapter 13 by Nick Miller, et al, section 13.4, for “Economic evaluation factors.”

## Slide 2: Discount rate
The discount rate, i, is the
annual payment as percentage of the amount owed.
The discount rate value may be thought of as reflecting the value given to possession of money now rather than later, since having it now allows it to be invested to earn a return. In this sense, the discount rate is the
annual income as percentage of the amount
invested, i.e., the average interest rate.

## Slide 3: Moving single amounts in time
“Present” amount of money
“Future” amount of money
Number of time periods
Observe that “F” may be a cost or a revenue. In either case, the equivalent amount of money in the present is smaller.
I prefer to incur a $100 cost later than a $100 cost now (If I spend the $100 later, I can keep it now and draw interest on it).
I prefer to obtain a $100 revenue now than a $100 revenue later (If I obtain it now, I can draw interest on it; so the value to me of obtaining it in the future is less.)

## Slide 4: Annuitizing
“Annual” amount of money
Note that payment A is made at the end of a period, so there is no payment made at the beginning of period 1; there is a payment made at the end of period N.

## Slide 5: Inflation
Discount rates may be given independent of the effects of inflation. This is the interest rate that is typically quoted on savings accounts, bonds, and loans; it quantifies the amount of amount you are paid (when you save or buy a bond) or must pay (when you obtain a loan). For example, if your savings account pays you 4% per year, and you deposit $100 at the beginning of the year, you will have $104 at the end of the year.
The 4% is called the nominal discount rate. We will represent it as in.

## Slide 6: Inflation
Now assume inflation is e=3% per year. Then, at a nominal rate of in=4%, the $104 at the end of year has a buying power that is diminished by e=3% relative to the beginning of the year. And so
You can see that this is correct as follows. Assume you hold $100.97 in your hands (and so there is no interest from the bank) for a year during which inflation is e=3%, and you ask, at year-end: “What was this $100.97 worth at the beginning of the year?” The answer would be:

## Slide 7: Inflation
Now here is another question: What is the interest rate that, when applied to the original $100, will give us $100.97? We might call this the effective interest rate, but the normal terminology is to call this the real interest (or discount) rate; we denote it by ir. And so:
Writing in terms of in and e, we obtain:

## Slide 8: Inflation
That is,
Solving for in results in:
Eliminating the “1”:
These are “exact” relations and should be used in calculations. But because e and ir are small numbers, the product ire is very small, and we obtain
These are useful for recalling relations between in, ir, e.
The Fisher equation.

## Slide 9: Inflation
Caution: It is tempting to think that, because inflation adds to ir to obtain in, that in represents inflation. This is not the case. Inflation is an effect that is counter to the interest (or discount) rate. With this in mind, the relation ir=in-e shows that it is the real interest rate that includes the effect of inflation.

## Slide 10: Inflation
Current or nominal dollars are actual cash flows that would occur during each particular year and are not, therefore, referenced to a particular year. Use nominal discount rate with current dollars.
Constant or real dollars adjust for inflation and are therefore “constant-value” dollars, i.e., their expression in one year has equivalent buying power as their (adjusted) expression in another year. Constant dollars are always referenced to a particular year, e.g., “2015 dollars.” Use real discount rate with constant dollars.
Unless otherwise stated, assume we use constant dollars with the real discount rate.
For example, when converting a series of cash flows to a present worth value,
If cash flows are current dollars (not inflation-adjusted), use nominal discount rate.
If cash flows are constant dollars (inflation-adjusted), use real discount rate.

## Slide 11: Fixed Costs
Investment costs:
These costs occur each year over the life of the plant and may be annuitized.

## Slide 12: Fixed costs
Non-investment fixed costs:
These costs occur each year over the life of the plant and may be annuitized.

## Slide 13: Levelizing Fixed Costs
To levelize (or annuitize) the fixed costs over a period of N years, we can do the following:
1. Obtain the present worth of all of future costs Ft, t=1,…,N via:
2. Annuitize this present worth cost to obtain the levelized annual revenue requirements (LARR):

## Slide 14: Fixed Charge Rate
The fixed charge rate is then given by
http://www.eia.gov/forecasts/aeo/assumptions/pdf/table_8.2.pdf
The overnight cost for a particular generation technology is the cost in $/kW to build that technology if it could be done in a single day. It does not include the allowance for funds used during construction, AFUDC.
Overnight costs are estimated by the US Energy Information Administration. For 2016, see

## Slide 15: Overnight cost
Observe this is stated in 2015 dollars. If we want to invest in a wind turbine in 2020, we can increase this cost by (1+e)5 and then use ir as discount rate. Alternatively, we can use the 2015 value in 2020 and then use in as discount rate.
www.eia.gov/forecasts/aeo/assumptions/pdf/table_8.2.pdf

## Slide 16: Notes on previous table
www.eia.gov/forecasts/aeo/assumptions/pdf/table_8.2.pdf

## Slide 17: Computation of LARR
www.eia.gov/forecasts/aeo/assumptions/pdf/table_8.2.pdf
Given the FCR and the overnight cost, the LARR is then computed according to

## Slide 18: Annual Operating Expenses (AOE)
The annual operating expenses (AOE) include
annual land lease cost (LLC)
levelized O&M cost (LOM), and
levelized replacement cost (LRC)
with units of $/year.
with units of $/year.

## Slide 19: Levelized cost of energy
We observe that LCOE is a function:
LARR:
  Investment costs
  Non-investment fixed costs
AOE:
  Operating cost
  Maintenance costs
Average Annual Energy Production Capacity
  Capacity
  Capacity factor

## Slide 20: Levelized cost of energy
When AOE is given in $/year.
When AOE is given in $/MWhr.

## Slide 21: Three good LCOE references
US DOE Energy Information Administration (EIA), “Levelized Cost and Levelized Avoided Cost of New Generation Resources in the Annual Energy Outlook 2016,” August 2016, available at www.eia.gov/forecasts/aeo/pdf/electricity_generation.pdf.
S. Tegen, M. Hand, B. Maples, E. Lantz, P. Schwabe, and A. Smith, “2010 Cost of Wind Energy Review,” NREL/TP-5000-52920, April 2012, available at http://www.nrel.gov/docs/fy12osti/52920.pdf.
C. Mone, T. Stehly, B. Maples, and E. Settle, “2014 Cost of Wind Energy Review,” NREL/TP-6A20-64281, October 2015, available at http://www.nrel.gov/docs/fy16osti/64281.pdf.

## Slide 22: Levelized cost of energy
Data | Wind Turbine
Purchase cost | $1820/kW
Installation cost | $600000
Levelized fixed charge rate | 20%
Plant rating | 1.5 MW
Capacity factor | 0.35
Discount rate | 8%
Levelized fixed charge rate:
Return on investment
Depreciation
Fed and state income taxes
Property tax
Insurance costs
The initial investment is
($1820/kw)*1500kW+600000=$3,300,000
The fixed annual charges are then 0.2*3,300,000=$660,000.
This is called the levelized annual revenue requirements (LARR)
The average annual energy production is
=Capacity*8760hrs/yr*CapacityFactor
=1.5MW*8760hrs/yr*.35=4599MWhrs
Assume annual operating expenses are 0;
and PTC impact is not included.

## Slide 23: Levelized cost of energy
Data | Wind Turbine
Purchase cost | $1820/kW
Installation cost | $600000
Levelized fixed charge rate | 11.6%
Plant rating | 1.5 MW
Capacity factor | 0.35
Discount rate | 8%
Levelized fixed charge rate:
Return on investment
Depreciation
Fed and state income taxes
Property tax
Insurance costs
The initial investment is
($1820/kw)*1500kW+600000=$3,300,000
The fixed annual charges are then 0.116*3,300,000=$382,800.
This is called the levelized annual revenue requirements (LARR)
The average annual energy production is
=Capacity*8760hrs/yr*CapacityFactor
=1.5MW*8760hrs/yr*.35=4599MWhrs
Assume annual operating expenses are 0;
and PTC impact is not included.

## Slide 24: Levelized cost of energy
Data | Wind Turbine
Purchase cost | $1820/kW
Installation cost | $600000
Levelized fixed charge rate | 20%
Plant rating | 1.5 MW
Capacity factor | 0.40
Dscount rate | 8%
Levelized fixed charge rate:
Return on investment
Depreciation
Fed and state income taxes
Property tax
Insurance costs
The initial investment is
($1820/kw)*1500kW+600000=$3,300,000
The fixed annual charges are then 0.2*3,300,000=$660,000.
This is called the levelized annual revenue requirements (LARR)
The average annual energy production is
=Capacity*8760hrs/yr*CapacityFactor
=1.5MW*8760hrs/yr*.40=5256MWhrs
Assume annual operating expenses are 0;
and PTC impact is not included.

## Slide 25: Levelized cost of energy
Data | Wind Turbine
Purchase cost | $1820/kW
Installation cost | $600000
Levelized fixed charge rate | 11.6%
Plant rating | 1.5 MW
Capacity factor | 0.40
Discount rate | 8%
Levelized fixed charge rate:
Return on investment
Depreciation
Fed and state income taxes
Property tax
Insurance costs
The initial investment is
($1820/kw)*1500kW+600000=$3,300,000
The fixed annual charges are then 0.116*3,300,000=$382,800.
This is called the levelized annual revenue requirements (LARR)
The average annual energy production is
=Capacity*8760hrs/yr*CapacityFactor
=1.5MW*8760hrs/yr*.40=5256MWhrs
Assume annual operating expenses are 0;
and PTC impact is not included.

## Slide 26: Levelized cost of energy
Resource | LCOE
PC plant | $59.94/MWhr
NGCC plant | $99.64/MWhr
Nuclear plant | $66.49/MWhr
Wind, CF=0.35, FCR=20% | $143.51/MWhr
Wind, CF=0.35, FCR=11.6% | $83.24/MWhr
Wind, CF=0.40, FCR=20% | $125.58/MWhr
Wind, CF=0.40, FCR=11.6% | $72.83/MWhr

## Slide 27: Levelized Cost of Energy
Source: US DOE Energy Information Administration (EIA), “Levelized Cost and Levelized Avoided Cost of New Generation Resources in the Annual Energy Outlook 2016,” August 2016, available at https://www.eia.gov/forecasts/aeo/pdf/electricity_generation.pdf.

## Slide 28: Levelized Cost of Energy
Source: US DOE Energy Information Administration (EIA), “Levelized Cost and Levelized Avoided Cost of New Generation Resources in the Annual Energy Outlook 2016,” August 2016, available at https://www.eia.gov/forecasts/aeo/pdf/electricity_generation.pdf.

## Slide 29: Representative split – capital costs
Source: P. Jamieson, “Innovation in wind turbine design,” Wiley, 2011. Note – this book has an entire chapter dedicated to “Cost of Energy.”
Component | Cost fraction
Blades | 0.177
Hub | 0.077
Gearbox | 0.143
Generator | 0.076
Yaw system | 0.019
Nacelle cover | 0.020
Nacelle structure | 0.040
Tower | 0.219
Variable speed system | 0.073
Pitch system | 0.043
Rotor brake | 0.006
Couplings | 0.003
Shaft | 0.041
Other | 0.063
Total turbine | 1.00
This is for capital (investment) costs.
It is for a representative wind turbine design, but one should recognize that there are different designs. But it does provide some indication of relative splits among major wind turbine components.

## Slide 30: Representative split - LCOE
Source: P. Jamieson, “Innovation in wind turbine design,” Wiley, 2011. Note – this book has an entire chapter dedicated to “Cost of Energy.”
Initial capital costs | Turbine | Rotor | Rotor lock | 0.0057
0.820 | 0.569 |  | Blades | 0.1037
 |  |  | Hub | 0.0142
 |  | Nacelle systems | Gearbox | 0.0961
 |  |  | Generator | 0.0378
 |  |  | Rotor brake | 0.0085
 |  |  | Nacelle cover | 0.0142
 |  |  | Nacelle structure | 0.0193
 |  |  | Couplings | 0.0057
 |  |  | Shaft | 0.0171
 |  |  | Yaw system | 0.0171
 |  |  | Bearings | 0.0171
 |  | Electrics and control | Pitch system | 0.0365
 |  |  | Variable speed system | 0.0551
 |  | Tower |  | 0.0896
 |  | Other |  | 0.0313
 | Balance of plant |  | Roads & civil works | 0.0221
 | 0.251 |  | Electrics and grid con | 0.0761
 |  |  | Assembly & insttlltn | 0.0073
 |  |  | Transportation | 0.0365
 |  |  | Foundations | 0.0675
 |  |  | Financial and legal | 0.0414
O&M | 0.180 |  | Labor | 0.0792
0.180 |  |  | Parts | 0.0630
 |  |  | Operation | 0.0216
 |  |  | Equipment | 0.0090
 |  |  | Facilities | 0.0072

## Slide 31: Levelized avoided cost of energy (LACE)
Recall that
Complaint: There may be design changes that significantly decrease LCOE but result in lower revenues per MWhr. For example, increasing tower height will increase LARR and increase energy production; if the latter effect is proportionally greater than the former, then the LCOE decreasesincreasing tower height looks like good idea.
However, what if increased energy production is at night?
Off-peak prices! Revenues stream might not look good!
1. C. Namovicz, “Assessing the economic value of new utility-scale renewable generation projects,” EIA Energy Conference, presentation slides, June 17, 2013. www.eia.gov/conference/2013/pdf/presentations/namovicz.pdf.
2. US DOE Energy Information Administration (EIA), “Levelized Cost and Levelized Avoided Cost of New Generation Resources in Annual Energy Outlook 2016,” Aug 2016, at www.eia.gov/forecasts/aeo/pdf/electricity_generation.pdf.

## Slide 32: Levelized avoided cost of energy (LACE)
1. C. Namovicz, “Assessing the economic value of new utility-scale renewable generation projects,” EIA Energy Conference, presentation slides, June 17, 2013. www.eia.gov/conference/2013/pdf/presentations/namovicz.pdf.
2. US DOE Energy Information Administration (EIA), “Levelized Cost and Levelized Avoided Cost of New Generation Resources in Annual Energy Outlook 2016,” Aug 2016, at www.eia.gov/forecasts/aeo/pdf/electricity_generation.pdf.
To account for this, another metric has been suggested:
Here:

## Slide 33: LACE vs LOCE
1. C. Namovicz, “Assessing the economic value of new utility-scale renewable generation projects,” EIA Energy Conference, presentation slides, June 17, 2013. www.eia.gov/conference/2013/pdf/presentations/namovicz.pdf.
2. US DOE Energy Information Administration (EIA), “Levelized Cost and Levelized Avoided Cost of New Generation Resources in Annual Energy Outlook 2016,” Aug 2016, at www.eia.gov/forecasts/aeo/pdf/electricity_generation.pdf.
Wind capacity is built when LACE exceeds its LCOE.