## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 281: Digital Logic

## Slide 2
Binary Numbers
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
  This is the official class web page:
  https://www.ece.iastate.edu/~alexs/classes/2024_Fall_2810/
  If you missed the first lecture, the syllabus and other class materials are posted there.

## Slide 4: Administrative Stuff
HW1 is out
It is due on Wednesday Sep 4 @ 10 pm.
Submit it on Canvas before the start of the lecture

## Slide 5: Did you get the textbook?

## Slide 6: Required Textbook

## Slide 7: Required Textbook

## Slide 8: Required Textbook

## Slide 9: Where is the eBook?
In Canvas,
click here

## Slide 10: Where is the eBook?
Then click here

## Slide 11: Where is the eBook?

## Slide 12: Lab Sections

## Slide 13: Administrative Stuff
The labs and recitations start next week:
The lab schedule is also posted on the class web page
The recitation is the first 50 minutes
The other 2 hours are the lab
Changing of sections is not allowed, unless you can formally make the change in the registration system.

## Slide 14: The Labs Start Next Week
Please download and read the lab assignment for next week before you go to your lab section.
You must print the answer sheet for each lab ahead of time.
Then answer the pre-lab questions before the start of the lab.
The TAs will check your answers at the beginning of the recitation.

## Slide 15: Grading Scale

## Slide 16: Grading Percentages

## Slide 17: The Labs Start Next Week
Figure 1.5 in the textbook: An FPGA board.

## Slide 19: The Decimal System
[http://www.chompchomp.com/images/irregular011.jpg ]

## Slide 20: The Decimal System
[http://www.chompchomp.com/images/irregular011.jpg ]
0
1
2
3
4
5
6
7
8
9

## Slide 21: What number system is this one?
[http://freedomhygiene.com/wp-content/themes/branfordmagazine/images/backgrounds/Hands_141756.jpg]

## Slide 22: The Binary System
[ http://divaprojections.blogspot.com/2011/11/alien.html]

## Slide 23: The Binary System
[ http://divaprojections.blogspot.com/2011/11/alien.html]
0
1

## Slide 24: Number Systems

## Slide 25: Number Systems
n-th digit
(most significant)
0-th digit
(least significant)

## Slide 26: Number Systems
n-th digit
(most significant)
0-th digit
(least significant)
base
power

## Slide 27: The Decimal System

## Slide 28: The Decimal System

## Slide 29: Another Way to Look at This
5
2
4

## Slide 30: Another Way to Look at This
5
2
4
102
101
100

## Slide 31: Another Way to Look at This
5
2
4
102
101
100
boxes
labels
Each box can contain only one digit and has only one label. From right
to left, the labels are increasing powers of the base, starting from 0.

## Slide 32: Base 7

## Slide 33: Base 7
base
power

## Slide 34: Base 7
most significant
digit
least significant
digit
base
power

## Slide 35: Base 7

## Slide 36: Another Way to Look at This
5
2
4
72
71
70
2
6
3
102
101
100
=

## Slide 37: Binary Numbers (Base 2)

## Slide 38: Binary Numbers (Base 2)
most significant bit
least significant bit
base
power

## Slide 39: Binary Numbers (Base 2)

## Slide 40: Another Example

## Slide 41: Powers of 2

## Slide 42: What is the value of this binary number?
0 0 1 0 1 1 0 0
0 0 1 0 1 1 0 0
0*27 + 0*26 + 1*25 + 0*24 + 1*23 + 1*22 + 0*21 + 0*20
0*128 + 0*64 + 1*32 + 0*16 + 1*8 + 1*4 + 0*2 + 0*1
0*128 + 0*64 + 1*32 + 0*16 + 1*8 + 1*4 + 0*2 + 0*1
32+ 8 + 4 = 44 (in decimal)

## Slide 43: Another Way to Look at This
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
27

## Slide 44: Some Terminology
A binary digit is called a bit
A group of eight bits is called a byte
One bit can represent only two possible states, which are denoted with 1 and 0

## Slide 45: Relationship Between a Byte and a Bit
1
0
1
0
1
1
1
0

## Slide 46: Relationship Between a Byte and a Bit
1
0
1
0
1
1
1
0
1 bit

## Slide 47: Relationship Between a Byte and a Bit
1
0
1
0
1
1
1
0
8 bits = 1 byte
1 bit

## Slide 48: Bit Permutations
1 bit
0
1
2 bits
00
01
10
11
3 bits
000
001
010
011
100
101
110
111
4 bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Each additional bit doubles the number of possible permutations
© 2004 Pearson Addison-Wesley. All rights reserved

## Slide 49: Bit Permutations
Each permutation can represent a particular item
There are 2N permutations of N bits
Therefore, N bits are needed to represent 2N unique items
21 = 2 items
22 = 4 items
23 = 8 items
24 = 16 items
25 = 32 items
1 bit ?
2 bits ?
3 bits ?
4 bits ?
5 bits ?
How many
items can be
represented by
© 2004 Pearson Addison-Wesley. All rights reserved

## Slide 50: What is the maximum number that can be stored in one byte (8 bits)?

## Slide 51: What is the maximum number that can be stored in one byte (8 bits)?
1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1
1*27 + 1*26 + 1*25 + 1*24 + 1*23 + 1*22 + 1*21 + 1*20
1*128 + 1*64 + 1*32 + 1*16 + 1*8 + 1*4 + 1*2 + 1*1
128 + 64 + 32 + 16 + 8 + 4 + 2 + 1 = 255 (in decimal)
Another way is: 1*28 – 1 = 256 – 1 = 255

## Slide 52: What would happen if we try to add 1 to the largest number that can be stored in one byte (8 bits)?
1 1 1 1 1 1 1 1
+
1
-------------------------------
1 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0

## Slide 53: Analogy with car odometers

## Slide 54: Analogy with car odometers
[http://www.hyperocity.com/volvo240/images/Volvo/odometerrepair/speedo999999.jpg]

## Slide 55: Decimal to Binary Conversion (Using Guessing)

## Slide 56: Decimal to Binary Conversion (Using Guessing)

## Slide 57: Converting from Decimal to Binary

## Slide 58: Converting from Decimal to Binary

## Slide 59
[ Figure 1.6 in the textbook ]

## Slide 60: Octal System (Base 8)

## Slide 61: Binary to Octal Conversion

## Slide 62: Binary to Octal Conversion
1011100101112 = ?8

## Slide 63: Binary to Octal Conversion
1011100101112 = ?8
101 110 010 111

## Slide 64: Binary to Octal Conversion
1011100101112 = ?8
101 110 010 111
5 6 2 7

## Slide 65: Binary to Octal Conversion
1011100101112 = ?8
101 110 010 111
5 6 2 7
Thus, 1011100101112 = 56278

## Slide 66: Hexadecimal System (Base 16)

## Slide 67: The 16 Hexadecimal Digits
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F

## Slide 68: The 16 Hexadecimal Digits
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
10, 11, 12, 13, 14, 15

## Slide 69: Hexadecimal to Decimal Conversion

## Slide 70: Hexadecimal to Decimal Conversion

## Slide 71: Hexadecimal to Decimal Conversion

## Slide 72: Binary to Hexadecimal Conversion

## Slide 73: Binary to Hexadecimal Conversion

## Slide 74: Binary to Hexadecimal Conversion
1011100101112 = ?16

## Slide 75: Binary to Hexadecimal Conversion
1011100101112 = ?16
1011 1001 0111

## Slide 76: Binary to Hexadecimal Conversion
1011100101112 = ?16
1011 1001 0111
B 9 7

## Slide 77: Binary to Hexadecimal Conversion
1011100101112 = ?16
1011 1001 0111
B 9 7
Thus, 1011100101112 = B9716

## Slide 78: Decimal to Hexadecimal Conversion

## Slide 79: Decimal to Hexadecimal Conversion

## Slide 80: Sample Midterm 1 Questions on Number Systems

## Slide 91: Signed integers are more complicated
We will talk more about them when we start with Chapter 3 in a couple of weeks.

## Slide 92: The story with floats is even more complicated IEEE 754-1985 Standard
[http://en.wikipedia.org/wiki/IEEE_754]

## Slide 93
In the example shown above, the sign is zero so s is +1, the exponent is 124 so e is −3, and the significand m is 1.01 (in binary, which is 1.25 in decimal). The represented number is therefore +1.25 × 2−3, which is +0.15625.
[http://en.wikipedia.org/wiki/IEEE_754]

## Slide 94: On-line IEEE 754 Converter
https://www.h-schmidt.net/FloatConverter/IEEE754.html
More about floating point numbers in Chapter 3.

## Slide 95: Storing Characters
This requires some convention that maps binary numbers to characters.
ASCII table
Unicode

## Slide 96: ASCII Table

## Slide 97: Extended ASCII Codes

## Slide 98: The Unicode Character Code
http://www.unicode.org/charts/
https://en.wikipedia.org/wiki/Unicode
The original standard uses 16 bits (2 bytes)
The later extensions use up to 32 bits.

## Slide 99: The Greek Alphabet
http://www.unicode.org/charts/

## Slide 100: Close up
http://www.unicode.org/charts/

## Slide 101: Close up
http://www.unicode.org/charts/
This is the Hexadecimal number
for the Greek letter alpha: 03B1

## Slide 102: Close up
http://www.unicode.org/charts/
This is the Hexadecimal number
for the Greek letter beta: 03B2

## Slide 103: Close up
http://www.unicode.org/charts/
This is the Hexadecimal number
for the Greek letter gamma: 03B3

## Slide 104: Close up
http://www.unicode.org/charts/
This is the Hexadecimal number
for the Greek letter pi: 03C0

## Slide 105: Egyptian Hieroglyphs
http://www.unicode.org/charts/

## Slide 106: Close up
http://www.unicode.org/charts/

## Slide 107: Questions?

## Slide 108: THE END