## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 281: Digital Logic

## Slide 2
Synthesis
Using AND, OR, and NOT Gates
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW2 is due on Wednesday Sep 6 @ 10pm
Please write clearly on the first page the following three things:
  Your First and Last Name
  Your Student ID Number
  Your Lab Section Letter
Submit on Canvas as *one* PDF file.
Please orient your pages such that the text can be read without the need to rotate the page.

## Slide 4: Administrative Stuff
Next week we will start with Lab2
Read the lab assignment and do the prelab at home.
Complete the prelab on paper before you go to the lab. Otherwise you’ll lose 20% of your grade for that lab.

## Slide 5: Quick Review

## Slide 6
x
1
x
2
x
1
x
2
+
AND gate
x
x
x
1
x
2
x
1
x
2
•
The Three Basic Logic Gates
[ Figure 2.8 from the textbook ]
OR gate
NOT gate

## Slide 7
Truth Table for NOT
x
x
0
1
1
0
x
x

## Slide 8
x
1
x
2
x
1
x
2
•
Truth Table for AND

## Slide 9
Truth Table for OR
x
1
x
2
x
1
x
2
+

## Slide 10
[ Figure 2.6b from the textbook ]
Truth Tables for AND and OR

## Slide 11: Boolean Algebra
George Boole
1815-1864
An algebraic structure consists of
  a set of elements {0, 1}
  binary operators {+, }
  and a unary operator { ’ } or { } or { ~ }
Introduced by George Boole in 1854
An effective means of describing circuits built with switches
A powerful tool that can be used for designing and analyzing logic circuits

## Slide 12: Different Notations for Negation
All three of these mean “negate x”
  x’
  x
  ~x

## Slide 13: Operator Precedence
In regular arithmetic and algebra, multiplication takes precedence over addition.
This is also true in Boolean algebra.
For example, x + y • z means
multiply y by z and add the product to x .
In other words, x + y • z is equal to x + (y • z) ,
not (x + y) • z .

## Slide 14: The multiplication dot is optional
In regular algebra, the multiplication operator is often omitted to shorten the equations.
This is also true in Boolean algebra.
Both of these mean the same thing:
xy is equal to x • y

## Slide 15: Operator Precedence (three different ways to write the same)

## Slide 16: Operator Precedence
Negation of a single variable takes precedence over multiplication of that variable with another variable.
For example,
A B means negate A first and then multiply A by B

## Slide 17: Operator Precedence
However, a horizontal bar over a product of two variables means that the negation is performed after the product is computed.
For example,
A B means multiply A and B and then negate

## Slide 18: Operator Precedence
Note that these two expressions are different:
A B is not equal to A B
A B means multiply A and B and then negate
A B means negate A and B separately and then multiply

## Slide 19: Operator Precedence
Note that these two expressions are different:
A B is not equal to A B
A | B | AB
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | AB
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 20: DeMorgan’s Theorem

## Slide 21: Proof of DeMorgan’s theorem

## Slide 22: Proof of DeMorgan’s theorem
These two columns are equal. Therefore, the theorem is true.

## Slide 23: How to remember DeMorgan’s theorem
x • y
start with the
left-hand side

## Slide 24: How to remember DeMorgan’s theorem
x • y
divide the bar
into 3 equal parts

## Slide 25: How to remember DeMorgan’s theorem
x • y
erase the
middle segment

## Slide 26: How to remember DeMorgan’s theorem
x + y
change the
product to a sum

## Slide 27: How to remember DeMorgan’s theorem
x + y
this is the
right-hand side

## Slide 28: How to remember DeMorgan’s theorem
x • y = x + y

## Slide 30: Proof of the other DeMorgan’s theorem
0
1
1
1
1
0
0
0
1
1
0
0
1
0
1
0
1
0
0
0

## Slide 31: Proof of the other DeMorgan’s theorem
0
1
1
1
1
0
0
0
1
1
0
0
1
0
1
0
1
0
0
0
These two columns are equal. Therefore, the theorem is true.

## Slide 32: A Short Digression

## Slide 33: The 2D Plane
x
y

## Slide 34: The 2D Plane
x
y
i = (1, 0)

## Slide 35: The 2D Plane
x
y
j = (0, 1)

## Slide 36: The 2D Plane
x
y
point p

## Slide 37: The 2D Plane
x
y
p = 3i + 2j

## Slide 38: The unit vectors i and j form a basis
Any point in the 2D plane can be represented as a linear combination of these two vectors.
i=(1, 0)
j=(0, 1)
Note that there is only one 1 in each.

## Slide 39: 3D Space
x
z
y
i = (1, 0, 0)
j = (0, 1, 0)
k = (0, 0, 1)

## Slide 40: 3D Space
x
z
p = 3i + 1j + 2k
y

## Slide 41: The 3D Basis
In 3D we have i, j, and k
i=(1, 0, 0)
j=(0, 1, 0)
k=(0, 0, 1)
Note that there is only one 1 in each.
Any point in the 3D space can be represented as a linear combination of these three basis vectors.

## Slide 42: The 4D Basis
In 4D we have four vectors
x1 = (1, 0, 0, 0)
x2 = (0, 1, 0, 0)
x3 = (0, 0, 1, 0)
x4 = (0, 0, 0, 1)
Note that there is only one 1 in each.
Any point in this 4D space can be represented as a linear combination of these four basis vectors.

## Slide 43: Basis Functions (for two variables)

## Slide 44: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y)
f00(x, y)
f01(x, y)
f10(x, y)

## Slide 45: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y)
f00(x, y)
f01(x, y)
f10(x, y)

## Slide 46: The Four Basis Functions
x | y |  | f00(x, y) | f01(x, y) | f10(x, y) | f11(x, y)
0 | 0 |  | 1 | 0 | 0 | 0
0 | 1 |  | 0 | 1 | 0 | 0
1 | 0 |  | 0 | 0 | 1 | 0
1 | 1 |  | 0 | 0 | 0 | 1

## Slide 47: The Four Basis Functions
x | y |  | x y | x y | x y | x y
0 | 0 |  | 1 | 0 | 0 | 0
0 | 1 |  | 0 | 1 | 0 | 0
1 | 0 |  | 0 | 0 | 1 | 0
1 | 1 |  | 0 | 0 | 0 | 1

## Slide 48: Circuits for the four basis functions
y
x
x
y
x
y
x
y
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y

## Slide 49: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y

## Slide 50: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y
Negate the variable if the corresponding subscript of f is 0.

## Slide 51: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y
Negate the variable if the corresponding subscript of f is 0.

## Slide 52: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y
Negate the variable if the corresponding subscript of f is 0.

## Slide 53: minterms (an alternative name for the set of basis functions)

## Slide 54: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y

## Slide 55: The Four Basis Functions
x | y | f00
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f01
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f10
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f11
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y
m0
m1
m2
m3
(alternative names)

## Slide 56: The Four Basis Functions
x | y | m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
f11(x, y) = x y
f00(x, y) = x y
f01(x, y) = x y
f10(x, y) = x y
m0
m1
m2
m3
( minterms )

## Slide 57: The Four Basis Functions
x | y |  | x y | x y | x y | x y
0 | 0 |  | 1 | 0 | 0 | 0
0 | 1 |  | 0 | 1 | 0 | 0
1 | 0 |  | 0 | 0 | 1 | 0
1 | 1 |  | 0 | 0 | 0 | 1
( minterms )

## Slide 58: Expressions for the minterms
m0 = x y
m1 = x y
m2 = x y
m3 = x y

## Slide 59: Expressions for the minterms
m0 = x y
m1 = x y
m2 = x y
m3 = x y
0 0
0 1
1 0
1 1
The bars coincide
with the 0’s
in the binary expansion
of the minterm sub-index

## Slide 60: Expressions for the minterms
m0 = x y
m1 = x y
m2 = x y
m3 = x y
0 0
0 1
1 0
1 1
The bars coincide
with the 0’s
in the binary expansion
of the minterm sub-index

## Slide 61: Function Synthesis Example (with two variables)

## Slide 62: Synthesize the Following Function
x1 | x2 | f(x1, x2)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 63: 1) Split the function into a sum of 4 functions
x1 | x2 | f(x1, x2) |  | f00(x1, x2) | f01(x1, x2) | f10(x1, x2) | f11(x1, x2)
0 | 0 | 1 |  | 1 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 0
1 | 1 | 1 |  | 0 | 0 | 0 | 1

## Slide 64: 1) Split the function into a sum of 4 functions
x1 | x2 | f(x1, x2) |  | f00(x1, x2) | f01(x1, x2) | f10(x1, x2) | f11(x1, x2)
0 | 0 | 1 |  | 1 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 0
1 | 1 | 1 |  | 0 | 0 | 0 | 1
f(x1, x2) = 1 • f00 + 1 • f01 + 0 • f10 + 1 • f11

## Slide 65: 2) Write the expressions for all four
x1 | x2 | f(x1, x2) |  | f00(x1, x2) | f01(x1, x2) | f10(x1, x2) | f11(x1, x2)
0 | 0 | 1 |  | 1 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 0
1 | 1 | 1 |  | 0 | 0 | 0 | 1
f(x1, x2) = 1 • f00 + 1 • f01 + 0 • f10 + 1 • f11

## Slide 66: 2) Write the expressions for all four
x1 | x2 | f(x1, x2) |  | f00(x1, x2) | f01(x1, x2) | f10(x1, x2) | f11(x1, x2)
0 | 0 | 1 |  | 1 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 0
1 | 1 | 1 |  | 0 | 0 | 0 | 1
f(x1, x2) = 1 • f00 + 1 • f01 + 0 • f10 + 1 • f11

## Slide 67: 3) Then just add them together
x1 | x2 | f(x1, x2) |  | f00(x1, x2) | f01(x1, x2) | f10(x1, x2) | f11(x1, x2)
0 | 0 | 1 |  | 1 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 0
1 | 1 | 1 |  | 0 | 0 | 0 | 1
f(x1, x2) = 1 • f00 + 1 • f01 + 0 • f10 + 1 • f11

## Slide 68: 3) Then just add them together
x1 | x2 | f(x1, x2) |  | f00(x1, x2) | f01(x1, x2) | f10(x1, x2) | f11(x1, x2)
0 | 0 | 1 |  | 1 | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 |  | 0 | 0 | 1 | 0
1 | 1 | 1 |  | 0 | 0 | 0 | 1

## Slide 69: A function to be synthesized
[ Figure 2.19 from the textbook ]

## Slide 70: Let’s look at it row by row. How can we express the last row?

## Slide 71: Let’s look at it row by row. How can we express the last row?

## Slide 72: Let’s look at it row by row. How can we express the last row?
x2
x1

## Slide 73: What about this row?
x2
x1

## Slide 74: What about this row?
x2
x1

## Slide 75: What about this row?
x2
x1
x1
x2

## Slide 76: What about the first row?
x2
x1
x1
x2

## Slide 77: What about the first row?
x2
x1
x1
x2

## Slide 78: What about the first row?
x2
x1
x1
x2
x1
x2

## Slide 79: Finally, what about the zero?
x2
x1
x1
x2
x1
x2

## Slide 80: Putting it all together
f
x
1
x
2

## Slide 81: Let’s verify that this circuit implements correctly the target truth table
f
x
1
x
2

## Slide 82: Let’s verify that this circuit implements correctly the target truth table
f
x
1
x
2

## Slide 83: Putting it all together
f
x
1
x
2

## Slide 84: Canonical Sum-Of-Products (SOP)
[ Figure 2.20a from the textbook ]
f
x
1
x
2

## Slide 85: Summary of This Procedure
Get the truth table of the function
Form a product term (AND gate) for each row of the table for which the function is 1
Each product term contains all input variables
In each row, if xi =1 enter it as xi , otherwise use xi
Sum all of these products (OR gate) to get the function

## Slide 86: Simplification Steps

## Slide 87: Simplification Steps
replicate
this term

## Slide 88: Simplification Steps
group
these terms

## Slide 89: Simplification Steps
These two terms are trivially equal to 1

## Slide 90: Simplification Steps
Drop the 1’s

## Slide 91: Minimal-cost realization
f
x
2
x
1
[ Figure 2.20b from the textbook ]

## Slide 92: Two implementations for the same function
[ Figure 2.20 from the textbook ]
(a) Canonical sum-of-products
f
(b) Minimal-cost realization
x
2
x
1
f
x
1
x
2

## Slide 93: Basis Functions / minterms (for three variables)

## Slide 94: The Eight Basis Functions
x | y | z | f000 | f001 | f010 | f011 | f100 | f101 | f110 | f111
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 95: The Eight Basis Functions
x | y | z | f000 | f001 | f010 | f011 | f100 | f101 | f110 | f111
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 96: The Eight minterms
x | y | z | m0 | m1 | m2 | m3 | m4 | m5 | m6 | m7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 97: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z

## Slide 98: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 0’s
in the binary expansion
of the minterm sub-index

## Slide 99: Function Synthesis Example (with three variables)

## Slide 100: Let’s look at another problem
[ Figure 2.21 from the textbook ]

## Slide 101: Let’s look at another problem
[ Figure 2.21b from the textbook ]

## Slide 102: Let’s look at another problem

## Slide 103: Let’s look at another problem

## Slide 104: Let’s look at another problem

## Slide 105: Let’s look at another problem

## Slide 106: Let’s look at another problem

## Slide 107: Let’s look at another problem

## Slide 108: Let’s look at another problem

## Slide 109: Let’s look at another problem (minimization)

## Slide 110: Let’s look at another problem (minimization)
f
s3
s2
s1

## Slide 111: Maxterms (an alternative set of basis functions)

## Slide 112: The Four Maxterms
x | y | M0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | M1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | M2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | M3
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
M3(x, y)
M0(x, y)
M1(x, y)
M2(x, y)

## Slide 113: The Four Maxterms
x | y | M0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | M1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | M2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | M3
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
M3(x, y)
M0(x, y)
M1(x, y)
M2(x, y)

## Slide 114: The Four Maxterms
x | y |  | M0(x, y) | M1(x, y) | M2(x, y) | M3(x, y)
0 | 0 |  | 0 | 1 | 1 | 1
0 | 1 |  | 1 | 0 | 1 | 1
1 | 0 |  | 1 | 1 | 0 | 1
1 | 1 |  | 1 | 1 | 1 | 0

## Slide 115: The Four Maxterms
x | y |  | x + y | x + y | x + y | x + y
0 | 0 |  | 0 | 1 | 1 | 1
0 | 1 |  | 1 | 0 | 1 | 1
1 | 0 |  | 1 | 1 | 0 | 1
1 | 1 |  | 1 | 1 | 1 | 0

## Slide 116: Expressions for the Maxterms
M0 = x + y
M1 = x + y
M2 = x + y
M3 = x + y

## Slide 117: Expressions for the Maxterms
M0 = x + y
M1 = x + y
M2 = x + y
M3 = x + y
Note that these are now
sums, not products.

## Slide 118: Expressions for the Maxterms
M0 = x + y
M1 = x + y
M2 = x + y
M3 = x + y
0 0
0 1
1 0
1 1
The bars coincide
with the 1’s
in the binary expansion
of the maxterm sub-index

## Slide 119: Expressions for the Maxterms
M0 = x + y
M1 = x + y
M2 = x + y
M3 = x + y
0 0
0 1
1 0
1 1
The bars coincide
with the 1’s
in the binary expansion
of the maxterm sub-index

## Slide 120: Minterms and Maxterms

## Slide 121: Minterms and Maxterms
Use these for
Sum-of-Products
Minimization
(1’s of the function)
Use these for
Product-of-Sums
Minimization
(0’s of the function)

## Slide 122: Minterms and Maxterms
Use these for
Sum-of-Products
Minimization
(1’s of the function)
Use these for
Product-of-Sums
Minimization
(0’s of the function)

## Slide 123: Sum-of-Products Form (uses the ones of the function)

## Slide 124: Sum-of-Products Form (for the AND logic function)
f (x1, x2)

## Slide 125: Sum-of-Products Form (for the AND logic function)
f (x1, x2)

## Slide 126: Sum-of-Products Form (for the AND logic function)
f (x1, x2)
f (x1, x2) = m3 = x1 x2
(In this case there is just one product and there is no need for a sum)

## Slide 127: Another Example

## Slide 128: Sum-of-Products Form
f (x1, x2)

## Slide 129: Sum-of-Products Form
f (x1, x2)

## Slide 130: Sum-of-Products Form
f (x1, x2)

## Slide 131: Product-of-Sums Form (uses the zeros of the function)

## Slide 132: Product-of-Sums Form (for the OR logic function)
f (x1, x2)

## Slide 133: Product-of-Sums Form (for the OR logic function)
f (x1, x2)

## Slide 134: Product-of-Sums Form (for the OR logic function)
f (x1, x2)
f (x1, x2) = M0 = x1 + x2
(In this case there is just one sum and there is no need for a product)

## Slide 135: Another Example

## Slide 136: Product-of-Sums Form (for this logic function)
f (x1, x2)

## Slide 137: Product-of-Sums Form (for this logic function)
f (x1, x2)

## Slide 138: Product-of-Sums Form (for this logic function)
f (x1, x2)
f (x1, x2) = M0 • M2 = ( x1 + x2 ) • ( x1 + x2 )

## Slide 139: Yet Another Example

## Slide 140: Product-of-Sums Form
f (x1, x2)
We need to minimize using the zeros of the function f.
But let’s first minimize the inverse of f, i.e., f.

## Slide 141: Product-of-Sums Form
f (x1, x2)
f (x1, x2)

## Slide 142: Product-of-Sums Form
f (x1, x2)
f (x1, x2)

## Slide 143: Product-of-Sums Form
f (x1, x2)
f (x1, x2)

## Slide 144: Product-of-Sums Form
f (x1, x2)
f (x1, x2)

## Slide 145: Product-of-Sums Form
f (x1, x2)
f (x1, x2)

## Slide 146: minterms (for three variables)

## Slide 147: The Eight minterms
x | y | z | m0 | m1 | m2 | m3 | m4 | m5 | m6 | m7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 148: The Eight minterms
x | y | z | m0 | m1 | m2 | m3 | m4 | m5 | m6 | m7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 149: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z

## Slide 150: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 0’s
in the binary expansion
of the minterm sub-index

## Slide 151: Maxterms (for three variables)

## Slide 152: The Eight Maxterms
x | y | z | M0 | M1 | M2 | M3 | M4 | M5 | M6 | M7
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 153: The Eight Maxterms
x | y | z | M0 | M1 | M2 | M3 | M4 | M5 | M6 | M7
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 154: Expressions for the Maxterms
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z

## Slide 155: Expressions for the Maxterms
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 1’s
in the binary expansion
of the maxterm sub-index

## Slide 156: minterms and Maxterms (for three variables)

## Slide 157: minterms and Maxterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z

## Slide 158: minterms and Maxterms (with three variables)
[ Figure 2.22 from the textbook ]

## Slide 159: Examples with three-variable functions

## Slide 160: A three-variable function
[ Figure 2.23 from the textbook ]

## Slide 161: Sum-of-Products (SOP)

## Slide 162: Sum-of-Products (SOP)

## Slide 163: Sum-of-Products (SOP)

## Slide 164: Sum-of-products realization of this function
[ Figure 2.24a from the textbook ]
f
x
1
x
2
x
3
f = x2 x3 + x1 x3

## Slide 165: A three-variable function
[ Figure 2.23 from the textbook ]

## Slide 166: Product-of-Sums (POS)

## Slide 167: Product-of-Sums (POS)

## Slide 168: Product-of-Sums (POS)

## Slide 169: Product-of-sums realization of this function
[ Figure 2.24b from the textbook ]
f
x
2
x
1
x
3
f = (x1 + x3) • ( x2 + x3 )

## Slide 170: Two realizations of this function
(a) A minimal sum-of-products realization
(b) A minimal product-of-sums realization
[ Figure 2.24 from the textbook ]
f
x
2
x
1
x
3
f
x
1
x
2
x
3

## Slide 171: Shorthand Notation for SOP
or

## Slide 172: Shorthand Notation for POS
or

## Slide 173: Shorthand Notation
Sum-of-Products (SOP)
or
Product-of-Sums (POS)
or

## Slide 174: The Cost of a Circuit
Count all gates
Count all inputs/wires to the gates
Add the two partial counts. That is the cost.

## Slide 175: What is the cost of this circuit?
f
x
1
x
2

## Slide 176: What is the cost of this circuit?
f
x
1
x
2
1
1
1
1
1
1
There are 6 gates.

## Slide 177: What is the cost of this circuit?
f
x
1
x
2
1
1
1
1
1
1
There are 6 gates and 11 inputs.
The total cost is 17.
2
2
2
3
1
1

## Slide 178: What is the cost of each circuit?
(a) A minimal sum-of-products realization
(b) A minimal product-of-sums realization
f
x
2
x
1
x
3
f
x
1
x
2
x
3

## Slide 179: Questions?

## Slide 180: THE END