## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 281: Digital Logic

## Slide 2
Karnaugh Maps
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW3 is due today

## Slide 4: Administrative Stuff
HW4 is out
It is due on Monday Sep 23 @ 10 pm
It is posted on the class web page
I also sent you an e-mail with the link.

## Slide 5: TA Office Hours
Hanif Lashari: Mondays 2:10 – 3:10pm
Le Zhang: Wednesdays 11 am – 1pm
Himani Kohli: Thursdays 9 – 10 am
Go to the Transformative Learning Area (TLA) on the first floor in Coover Hall. Look for a sign that says “CprE 2810 TA.”

## Slide 6: Administrative Stuff
Midterm Exam #1
When: Friday Sep 27.
What: Chapter 1 and Chapter 2 plus number systems
The exam will be closed book but open notes (you can bring up to 3 pages of handwritten notes).
Sample exams are posted on the class web page.
More details to follow.

## Slide 7: Quick Review

## Slide 8: Do You Still Remember This Boolean Algebra Theorem?

## Slide 9: Let’s prove 14.a

## Slide 10: Let’s prove 14.a
0
0
0
1

## Slide 11: Let’s prove 14.a
0
0
0
1
0
0
1
0

## Slide 12: Let’s prove 14.a
0
0
0
1
0
0
1
0
0
0
1
1

## Slide 13: Let’s prove 14.a
0
0
0
1
0
0
1
0
0
0
1
1
0
0
1
1

## Slide 14: Let’s prove 14.a
0
0
0
1
0
0
1
0
0
0
1
1
0
0
1
1
They are equal.

## Slide 16: Motivation
An approach for simplifying logic expressions.
How do we guarantee that we have reached the minimum SOP/POS representation?

## Slide 17: This method was described in 1953
M. Karnaugh, “The map method for synthesis of combinational logic circuits”
Transactions of the American Institute of Electrical Engineers, Part I: Communication and Electronics (pages 593 – 599, Volume: 72, Issue: 5, Nov. 1953)
https://ieeexplore.ieee.org/document/6371932

## Slide 18: Two-Variable K-Map

## Slide 19: Karnaugh Map (K-map)
A visual representation of the function
Same information as the truth table
Easier to group minterms
x
2
(a) Truth table
(b) Karnaugh map
0
1
0
1
0
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
0
1
1
0
x
1
f

## Slide 20: Karnaugh Map (K-map)
A visual representation of the function
Same information as the truth table
Easier to group minterms
x
2
(a) Truth table
(b) Karnaugh map
0
1
0
1
m
0
m
2
m
3
m
1
x
1
x
2
0
0
0
1
1
0
1
1
m
0
m
1
m
3
m
2
x
1
[ Figure 2.49 from the textbook ]
f

## Slide 21: Minterms
x
1
x
2
0
0
0
1
1
0
1
1
m
0
m
1
m
3
m
2
x
1
x
2
0
0
0
1
1
0
1
1
1
0
0
0
m
m
m
m
0
1
0
0
0
0
0
1
0
0
1
0
0
1
2
3
f

## Slide 22: Minterm Addition Example
x
1
x
2
0
0
0
1
1
0
1
1
0
1
1
0
x
1
x
2
0
0
0
1
1
0
1
1
1
0
0
0
m
m
m
m
0
1
0
0
0
0
0
1
0
0
1
0
0
1
2
3
0
1
1
0
m
+ m
1
3
f

## Slide 23: Minterm Addition Example
x
1
x
2
0
0
0
1
1
0
1
1
0
1
1
0
x
1
x
2
0
0
0
1
1
0
1
1
1
0
0
0
m
m
m
m
0
1
0
0
0
0
0
1
0
0
1
0
0
1
2
3
0
1
1
0
m
+ m
1
3
x1x2 + x1x2 = x2
_
f

## Slide 24: Minterm Addition Example
x
1
x
2
0
0
0
1
1
0
1
1
0
1
1
0
x1x2 + x1x2 = x2
_
f
x
2
0
1
0
1
0
0
1
1
x
1

## Slide 25: Minterm Addition Example
x
1
x
2
0
0
0
1
1
0
1
1
0
1
1
0
x1x2 + x1x2 = x2
_
f
x
2
0
1
0
1
0
0
1
1
x
1
x2

## Slide 26: Another Grouping Example
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
m0
m1

## Slide 27: Another Grouping Example
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
m0
m1
x
2
0
1
0
1
1
0
0
1
x
1
m0 + m1
+
+
=
=

## Slide 28: Another Grouping Example
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
m0
m1
x
2
0
1
0
1
1
0
0
1
x
1
m0 + m1
+
+
=
=

## Slide 29: Another Grouping Example
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
m0
m1
x
2
0
1
0
1
1
0
0
1
x
1
m0 + m1
+
+
+
x1x2
x1
=
=
=
x1x2
_
_
_
_
Property 14a (Combining)

## Slide 30: Grouping Rules
Group “1”s with rectangles
Both sides must be a power of 2:
  1x1, 1x2, 2x1, 2x2, 1x4, 4x1, 2x4, 4x2, 4x4
Can use/cover the same minterm more than once
Can wrap around the edges of the map
Some rules in selecting groups:
  Try to use as few groups as possible to cover all “1”s.
  For each group, try to make it as large as you can (i.e., if you can use a 2x2, don’t use a 2x1 even if that is enough).

## Slide 31: Two-Variable K-map
x
2
(a) Truth table
(b) Karnaugh map
0
1
0
1
m
0
m
2
m
3
m
1
x
1
x
2
0
0
0
1
1
0
1
1
m
0
m
1
m
3
m
2
x
1
[ Figure 2.49 from the textbook ]
f

## Slide 32: Step-By-Step Example
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
f

## Slide 33: 1. Draw The Map
x
2
0
1
0
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
f

## Slide 34: 2. Fill The Map
x
2
0
1
0
1
m
0
m
2
m
3
m
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
m
0
m
1
m
3
m
2
f

## Slide 35: 2. Fill The Map
x
2
0
1
0
1
m
0
m
2
m
3
m
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
m
0
m
1
m
3
m
2
f

## Slide 36: 2. Fill The Map
x
2
0
1
0
1
1
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
m
0
m
1
m
3
m
2
f

## Slide 37: 3. Group
x
2
0
1
0
1
1
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
m
0
m
1
m
3
m
2
f

## Slide 38: 3. Group
x
2
0
1
0
1
1
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
m
0
m
1
m
3
m
2
f

## Slide 39: 3. Group
x
2
0
1
0
1
1
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
m
0
m
1
m
3
m
2
f

## Slide 40: 4. Write The Expression
x
2
0
1
0
1
1
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
f

## Slide 41: 4. Write The Expression
x
2
0
1
0
1
1
0
1
1
x
1
x
2
0
0
0
1
1
0
1
1
1
1
1
0
x
1
x1 + x2
_
f

## Slide 42: Writing The Expression
Find which variable is constant
x
2
0
1
0
1
1
0
0
1
x
1
x1
_

## Slide 43: Writing The Expression
Find which variable is constant
x
2
0
1
0
1
0
1
1
0
x
1
x1

## Slide 44: Writing The Expression
Find which variable is constant
x
2
0
1
0
1
1
1
0
0
x
1
x2
_

## Slide 45: Writing The Expression
Find which variable is constant
x
2
0
1
0
1
0
0
1
1
x
1
x2

## Slide 47: These are all valid groupings
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
x
2
0
1
0
1
0
1
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
x1 x2
_
_
x1 x2
_
x1 x2
_
x1 x2

## Slide 48: These are all valid groupings
x
2
0
1
0
1
1
0
0
1
x
1
x
2
0
1
0
1
0
1
1
0
x
1
x
2
0
1
0
1
1
1
0
0
x
1
x
2
0
1
0
1
0
0
1
1
x
1
x1
_
x1
x2
_
x2

## Slide 49: This one is valid too
x
2
0
1
0
1
1
1
1
1
x
1
In this case the result is the constant function 1.

## Slide 50: Invalid Groupings
x
2
0
1
0
1
1
0
1
0
x
1
x
2
0
1
0
1
0
1
0
1
x
1

## Slide 51: Can’t group diagonally. Why?
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
m0
m3

## Slide 52: Can’t group diagonally. Why?
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
m0
m3
x
2
0
1
0
1
1
0
1
0
x
1
m0 + m3
+
+
=
=

## Slide 53: Can’t group diagonally. Why?
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
m0
m3
x
2
0
1
0
1
1
0
1
0
x
1
m0 + m3
+
+
=
=

## Slide 54: Can’t group diagonally. Why?
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
m0
m3
x
2
0
1
0
1
1
0
1
0
x
1
m0 + m3
+
+
=
=
+
x1x2
x1x2
_
_
=
x1x2
+
x1x2
_
_
We can’t use Property 14a here. This can’t be simplified.

## Slide 55: Three-Variable K-Map

## Slide 56
Location of three-variable minterms
[ Figure 2.51 from the textbook ]

## Slide 57
Location of three-variable minterms
Notice the placement of
  Variables
  Binary pair values
  Minterms

## Slide 58
Location of three-variable minterms
Notice the placement of
  Variables
  Binary pair values
  Minterms

## Slide 59
Location of three-variable minterms
Notice the placement of
  Variables
  Binary pair values
  Minterms

## Slide 60: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
00
01
11
10

## Slide 61: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 62: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 63: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 64: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 65: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 66: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 67: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 68: Gray Code
Sequence of binary codes
Two neighboring lines vary by only 1 bit
000
001
011
010
110
111
101
100

## Slide 69: Gray Code & K-map
s x1
x2

## Slide 70: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 71: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 72: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 73: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 74: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 75: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the LAST bit

## Slide 76: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the LAST bit

## Slide 77: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the FIRST bit

## Slide 78: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These four neighbors
differ in the FIRST and LAST bit
They are similar in their MIDDLE bit

## Slide 79: Adjacency Rules
adjacent
columns

## Slide 80: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These two neighbors
differ only in the FIRST bit

## Slide 81: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These four neighbors
differ in the FIRST and LAST bit
They are similar in their MIDDLE bit

## Slide 82: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder

## Slide 83: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5

## Slide 84: Adjacency Rules
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5
adjacent
columns

## Slide 85: Adjacency Rules
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5
adjacent
columns

## Slide 86: Examples of Valid Groupings

## Slide 87: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 0
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 88: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 1
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 89: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 0
 | 1 | 1 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 1
x1 x2
x1 x2
x1 x2
x1 x2

## Slide 90: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 1
 | 1 | 0 | 0 | 0 | 0
x1 x3
x2 x3
x1 x3
x2 x3

## Slide 91: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 0 | 0 | 1
x1 x3
x2 x3
x1 x3
x2 x3

## Slide 92: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 1
 | 1 | 0 | 0 | 1 | 1
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 0 | 1
 | 1 | 1 | 0 | 0 | 1
x1
x2
x1
x2

## Slide 93: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 1
x3
x3

## Slide 94: Groupings and Expressions
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1 | 1
0
1

## Slide 95: Examples of Invalid Groupings

## Slide 96: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 0 | 0
Can’t group diagonally.

## Slide 97: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 1 | 1
Can’t group three in a row.
Each side must be a power of 2.

## Slide 98: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Can’t group zeros and ones together.

## Slide 99: Minimization Examples with 3-variable K-Maps

## Slide 100
[ Figure 2.52a from the textbook ]
Examples of three-variable Karnaugh maps

## Slide 101
[ Figure 2.52b from the textbook ]
Examples of three-variable Karnaugh maps

## Slide 102: Four-Variable K-Map

## Slide 103
[ Figure 2.53 from the textbook ]
A four-variable Karnaugh map

## Slide 104
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 105
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 106
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 107
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 108
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 109
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 110
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 111
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 112
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 113: Adjacency Rules
adjacent
columns
adjacent
columns
adjacent
rows

## Slide 114: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus

## Slide 115: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 116: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 117: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 118
Some Valid Groupings

## Slide 119
Some Valid Groupings

## Slide 120
Some Valid Groupings

## Slide 121
Some Valid Groupings

## Slide 122
Some Invalid Groupings
All sides must be powers of 2.

## Slide 123
Some valid Groupings
All sides must be powers of 2.

## Slide 124: Minimization Examples with 4-variable K-Maps

## Slide 125
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 126
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 127
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 128
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 129: Five-Variable K-Map

## Slide 130
[ Figure 2.55 from the textbook ]
A five-variable Karnaugh map

## Slide 131: Six-Variable K-Map

## Slide 132
[ Figure 16, in Karnaugh 1953]
A six-variable Karnaugh map

## Slide 133
[ Figure 16, in Karnaugh 1953]
A six-variable Karnaugh map
A
B

## Slide 134
[ Figure 16, in Karnaugh 1953]
A six-variable Karnaugh map
A
B
C
E
F
D

## Slide 135: Seven-Variable K-Map

## Slide 136
A seven-variable Karnaugh map

## Slide 137
G = 0
G = 1
[Suggested in Karnaugh 1953]
A seven-variable Karnaugh map

## Slide 138: Questions?

## Slide 139: THE END