## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Incompletely Specified Functions &
Multiple-Output Circuits
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW4 is due on Monday Sep 23 @ 10 pm
It is posted on the class web page
I also sent you an e-mail with the link.

## Slide 4: Administrative Stuff
HW5 is due on Monday Sep 30 @ 10 pm
It is posted on the class web page
I also sent you an e-mail with the link.

## Slide 5: TA Office Hours
Hanif Lashari: Mondays 2:10 – 3:10pm
Le Zhang: Wednesdays 11 am – 1pm
Himani Kohli: Thursdays 9 – 10 am
Go to the Transformative Learning Area (TLA) on the first floor in Coover Hall. Look for a sign that says “CprE 2810 TA.”

## Slide 6: Administrative Stuff
Midterm Exam #1
When: Friday Sep 27.
What: Chapter 1 and Chapter 2 plus number systems
The exam will be closed book but open notes (you can bring up to 3 pages of handwritten notes).
It will be in this room.
Sample exams are posted on the class web page.

## Slide 7: Topics for the Midterm Exam
Binary Numbers
Octal Numbers
Hexadecimal Numbers
Conversion between the different number systems
Truth Tables
Boolean Algebra
Logic Gates
Circuit Synthesis with AND, OR, NOT
Circuit Synthesis with NAND, NOR
Converting an AND/OR/NOT circuit to NAND circuit
Converting an AND/OR/NOT circuit to NOR circuit
SOP and POS expressions

## Slide 8: Topics for the Midterm Exam
Mapping a Circuit to Verilog code
Mapping Verilog code to a circuit
Multiplexers
Venn Diagrams
K-maps for 2, 3, and 4 variables
Minimization of Boolean expressions using theorems
Minimization of Boolean expressions with K-maps
Incompletely specified functions (with don’t cares)
Functions with multiple outputs
Something from Star Wars

## Slide 9: One-Variable K-Map

## Slide 10: One-Variable K-map
(a) Truth table
(b) Karnaugh map
0
1
m
0
m
1
x
1
x
1
0
1
m
0
m
1
f

## Slide 11: One-Variable K-map
(a) Truth table
(b) Karnaugh map
0
1
1
0
x
1
x1
x
1
0
1
1
0
f

## Slide 12: Two-Variable K-Map

## Slide 13: Two-Variable K-map
x
2
(a) Truth table
(b) Karnaugh map
0
1
0
1
m
0
m
2
m
3
m
1
x
1
x
2
0
0
0
1
1
0
1
1
m
0
m
1
m
3
m
2
x
1
[ Figure 2.49 from the textbook ]

## Slide 14: These are all valid groupings
x
2
0
1
0
1
1
0
0
0
x
1
x
2
0
1
0
1
0
0
0
1
x
1
x
2
0
1
0
1
0
1
0
0
x
1
x
2
0
1
0
1
0
0
1
0
x
1
x1 x2
_
_
x1 x2
_
x1 x2
_
x1 x2

## Slide 15: These are all valid groupings
x
2
0
1
0
1
1
0
0
1
x
1
x
2
0
1
0
1
0
1
1
0
x
1
x
2
0
1
0
1
1
1
0
0
x
1
x
2
0
1
0
1
0
0
1
1
x
1
x1
_
x1
x2
_
x2

## Slide 16: This one is valid too
x
2
0
1
0
1
1
1
1
1
x
1
In this case the result is the constant function 1.

## Slide 17: Why are these two not valid?
x
2
0
1
0
1
1
0
1
0
x
1
x
2
0
1
0
1
0
1
0
1
x
1

## Slide 18: Minimization Example with a two-variable K-map
[ Figure 2.50 from the textbook ]
1

## Slide 19: Three-Variable K-Map

## Slide 20
Three-Variable K-map
[ Figure 2.51 from the textbook ]

## Slide 21
Location of three-variable minterms
Notice the placement of
  Variables
  Binary pair values
  Minterms

## Slide 22: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder

## Slide 23: Adjacency Rules
adjacent
columns
As if the K-map were
drawn on a cylinder
m0
m2
m4
m1
m3
m5

## Slide 24: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 0 | 0
 | 1 | 0 | 0 | 1 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 0 | 0
Can’t group diagonally.

## Slide 25: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 1 | 0
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | 1 | 1
Can’t group three in a row.
Each side must be a power of 2.

## Slide 26: Some Invalid Groupings
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 1 | 0 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | 0 | 0 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Can’t group zeros and ones together.

## Slide 27: Three-Variable K-map
[ Figure 2.52 from the textbook ]

## Slide 28: From Boolean Expression to K-map

## Slide 29: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | m0 | m2 | m6 | m4
 | 1 | m1 | m3 | m7 | m5
F = A C + A B + A B C

## Slide 30: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 |  |  |  | 
 | 1 |  |  |  | 
F = A C + A B + A B C

## Slide 31: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 |  |  |  | 
F = A C + A B + A B C

## Slide 32: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 |  |  |  | 
F = A C + A B + A B C

## Slide 33: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 | 1 |  |  | 
F = A C + A B + A B C

## Slide 34: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 | 1 |  |  | 
F = A C + A B + A B C

## Slide 35: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 |  | 
 | 1 | 1 | 1 |  | 
F = A C + A B + A B C

## Slide 36: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F = A C + A B + A B C

## Slide 37: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F = A C + A B + A B C
A

## Slide 38: From Boolean Expression to K-map
 | AB |  |  |  | 
C |  | 00 | 01 | 11 | 10
 | 0 | 1 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0
F = A C + A B + A B C = A
A

## Slide 39: Different Ways to Draw the K-map

## Slide 40: Two Different Ways to Draw the K-map
 | x2x3 |  |  |  | 
x1 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6

## Slide 41: Another Way to Draw 3-variable K-map
 | x1 |  | 
x2x3 |  | 0 | 1
 | 00 | m0 | m4
 | 01 | m1 | m5
 | 11 | m3 | m7
 | 10 | m2 | m6

## Slide 42: There are 4 different versions!
 | x1x2 |  |  |  | 
x3 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m2 | m6 | m4
 | 1 | m1 | m3 | m7 | m5
 | x3 |  | 
x1x2 |  | 0 | 1
 | 00 | m0 | m1
 | 01 | m2 | m3
 | 11 | m6 | m7
 | 10 | m4 | m5
 | x2x3 |  |  |  | 
x1 |  | 00 | 01 | 11 | 10
 | 0 | m0 | m1 | m3 | m2
 | 1 | m4 | m5 | m7 | m6
 | x1 |  | 
x2x3 |  | 0 | 1
 | 00 | m0 | m4
 | 01 | m1 | m5
 | 11 | m3 | m7
 | 10 | m2 | m6

## Slide 43: Why is it OK to combine a group of four ones?

## Slide 44: Gray Code & K-map
s x1
x2

## Slide 45: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101

## Slide 46: Gray Code & K-map
s x1
x2
000
010
110
100
001
011
111
101
These four neighbors
differ in the FIRST and LAST bit
They are similar in their MIDDLE bit

## Slide 47: The K-Map theory uses the combining theorems of Boolean algebra

## Slide 48: The K-Map theory uses the combining theorems of Boolean algebra
optimization by 1’s

## Slide 49: The K-Map theory uses the combining theorems of Boolean algebra
optimization by 0’s

## Slide 50: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Theorem 14a is behind the K-Map theory.
But that theorem is just for two variables.
Why is this grouping of four ones possible?

## Slide 51: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0

## Slide 52: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z

## Slide 53: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z
_ _
( x y + x y ) z
_
( x y + x y ) z

## Slide 54: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = (x y + x y) z + (x y + x y) z

## Slide 55: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = (x y + x y) z + (x y + x y) z
_
y z (by 14a)
y z (by 14a)

## Slide 56: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = y z + y z

## Slide 57: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = y z + y z
y (by 14a)

## Slide 58: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
f = y

## Slide 59: Why can we group these four ones?
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Answer: We can combine them because Theorem 14a
is applied three times, not just once.

## Slide 60: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0

## Slide 61: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z

## Slide 62: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z

## Slide 63: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _ _
f = x y z + x y z + x y z + x y z
_ _
x ( y z + y z )
_
x ( y z + y z )

## Slide 64: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = x (y z + y z) + x (y z + y z)

## Slide 65: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_ _ _
f = x (y z + y z) + x (y z + y z)
_
x y (by 14a)
x y (by 14a)

## Slide 66: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = x y + x y

## Slide 67: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
_
f = x y + x y
y (by 14a)

## Slide 68: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
f = y

## Slide 69: Alternative Derivation
 | x y |  |  |  | 
z |  | 00 | 01 | 11 | 10
 | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 1 | 1 | 0
Answer: We can combine them because Theorem 14a
is applied three times, not just once.

## Slide 70: Four-Variable K-Map

## Slide 71
[ Figure 2.53 from the textbook ]
A four-variable Karnaugh map

## Slide 72
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map

## Slide 73
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
Gray Code & K-map

## Slide 74
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
Gray Code & K-map
0000
0100
1100
1000
0001
0101
1101
1001
0011
0111
1111
1011
0010
0110
1110
1010

## Slide 75: Adjacency Rules
adjacent
columns
adjacent
columns
adjacent
rows

## Slide 76: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus

## Slide 77: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 78: Adjacency Rules
adjacent
columns
adjacent
rows
As if the K-map were
drawn on a torus
m0
m2
m12
m8
m10
m4
m6
m14

## Slide 79
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 80
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 81
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 82
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 83
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 84
[ Figure 2.54 from the textbook ]
Example of a four-variable Karnaugh map

## Slide 85: Other Four-Variable K-map Examples
[ Figure 2.54 from the textbook ]

## Slide 86: POS Minimization

## Slide 87
[ Figure 2.60 from the textbook ]
POS minimization of f (x1, x2, x3) = ∏ M(4, 5, 6)

## Slide 88
[ Figure 2.60 from the textbook ]
POS minimization of f (x1, x2, x3) = ∏ M(4, 5, 6)
f (x1, x2, x3) = ( x1 + x3 ) ( x1 + x3 )

## Slide 89
x
1
x
2
x
3
x
4
0
00
01
11
10
0
0
0
0
1
1
0
1
1
0
1
1
1
1
1
00
01
11
10
x
2
x
3
+
(
)
x
3
x
4
+
(
)
x
1
x
2
x
3
x
4
+
+
+
(
)
[ Figure 2.61 from the textbook ]
POS minimization of f ( x1,…, x4) = ∏ M(0, 1, 4, 8, 9, 12, 15)

## Slide 90
x
1
x
2
x
3
x
4
0
00
01
11
10
0
0
0
0
1
1
0
1
1
0
1
1
1
1
1
00
01
11
10
x
2
x
3
+
(
)
x
3
x
4
+
(
)
x
1
x
2
x
3
x
4
+
+
+
(
)
[ Figure 2.61 from the textbook ]
POS minimization of f ( x1,…, x4) = ∏ M(0, 1, 4, 8, 9, 12, 15)
f (x1, x2, x3 , x4) = ( x3 + x4 ) ( x2 + x3 ) ( x1 + x2 + x3 + x4 )

## Slide 91: Example: Incompletely Specified Function

## Slide 92: Three Ways to Specify the Function
f(x1, x2, x3, x4) = Σ m(2, 4, 5, 6, 10) + D(12, 13, 14, 15)

## Slide 93: Three Ways to Specify the Function
f(x1, x2, x3, x4) = Σ m(2, 4, 5, 6, 10) + D(12, 13, 14, 15)
x
1
x
2
x
3
x
4
0
00
01
11
10
1
d
0
0
1
d
0
0
0
d
0
1
1
d
1
00
01
11
10
0
0
1
0
1
1
1
0
0
1
0
d
d
d
d

## Slide 94: SOP implementation
x
x
1
x
2
x
3
x
4
0
00
01
11
10
1
d
0
0
1
d
0
0
0
d
0
1
1
d
1
00
01
11
10
x
2
x
3
x
3
4
(a) SOP implementation
[ Figure 2.62 from the textbook ]

## Slide 95: POS implementation
x
x
1
x
2
x
3
x
4
0
00
01
11
10
1
d
0
0
1
d
0
0
0
d
0
1
1
d
1
00
01
11
10
x
2
x
3
+
(
)
3
x
4
+
(
)
(b) POS implementation
[ Figure 2.62 from the textbook ]

## Slide 96: Example: A circuit with multiple outputs

## Slide 97: Seven-Segment Indicator

## Slide 98: Seven-Segment Indicator

## Slide 99: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1

## Slide 100: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d

## Slide 101: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d

## Slide 102: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d
x
3
x
2
x
1
x
0
00
01
11
10
00
01
11
10

## Slide 103: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
1
d
1
1
1
d
d
1
1
d
d
00
01
11
10

## Slide 104: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d d d d d d d d
d d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
1
d
1
1
1
d
d
1
1
d
d
00
01
11
10

## Slide 105: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d
1 d d d d d d
1 d d d d d d
1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
1
1
0
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
In this case all d's were treated as 1's.

## Slide 106: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d

## Slide 107: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
00
01
11
10
00
01
11
10

## Slide 108: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
0
d
0
0
0
d
d
1
1
d
d
00
01
11
10

## Slide 109: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d 1 d d d d d d
1 d d d d d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
d
1
0
0
d
0
0
0
d
d
1
1
d
d
00
01
11
10

## Slide 110: Seven-Segment Indicator
0 1 0
1 0 1 1
1 0 0
1 1 0 1
1 1 1 0
1 1 1
1 d d d 1 d d
1 d d d 0 d d 1 d d d 0 d d
1 d d d 0 d d 1 d d d 1 d d
1 d d d 0 d d
x
3
x
2
x
1
x
0
1
00
01
11
10
0
0
1
0
0
0
0
0
0
0
0
1
1
1
1
00
01
11
10
In this case some d's were treated as 1's, others as 0's.

## Slide 111: Seven-Segment Indicator

## Slide 112: Another Example

## Slide 113
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
[ Figure 2.64 from the textbook ]

## Slide 114
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2

## Slide 115
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_

## Slide 116
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_

## Slide 117
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_

## Slide 118
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_

## Slide 119
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_
x1 x3
_

## Slide 120
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 121
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 122
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 123
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 124
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 125
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
x1 x3
_
x1 x3
_
x1 x3
_
x2 x3 x4
_
x2 x3 x4

## Slide 126
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
00
01
11
10
(a) Function
1
f
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
1
1
1
1
1
00
01
11
10
(b) Function
f
2
f
1
f
2
x
2
x
3
x
4
x
1
x
3
x
1
x
3
x
2
x
3
x
4
(c) Combined circuit for
f
1
f
2
and
[ Figure 2.64 from the textbook ]

## Slide 127: Individual vs Joint Optimization

## Slide 128: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1

## Slide 129: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1

## Slide 130: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1

## Slide 131: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
cost = 14
cost = 15

## Slide 132: Individual Optimization
f
3
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
3
x
2
f
4
x
4
x
3
x
4
x
1
x
1
x
2
x
4
Circuit only for
f
4
x
2
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
1
f
3
1
1
(b) Optimal realization of
f
4
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
cost = 14
cost = 15
TOTAL cost: 29

## Slide 134: Individual vs Joint Optimization
[ Figure 2.65 from the textbook ]
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
(a) Optimal realization of
(b) Optimal realization of
1
f
3
f
4
(c) Optimal realization of
f
3
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
Individual
Joint

## Slide 135: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2

## Slide 136: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2
shared gate

## Slide 137: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2
another shared gate

## Slide 138: Joint Optimization
[ Figure 2.65 from the textbook ]
(c) Optimal realization of
f
3
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
x
1
x
2
x
3
x
4
00
01
11
10
1
1
1
1
00
01
11
10
1
1
1
and
together
f
4
f
3
f
4
x
1
x
4
x
3
x
4
x
1
x
1
x
2
x
2
x
4
x
4
(d) Combined circuit for
f
3
f
4
and
x
2
cost = 23

## Slide 139: Questions?

## Slide 140: THE END