## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Examples of Solved Problems
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW4 is due today

## Slide 4: Administrative Stuff
HW5 is out
It is due on Monday Sep 30 @ 10pm.
It is posted on the class web page
I also sent you an e-mail with the link.
You can use this as a preparation for the exam.

## Slide 5: Administrative Stuff
Midterm Exam #1
When: Friday Sep 27.
What: Chapter 1 and Chapter 2 plus number systems
The exam will be closed book but open notes (you can bring up to 3 pages of handwritten notes).
It will be in this room.
Review session: This Wednesday during lecture

## Slide 6: Topics for the Midterm Exam
Binary Numbers
Octal Numbers
Hexadecimal Numbers
Conversion between the different number systems
Truth Tables
Boolean Algebra
Logic Gates
Circuit Synthesis with AND, OR, NOT
Circuit Synthesis with NAND, NOR
Converting an AND/OR/NOT circuit to NAND circuit
Converting an AND/OR/NOT circuit to NOR circuit
SOP and POS expressions

## Slide 7: Topics for the Midterm Exam
Mapping a Circuit to Verilog code
Mapping Verilog code to a circuit
Multiplexers
Venn Diagrams
K-maps for 2, 3, and 4 variables
Minimization of Boolean expressions using theorems
Minimization of Boolean expressions with K-maps
Incompletely specified functions (with don’t cares)
Functions with multiple outputs
Something from Star Wars

## Slide 8: All possible Boolean functions with two input variables

## Slide 9: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 10: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
constant 0
constant 1

## Slide 11: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NOR(x, y)
OR(x, y)

## Slide 12: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
m1 = x y
_
M1 = x + y
_

## Slide 13: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NOT(x)
x

## Slide 14: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
m2 = x y
_
M2 = x + y
_

## Slide 15: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NOT(y)
y

## Slide 16: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
XOR(x, y)
XNOR(x, y)

## Slide 17: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NAND(x, y)
AND(x, y)

## Slide 18: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0
1
NAND
AND
XOR
XNOR
y
m2
M2
x
NOR
OR
m1
M1
x
_
y
_

## Slide 19: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0
1
XOR
XNOR
y
m2
M2
x
m1
M1
x
_
y
_
m0
m3
M0
M3

## Slide 20: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0
1
M1 • M2
y
m2
M2
x
m1
M1
x
_
y
_
m0
m3
M0
M3
m1 + m2

## Slide 21: There are 16 possible Boolean functions with two input variables
x | y | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | F8 | F9 | F10 | F11 | F12 | F13 | F14 | F15
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0
1
M1 • M2
m2
M2
m1
M1
m0
m3
M0
M3
m1 + m2
m0 + m1
m0 + m2
M0 • M2
M0 • M1

## Slide 22: K-Maps for all 16 possible functions with two input variables

## Slide 23: K-Maps for the 16 functions
y
0
1
0
1
1
0
0
0
x
y
0
1
0
1
0
0
0
1
x
y
0
1
0
1
0
1
0
0
x
y
0
1
0
1
0
0
1
0
x
x y
_
_
x y
_
x y
_
x y
F1
F2
F4
F8

## Slide 24: K-Maps for the 16 functions
y
0
1
0
1
1
0
0
1
x
y
0
1
0
1
0
1
1
0
x
y
0
1
0
1
1
1
0
0
x
y
0
1
0
1
0
0
1
1
x
x
_
x
y
_
y
F3
F12
F5
F10

## Slide 25: K-Maps for the 16 functions
y
0
1
0
1
1
1
0
1
x
y
0
1
0
1
1
0
1
1
x
y
0
1
0
1
1
1
1
0
x
y
0
1
0
1
0
1
1
1
x
x + y
_
_
x + y
_
x + y
_
x + y
F7
F11
F13
F14

## Slide 26: K-Maps for the 16 functions
y
0
1
0
1
0
0
0
0
x
constant 0
y
0
1
0
1
1
1
1
1
x
constant 1
F0
F15

## Slide 27: These are not valid groupings, but they correspond to XOR and XNOR
y
0
1
0
1
1
0
1
0
x
y
0
1
0
1
0
1
0
1
x

## Slide 28: These are not valid groupings, but they correspond to XOR and XNOR
y
0
1
0
1
1
0
1
0
x
y
0
1
0
1
0
1
0
1
x
XOR(x, y)
XNOR(x, y)
F6
F9

## Slide 29: The Link Between Truth Tables and Venn Diagrams

## Slide 30: Place the minterms on the Venn diagram
A | B | 
0 | 0 | m0
0 | 1 | m1
1 | 0 | m2
1 | 1 | m3

## Slide 31: Place the minterms on the Venn diagram
A | B | 
0 | 0 | m0
0 | 1 | m1
1 | 0 | m2
1 | 1 | m3

## Slide 33: Color the Venn diagram for XOR
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 34: Color the Venn diagram for XOR
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 35: Color the Venn diagram for XOR
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
m0
m1
m2
m3
F = A B + A B

## Slide 37: Place the minterms on the Venn diagram
A | B | C | 
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7

## Slide 38: Place the minterms on the Venn diagram
A | B | C | 
0 | 0 | 0 | m0
0 | 0 | 1 | m1
0 | 1 | 0 | m2
0 | 1 | 1 | m3
1 | 0 | 0 | m4
1 | 0 | 1 | m5
1 | 1 | 0 | m6
1 | 1 | 1 | m7

## Slide 40: Color the Venn diagram for this function
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 41: Color the Venn diagram for this function
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 42: Place the minterms on the Venn diagram
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
m0
m1
m2
m3
m4
m5
m6
m7

## Slide 44: Color the Venn diagram for this function
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 45: Color the Venn diagram for this function
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 46: Place the minterms on the Venn diagram
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
m0
m1
m2
m3
m4
m5
m6
m7

## Slide 48: Write the expression that is represented by each of the three Venn diagrams:

## Slide 49: Write the expression that is represented by each of the three Venn diagrams:
X Y
X Y
_
X Y Z
_
_

## Slide 50: Example 1
Determine if the following equation is valid

## Slide 51
?

## Slide 52
?
LHS
RHS

## Slide 53: Left-Hand Side (LHS)

## Slide 54: Left-Hand Side (LHS)

## Slide 55: Left-Hand Side (LHS)

## Slide 56: Right-Hand Side (RHS)

## Slide 57: Right-Hand Side (RHS)

## Slide 58: Right-Hand Side (RHS)

## Slide 59
?
LHS
RHS
They are equal.

## Slide 60: Example 2
Design the minimum-cost product-of-sums expression for the function
f(x1, x2, x3) = Σ m(0, 2, 4, 5, 6, 7)

## Slide 61: Minterms and Maxterms (with three variables)
[ Figure 2.22 from the textbook ]

## Slide 62: Minterms and Maxterms (with three variables)
The function is
1 for these rows

## Slide 63: Minterms and Maxterms (with three variables)
The function is
1 for these rows
The function is
0 for these rows

## Slide 64: Two different ways to specify the same function f of three variables
f(x1, x2, x3) = Σ m(0, 2, 4, 5, 6, 7)
f(x1, x2, x3) = Π M(1, 3)

## Slide 65: Two different ways to specify the same function f of three variables
f(x1, x2, x3) = Σ m(0, 2, 4, 5, 6, 7)
f(x1, x2, x3) = Π M(1, 3)
= M1 M3
= ( x1 + x2 + x3)( x1 + x2 + x3)

## Slide 66: The Minimum POS Expression
f(x1, x2, x3)
= ( x1 + x2 + x3)( x1 + x2 + x3)
= ( x1 + x3 + x2)( x1 + x3 + x2)
= ( x1 + x3 )
Hint: Use the following Boolean Algebra theorem

## Slide 67: Alternative Solution Using K-Maps

## Slide 68: Alternative Solution Using K-Maps

## Slide 69: Alternative Solution Using K-Maps

## Slide 70: Alternative Solution Using K-Maps

## Slide 71: Alternative Solution Using K-Maps
1
0
0
1
1
1
1
1

## Slide 72: Alternative Solution Using K-Maps
1
0
0
1
1
1
1
1
( x1 + x3 )

## Slide 73: Example 3

## Slide 74: Condition A

## Slide 75: Condition A

## Slide 76: Condition B

## Slide 77: Condition B

## Slide 78: Condition C

## Slide 79: Condition C

## Slide 80: The output of the circuit can be expressed as f = AB + AC + BC

## Slide 81: The output of the circuit can be expressed as f = AB + AC + BC

## Slide 82: The output of the circuit can be expressed as f = AB + AC + BC

## Slide 83: Finally, we get

## Slide 84: Example 4
Solve the previous problem using Venn diagrams.

## Slide 85: Venn Diagrams (find the areas that are shaded at least two times)
(a) Function
A:
(b) Function
B
(c) Function
C
(d) Function
f
x1
x2
x3
x1
x2
x3
[ Figure 2.66 from the textbook ]
x1
x3
x2
x2
x1
x2
x3

## Slide 86: Example 5
Design the minimum-cost SOP and POS
expression for the function
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)

## Slide 87: Let’s Use a K-Map
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)

## Slide 88: Let’s Use a K-Map
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 89: Let’s Use a K-Map
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 90: Let’s Use a K-Map
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 91: Let’s Use a K-Map
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 92: Two Alternative Solutions
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 93: The SOP Expression
[ Figure 2.67a from the textbook ]
_ _ _ _
f = x1 x2 + x1 x2 + x1 x3 x4 + x3 x4

## Slide 94: What about the POS Expression?
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 95: What about the POS Expression?
f(x1, x2, x3, x4) = Σ m(4, 6, 8, 10, 11, 12, 15) + D(3, 5, 7, 9)
0
0
1
d
d
0
d
1
1
0
1
d
1
0
1
1

## Slide 96: The POS Expression
[ Figure 2.67b from the textbook ]
_ _ _ _
f = (x1 + x2)•(x3 + x4)•(x1 + x2 + x3 + x4)

## Slide 97: Example 6
Use K-maps to find the minimum-cost SOP and POS
expression for the function

## Slide 98: Let’s map the expression to the K-Map

## Slide 99: Let’s map the expression to the K-Map
d
d
d

## Slide 100: Let’s map the expression to the K-Map
d
d
d

## Slide 101: Let’s map the expression to the K-Map
d
d
d

## Slide 102: Let’s map the expression to the K-Map
d
d
d

## Slide 103: Let’s map the expression to the K-Map
d
d
d

## Slide 104: Let’s map the expression to the K-Map
d
d
d

## Slide 105: Let’s map the expression to the K-Map
1
1
1
0
1
0
1
0
d
1
0
d
1
d
1
0
d
d
d

## Slide 106: Let’s map the expression to the K-Map
1
1
1
0
1
0
1
0
d
1
0
d
1
d
1
0

## Slide 107: Let’s map the expression to the K-Map
1
1
1
0
1
0
1
0
d
1
0
d
1
d
1
0

## Slide 108: The SOP Expression
[ Figure 2.68a from the textbook ]

## Slide 109: What about the POS Expression?
1
1
1
0
1
0
1
0
d
1
0
d
1
d
1
0

## Slide 110: What about the POS Expression?
1
1
1
0
1
0
1
0
d
1
0
d
1
d
1
0

## Slide 111: The POS Expression
[ Figure 2.68b from the textbook ]

## Slide 112: Example 7
Derive the minimum-cost SOP expression for

## Slide 113: First, expand the expression using property 12a

## Slide 114: Construct the K-Map for this expression
s1 s2 s3
s1 s2
s3

## Slide 115: Construct the K-Map for this expression
s1 s2 s3
s1 s2
s3

## Slide 116: Construct the K-Map for this expression
s1 s2 s3
s1 s2
s3

## Slide 117: Construct the K-Map for this expression
s1 s2 s3
s1 s2
s3

## Slide 118: Construct the K-Map for this expression
s1 s2 s3
s1 s2
s3
0
1
0
1
1
1
1
0
0
1
0
1
0
1
1
1

## Slide 119: Construct the K-Map for this expression
s1 s2 s3
s1 s2
s3
0
1
0
1
1
1
1
0
0
1
0
1
0
1
1
1
Simplified Expression: f = s3 + s1 s2

## Slide 120: Construct the K-Map for this expression
[ Figure 2.69 from the textbook ]

## Slide 121: Construct the K-Map for this expression
[ Figure 2.69 from the textbook ]
Simplified Expression: f = s3 + s1 s2

## Slide 122: Example 8
Write the Verilog code for the following circuit …

## Slide 123: Logic Circuit
[ Figure 2.70 from the textbook ]

## Slide 124: Circuit for 2-1 Multiplexer
f
x
1
x
2
s
f
s
x
1
x
2
0
1
(c) Graphical symbol
(b) Circuit
[ Figure 2.33b-c from the textbook ]
f (s, x1, x2) =
s x1
s x2
+

## Slide 125: Logic Circuit vs Verilog Code
[ Figure 2.71 from the textbook ]
[ Figure 2.70 from the textbook ]

## Slide 126: Example 9
Write the Verilog code for the following circuit …

## Slide 127: The Logic Circuit for this Example
[ Figure 2.72 from the textbook ]

## Slide 128: Circuit for 2-1 Multiplexer
f
x
1
x
2
s
f
s
x
1
x
2
0
1
(c) Graphical symbol
(b) Circuit
[ Figure 2.33b-c from the textbook ]
f (s, x1, x2) =
s x1
s x2
+

## Slide 129
Addition of Binary Numbers

## Slide 130: Logic Circuit vs Verilog Code
[ Figure 2.73 from the textbook ]

## Slide 131: Some material form Appendix B

## Slide 132: Programmable Logic Array (PLA)
f
1
AND plane
OR plane
Input buffers
inverters
and
P
1
P
k
f
m
x
1
x
2
x
n
x
1
x
1
x
n
x
n
[ Figure B.25 from textbook ]

## Slide 133: Gate-Level Diagram of a PLA
f
1
P
1
P
2
f
2
x
1
x
2
x
3
OR plane
Programmable
AND plane
connections
P
3
P
4
[ Figure B.26 from textbook ]

## Slide 134: Customary Schematic for PLA
f
1
P
1
P
2
f
2
x
1
x
2
x
3
OR plane
AND plane
P
3
P
4
[ Figure B.27 from textbook ]

## Slide 135: Programmable Array Logic (PAL)
f
1
P
1
P
2
f
2
x
1
x
2
x
3
AND plane
P
3
P
4
[ Figure B.28 from textbook ]

## Slide 136: Programmable Array Logic (PAL)
f
1
P
1
P
2
f
2
x
1
x
2
x
3
AND plane
P
3
P
4
[ Figure B.28 from textbook ]
Only the AND plane is programmable.
The OR plane is fixed.

## Slide 137: Questions?

## Slide 138: THE END