## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Signed Numbers
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3
Signed Integer Numbers
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 4
Today’s Lecture is About
Addition and Subtraction of
Signed Numbers

## Slide 5
Quick Review

## Slide 6
Signed v.s. Unsigned Numbers

## Slide 7
Signed v.s. Unsigned Numbers
positive
and
negative
integers
only
positive
integers

## Slide 8
Signed v.s. Unsigned Numbers
positive
and
negative
integers
and zero
only
positive
integers
and zero

## Slide 9: Two Different Types of Binary Numbers
Unsigned numbers
All bits jointly represent a positive integer.
Negative numbers cannot be represented this way.
Signed numbers
The left-most bit represents the sign of the number.
If that bit is 0, then the number is positive.
If that bit is 1, then the number is negative.
The magnitude of the largest number that can be represented in this way is twice smaller than the largest number in the unsigned representation.

## Slide 10: Two Different Types of Binary Numbers
Unsigned numbers
All bits jointly represent a positive integer.
Negative numbers cannot be represented this way.
Signed numbers
The left-most bit represents the sign of the number.
If that bit is 0, then the number is positive.
If that bit is 1, then the number is negative.
The magnitude of the largest number that can be represented in this way is twice smaller than the largest number in the unsigned representation.
There are 3 different ways to represent signed numbers. They will be introduced today.
But only the last method will be used later.

## Slide 11
Important Clarificaiton

## Slide 12
Important Clarification:
There are two types of addition
Addition of Boolean variables, e.g.,
  x + y where x, y ∊ {0, 1}
Addition of n-bit Binary numbers, e.g.,
  x4x3x2x1x0 + y4y3y2y1y0 where each xk, yk ∊ {0, 1}

## Slide 13
Important Clarification:
There are two types of addition
Addition of Boolean variables, e.g.,
  1 + 0 = 1
Addition of n-bit Binary numbers, e.g.,
  00101 + 00110 = 01011

## Slide 14
Important Clarification:
There are two types of addition
Addition of two Boolean variables, e.g.,
Addition of two 5-bit Binary numbers, e.g.,
1
0
1

## Slide 15
Important Clarification:
There are two types of addition
Addition of two Boolean variables, e.g.,
Addition of two 5-bit Binary numbers, e.g.,
1
0
1
we derived this
circuit last time

## Slide 16
Important Clarification:
There are two types of addition
Addition of two Boolean variables, e.g.,
  1 + 1 = 1 (according to the rules of Boolean algebra)
Addition of two 1-bit Binary numbers, e.g.,
  1 + 1 = 10 (because in decimal 1 + 1 = 2 )

## Slide 17
Important Clarification:
There are two types of addition
Addition of two Boolean variables, e.g.,
Addition of two 1-bit Binary numbers, e.g.,
1
1
1
0
1
1
1
In this case, the
adder circuit simplifies
to the half-adder.

## Slide 18
Addition of 1-bit Unsigned Numbers

## Slide 19
[ Figure 3.1a from the textbook ]
Addition of two 1-bit numbers
(there are four possible cases)

## Slide 20
[ Figure 3.1a from the textbook ]
Addition of two 1-bit numbers
(there are four possible cases)
010
110
110
210

## Slide 21
[ Figure 3.1b from the textbook ]
Adding two bits
(the truth table)
s

## Slide 22
[ Figure 3.1b from the textbook ]
Adding two bits
(the truth table)
s
+
+
+
+
=
=
=
=
= 010
= 110
= 110
= 210

## Slide 23
[ Figure 3.1c from the textbook ]
Adding two bits
(the logic circuit)

## Slide 24
[ Figure 3.1c-d from the textbook ]
The Half-Adder

## Slide 25
Addition of Multibit Unsigned Numbers

## Slide 26
Bit position i
Addition of multibit numbers
[ Figure 3.2 from the textbook ]

## Slide 27: Analogy with addition in base 10
c3 c2 c1 c0
x2 x1 x0
y2 y1 y0
s2 s1 s0
+

## Slide 28: Analogy with addition in base 10
3 8 9
1 5 7
5 4 6
+

## Slide 29: Analogy with addition in base 10
0 1 1 0
3 8 9
1 5 7
5 4 6
+
carry

## Slide 30: Analogy with addition in base 10
c3 c2 c1 c0
x2 x1 x0
y2 y1 y0
s2 s1 s0
+

## Slide 31: Another example in base 10
9 3 8
2 1 4
1 1 5 2
+

## Slide 32: Another example in base 10
1 0 1 0
9 3 8
2 1 4
1 5 2
+
carry

## Slide 33: Example in base 2
1 0 1
1 1 0
+

## Slide 34: Example in base 2
1 0 0 0
1 0 1
1 1 0
1 0 1 1
+
carry

## Slide 35: Example in base 2
1 0 0 0
1 0 1
1 1 0
1 0 1 1
+
carry
610
510
1110
+

## Slide 36
Problem Statement and Truth Table
[ Figure 3.3a from the textbook ]
[ Figure 3.2b from the textbook ]

## Slide 37
Problem Statement and Truth Table
[ Figure 3.3a from the textbook ]
[ Figure 3.2b from the textbook ]
= 010
= 110
= 110
= 210
= 110
= 210
= 210
= 310
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
=
=
=
=
=
=
=
=

## Slide 38
Let’s fill-in the two K-maps
[ Figure 3.3a-b from the textbook ]

## Slide 39
Let’s fill-in the two K-maps
[ Figure 3.3a-b from the textbook ]

## Slide 40
The circuit for the two expressions
[ Figure 3.3c from the textbook ]

## Slide 41
This is called the Full-Adder
[ Figure 3.3c from the textbook ]

## Slide 42
XOR Magic
(si can be implemented in two different ways)

## Slide 43
These two circuits are equivalent
c
i
x
i
y
i
c
i
1
+
s
i
ci+1 =( xi + yi )ci + xi yi
si = xi + yi + ci

## Slide 44
HA
HA
s
c
s
c
c
i
x
i
y
i
c
i
1
+
s
i
c
i
x
i
y
i
c
i
1
+
s
i
(a) Block diagram
(b) Detailed diagram
A decomposed implementation
of the full-adder circuit
[ Figure 3.4 from the textbook ]

## Slide 45
HA
HA
s
c
s
c
c
i
x
i
y
i
c
i
1
+
s
i
c
i
x
i
y
i
c
i
1
+
s
i
(a) Block diagram
(b) Detailed diagram
A decomposed implementation
of the full-adder circuit
[ Figure 3.4 from the textbook ]
HA
HA

## Slide 46
FA
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 47
FA
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 48
FA
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 49
FA
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 50
HA
HA
s
c
s
c
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 51
FA
c
i
x
i
y
i
c
i
1
+
s
i
The Full-Adder Abstraction

## Slide 52
FA
We can place the arrows anywhere
xi
yi
si
ci+1
ci

## Slide 53
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
MSB position
LSB position
n-bit ripple-carry adder
[ Figure 3.5 from the textbook ]
-

## Slide 54
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
MSB position
LSB position
n-bit ripple-carry adder abstraction
-

## Slide 55
x
n –
1
c
n
y
n
1
–
s
n
1
–
x
1
y
1
s
1
x
0
y
0
s
0
c
0
n-bit ripple-carry adder abstraction

## Slide 56
The x and y lines are typically
grouped together for better visualization,
but the underlying logic remains the same
x
n –
1
c
n
y
n
1
–
s
n
1
–
x
1
y
1
s
1
y
0
s
0
c
0
x
0

## Slide 57
Example:
Computing 5+6 using a 5-bit adder

## Slide 58
Example:
Computing 5+6 using a 5-bit adder
11 in decimal
5 in decimal
6 in decimal
0 in decimal

## Slide 59
Example:
Computing 5+6 using a 5-bit adder
11 in decimal
5 in decimal
6 in decimal
0
0 0 1 0 1
0 0 1 1 0
0 0 1 0 1 1
+
0

## Slide 60
Math Review

## Slide 61: Math Review: Subtraction
39
15
-
??

## Slide 62: Math Review: Subtraction
39
15
-
24

## Slide 63: Math Review: Subtraction
82
61
-
??
48
26
-
??
32
11
-
??

## Slide 64: Math Review: Subtraction
82
61
-
21
48
26
-
22
32
11
-
21

## Slide 66: Math Review: Subtraction
82
64
-
??
48
29
-
??
32
13
-
??

## Slide 67: Math Review: Subtraction
82
64
-
18
48
29
-
19
32
13
-
19

## Slide 69: The problems in which row are easier to calculate?
82
64
-
??
48
29
-
??
32
13
-
??
82
61
-
??
48
26
-
??
32
11
-
??

## Slide 70: The problems in which row are easier to calculate?
82
64
-
18
48
29
-
19
32
13
-
19
82
61
-
21
48
26
-
22
32
11
-
21
Why?

## Slide 71: Another Way to Do Subtraction
82 – 64 = 82 + 100 – 100 - 64

## Slide 72: Another Way to Do Subtraction
82 – 64 = 82 + 100 – 100 - 64
= 82 + (100 – 64) - 100

## Slide 73: Another Way to Do Subtraction
82 – 64 = 82 + 100 – 100 - 64
= 82 + (100 – 64) - 100
= 82 + (99 + 1 – 64) - 100

## Slide 74: Another Way to Do Subtraction
82 – 64 = 82 + 100 – 100 - 64
= 82 + (100 – 64) - 100
= 82 + (99 + 1 – 64) - 100
= 82 + (99 – 64) +1 - 100

## Slide 75: Another Way to Do Subtraction
82 – 64 = 82 + 100 – 100 - 64
= 82 + (100 – 64) - 100
= 82 + (99 + 1 – 64) - 100
= 82 + (99 – 64) +1 - 100
Does not require borrows

## Slide 76: 9’s Complement (subtract each digit from 9)
99
64
-
35

## Slide 77: 10’s Complement (subtract each digit from 9 and add 1 to the result)
99
64
-
35 + 1 = 36

## Slide 78: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100

## Slide 79: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100
9’s complement

## Slide 80: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100
= 82 + 35 + 1 - 100
9’s complement

## Slide 81: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100
= 82 + 35 + 1 - 100
9’s complement
10’s complement

## Slide 82: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100
= 82 + 35 + 1 - 100
9’s complement
= 82 + 36 - 100
10’s complement

## Slide 83: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100
= 82 + 35 + 1 - 100
= 118 - 100
9’s complement
= 82 + 36 - 100
10’s complement
// Add the first two.

## Slide 84: Another Way to Do Subtraction
82 – 64 = 82 + (99 – 64) +1 - 100
= 82 + 35 + 1 - 100
= 118 - 100
9’s complement
= 82 + 36 - 100
= 18
10’s complement
// Add the first two.
// Just delete the leading 1.
// No need to subtract 100.

## Slide 85: Ways to Represent Negative Integers

## Slide 86
b
n
1
–
b
1
b
0
Magnitude
MSB
(a) Unsigned number
b
n
1
–
b
1
b
0
Magnitude
Sign
(b) Signed number
b
n
2
–
0 denotes
1 denotes
+
–
MSB
Formats for representation of integers
[ Figure 3.7 from the textbook ]

## Slide 87: Unsigned Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
27
This represents + 44.

## Slide 88: Unsigned Representation
1
0
1
0
1
1
0
0
20
21
22
23
24
25
26
27
This represents + 172.

## Slide 89
Three Different Ways to
Represent Negative Integer Numbers
Sign and magnitude
1’s complement
2’s complement

## Slide 90
Three Different Ways to
Represent Negative Integer Numbers
Sign and magnitude
1’s complement
2’s complement
only this method is used
in modern computers

## Slide 91
[ Table 3.2 from the textbook ]
Interpretation of four-bit signed integers

## Slide 92
Interpretation of four-bit signed integers
The top half is the same in all three representations.
It corresponds to the positive integers.

## Slide 93
Interpretation of four-bit signed integers
In all three representations the first bit represents the sign.
If that bit is 1, then the number is negative.

## Slide 94
Interpretation of four-bit signed integers
Notice that in this representation there are two zeros!

## Slide 95
Interpretation of four-bit signed integers
There are two zeros in this representation as well!

## Slide 96
Interpretation of four-bit signed integers
In this representation there is one more negative number.

## Slide 97: Sign and Magnitude

## Slide 98: Sign and Magnitude Representation (using the left-most bit as the sign)
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
This represents + 44.

## Slide 99: Sign and Magnitude Representation (using the left-most bit as the sign)
1
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
This represents – 44.

## Slide 100: Circuit for negating a number stored in sign and magnitude representation
y7
y7
_
y6
y6
y5
y5
y4
y4
y3
y3
y2
y2
y1
y1
y0
y0

## Slide 101: Circuit for negating a number stored in sign and magnitude representation
0
1
0
0
1
1
0
0
1
1
1
1
0
0
0
0

## Slide 102: 1’s Complement

## Slide 103
Let K be the negative equivalent of an n-bit positive number P.
Then, in 1’s complement representation K is obtained by subtracting P from 2n – 1, namely
K = (2n – 1) – P
This means that K can be obtained by inverting all bits of P.
1’s complement
(subtract each digit from 1)

## Slide 104
Let K be the negative equivalent of an 8-bit positive number P.
Then, in 1’s complement representation K is obtained by subtracting P from 28 – 1, namely
K = (28 – 1) – P = 255 - P
This means that K can be obtained by inverting all bits of P.
Provided that P is between 0 and 127, because the most significant bit must be zero to indicate that it is positive.
1’s complement
(subtract each digit from 1)

## Slide 105: 1’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign

## Slide 106: 1’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
25 + 23 + 22 = 44

## Slide 107: 1’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
+ 44 in 1’s complement representation

## Slide 108: 1’s Complement Representation (invert all the bits to negate the number)
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44

## Slide 109: 1’s Complement Representation (invert all the bits to negate the number)
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
negative
positive

## Slide 110: 1’s Complement Representation (invert all the bits to negate the number)
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
27 + 26 + 24 + 21 + 20 = 211 (as unsigned)

## Slide 111: 1’s Complement Representation (invert all the bits to negate the number)
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
211 = 255 – 44 (as unsigned)

## Slide 112: 1’s Complement Representation (invert all the bits to negate the number)
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
- 44 in 1’s complement representation

## Slide 113
1
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
1’s complement
(subtract each digit from 1)
0
0
1
0
1
1
0
0
_

## Slide 114
1
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
1’s complement
(subtract each digit from 1)
0
0
1
0
1
1
0
0
_
No need to borrow!

## Slide 115
1
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
1’s complement
(subtract each digit from 1)
0
0
1
0
1
1
0
0
_
255
44

## Slide 116
1
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
1’s complement
(subtract each digit from 1)
0
0
1
0
1
1
0
0
_
211
211 = 255 – 44 (as unsigned)

## Slide 117
1
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
1’s complement
(subtract each digit from 1)
0
0
1
0
1
1
0
0
_
- 44
211 = 255 – 44 (as unsigned)
or
- 44 in 1’s complement representation

## Slide 118: Circuit for negating a number stored in 1’s complement representation
y7
y7
_
y6
y6
_
y5
y5
_
y4
y4
_
y3
y3
_
y2
y2
_
y1
y1
_
y0
y0
_

## Slide 119: Circuit for negating a number stored in 1’s complement representation
0
1
0
1
1
0
0
1
1
0
1
0
0
1
0
1

## Slide 120: This works in reverse too (from negative to positive)

## Slide 121: 1’s Complement Representation
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44

## Slide 122: 1’s Complement Representation (invert all the bits to negate the number)
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44

## Slide 123: 1’s Complement Representation (invert all the bits to negate the number)
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
44 = 255 – 211 (as unsigned)
211 (as unsigned)

## Slide 124: 1’s Complement Representation (invert all the bits to negate the number)
1
1
0
1
0
0
1
1
20
21
22
23
24
25
26
sign
- 44
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
- 44 in 1’s complement representation
+ 44 in 1’s complement representation

## Slide 125
0 1 0 1
1 0 1 1
0 1 1 1
1 1 1 0
Negate these numbers stored in
1’s complement representation

## Slide 126
0 1 0 1
1 0 1 1
0 1 1 1
1 1 1 0
1 0 1 0
0 1 0 0
1 0 0 0
0 0 0 1
Just flip 1's to 0's and vice versa.
Negate these numbers stored in
1’s complement representation

## Slide 127
0 1 0 1 = +5
1 0 1 1 = -4
0 1 1 1 = +7
1 1 1 0 = -1
1 0 1 0 = -5
0 1 0 0 = +4
1 0 0 0 = -7
0 0 0 1 = +1
Just flip 1's to 0's and vice versa.
Negate these numbers stored in
1’s complement representation

## Slide 128: Addition of two numbers stored in 1’s complement representation

## Slide 129: There are four cases to consider
(+5) + (+2)
(-5) + (+2)
(+5) + (-2)
(-5) + (-2)

## Slide 130: There are four cases to consider
(+5) + (+2) positive plus positive
(-5) + (+2) negative plus positive
(+5) + (-2) positive plus negative
(-5) + (-2) negative plus negative

## Slide 131
A) Example of 1’s complement addition
+
0 1 1 1
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
7
+
(
)
+
[ Figure 3.8 from the textbook ]

## Slide 132
A) Example of 1’s complement addition
+
0 1 1 1
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
7
+
(
)
+

## Slide 133
B) Example of 1’s complement addition
+
1 1 0 0
1 0 1 0
0 0 1 0
5
-
(
)
2
+
(
)
3
-
(
)
+
[ Figure 3.8 from the textbook ]

## Slide 134
B) Example of 1’s complement addition
+
1 1 0 0
1 0 1 0
0 0 1 0
5
-
(
)
2
+
(
)
3
-
(
)
+

## Slide 135
C) Example of 1’s complement addition
+
0 0 1 0
0 1 0 1
1 1 0 1
1
5
+
(
)
3
+
(
)
+
2
–
(
)
[ Figure 3.8 from the textbook ]

## Slide 136
C) Example of 1’s complement addition
+
0 0 1 0
0 1 0 1
1 1 0 1
1
5
+
(
)
3
+
(
)
+
2
–
(
)

## Slide 137
C) Example of 1’s complement addition
+
0 0 1 0
0 1 0 1
1 1 0 1
1
5
+
(
)
3
+
(
)
+
2
–
(
)
But this is 2!

## Slide 138
C) Example of 1’s complement addition
+
0 0 1 0
0 1 0 1
1 1 0 1
1
1
0 0 1 1
5
+
(
)
3
+
(
)
+
2
–
(
)
We need to perform one
more addition to get the result.

## Slide 139
0 0 1 0
C) Example of 1’s complement addition
+
0 1 0 1
1 1 0 1
1
1
0 0 1 1
5
+
(
)
3
+
(
)
+
2
–
(
)
We need to perform one
more addition to get the result.

## Slide 140
D) Example of 1’s complement addition
+
0 1 1 1
1 0 1 0
1 1 0 1
1
5
–
(
)
7
–
(
)
+
2
–
(
)
[ Figure 3.8 from the textbook ]

## Slide 141
D) Example of 1’s complement addition
+
0 1 1 1
1 0 1 0
1 1 0 1
1
5
–
(
)
7
–
(
)
+
2
–
(
)

## Slide 142
D) Example of 1’s complement addition
+
0 1 1 1
1 0 1 0
1 1 0 1
1
5
–
(
)
7
–
(
)
+
2
–
(
)
But this is +7!

## Slide 143
D) Example of 1’s complement addition
We need to perform one
more addition to get the result.
+
0 1 1 1
1 0 1 0
1 1 0 1
1
1
1 0 0 0
5
–
(
)
7
–
(
)
+
2
–
(
)

## Slide 144
D) Example of 1’s complement addition
We need to perform one
more addition to get the result.
+
0 1 1 1
1 0 1 0
1 1 0 1
1
1
1 0 0 0
5
–
(
)
7
–
(
)
+
2
–
(
)

## Slide 145
Implications for arithmetic operations
in 1’s complement representation
We could do addition in 1’s complement, but the circuit will need to handle these exceptions.
In some cases, it will run faster that others, thus creating uncertainties in the timing.
Therefore, 1’s complement is not used in practice to do arithmetic operations.
But it may show up as an intermediary step in doing 2’s complement operations.

## Slide 146: 2’s Complement

## Slide 147
Let K be the negative equivalent of an n-bit positive number P.
Then, in 2’s complement representation K is obtained by subtracting P from 2n , namely
K = 2n – P
2’s complement
(subtract each digit from 1 and add 1 to the result)

## Slide 148
Let K be the negative equivalent of an 8-bit positive number P.
Then, in 2’s complement representation K is obtained by subtracting P from 28 , namely
K = 28 – P = 256 - P
2’s complement
(subtract each digit from 1 and add 1 to the result)

## Slide 149: 2’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44

## Slide 150: 2’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
1
0
0
20
21
22
23
24
25
26
sign
- 44

## Slide 151: 2’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
1
0
0
20
21
22
23
24
25
26
sign
- 44
negative
positive

## Slide 152: 2’s Complement Representation
0
0
1
0
1
1
0
0
20
21
22
23
24
25
26
sign
+ 44
1
1
0
1
0
1
0
0
20
21
22
23
24
25
26
sign
- 44
212 = 256 - 44

## Slide 153
For a positive n-bit number P, let K1 and K2 denote its 1’s and 2’s complements, respectively.
K1 = (2n – 1) – P
K2 = 2n – P
Since K2 = K1 + 1, it is evident that in a logic circuit the 2’s complement can be computed by inverting all bits of P and then adding 1 to the resulting 1’s-complement number.
Deriving 2’s complement

## Slide 154
For a positive 8-bit number P, let K1 and K2 denote its 1’s and 2’s complements, respectively.
K1 = (2n – 1) – P = 255 - P
K2 = 2n – P = 256 - P
Since K2 = K1 + 1, it is evident that in a logic circuit the 2’s complement can be computed by inverting all bits of P and then adding 1 to the resulting 1’s-complement number.
Deriving 2’s complement

## Slide 155
0 1 0 1
0 1 1 1
1 1 0 0
Negate these numbers stored in
2’s complement representation
1 1 1 0

## Slide 156
0 1 0 1
0 1 1 1
1 0 1 0
1 0 0 0
Invert all bits…
Negate these numbers stored in
2’s complement representation
1 1 1 0
0 0 0 1
1 1 0 0
0 0 1 1

## Slide 157
0 1 0 1
0 1 1 1
1 0 1 0
1
1 0 1 1
+
1 0 0 0
1
1 0 0 1
+
.. then add 1.
Negate these numbers stored in
2’s complement representation
1 1 1 0
0 0 0 1
1
0 0 1 0
+
1 1 0 0
0 0 1 1
1
0 1 0 0
+

## Slide 158
0 1 0 1
1 1 1 0
0 1 1 1
1 1 0 0
1 0 1 0
1
1 0 1 1
+
0 0 1 1
1
0 1 0 0
+
1 0 0 0
1
1 0 0 1
+
0 0 0 1
1
0 0 1 0
+
Negate these numbers stored in
2’s complement representation
= +5
= -5
= -2
= +2
= -4
= +4
= +7
= -7

## Slide 159
Circuit #1 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
1
1
0
1
0
1
1
0

## Slide 160
Circuit #1 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
1
1
0
1
0
1
1
0
= +5
(in 2’s complement)

## Slide 161
Circuit #1 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
1
1
0
1
0
1
1
0
invert all the bits

## Slide 162
Circuit #1 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
1
1
0
1
0
1
1
0
+1 =
(in 2’s complement)

## Slide 163
Circuit #1 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
1
1
0
1
0
1
1
0
= -5 (in 2’s complement)

## Slide 164: Alternative Circuit

## Slide 165
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0

## Slide 166
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
0 =
(in 2’s complement)

## Slide 167
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
= +5
(in 2’s complement)

## Slide 168
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
invert all the bits

## Slide 169
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
add 1 by setting the
c0 carry input to 1

## Slide 170
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
= -5 (in 2’s complement)

## Slide 171: This also works for negating a negative number, thus making it positive

## Slide 172
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0

## Slide 173
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
0 =
(in 2’s complement)

## Slide 174
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
= -4
(in 2’s complement)

## Slide 175
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
invert all the bits

## Slide 176
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
add 1 by setting the
c0 carry input to 1

## Slide 177
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
= +4 (in 2’s complement)

## Slide 178: Quick way (for a human) to negate a number stored in 2’s complement
Scan the binary number from right to left
Copy all bits that are 0 from right to left
Stop at the first 1
Copy that 1 as well
Invert all remaining bits

## Slide 179
0 1 0 1
1 1 1 0
0 1 1 1
1 1 0 0
Negate these numbers stored in
2’s complement representation

## Slide 180
0 1 0 1
1 1 1 0
0 1 1 1
1 1 0 0
. . . .
. . 0 0
. . . .
. . . 0
Copy all bits that are 0 from right to left.
Negate these numbers stored in
2’s complement representation

## Slide 181
0 1 0 1
1 1 1 0
0 1 1 1
1 1 0 0
. . . 1
. 1 0 0
. . . 1
. . 1 0
Stop at the first 1. Copy that 1 as well.
Negate these numbers stored in
2’s complement representation

## Slide 182
0 1 0 1
1 1 1 0
0 1 1 1
1 1 0 0
1 0 1 1
0 1 0 0
1 0 0 1
0 0 1 0
Invert all remaining bits.
Negate these numbers stored in
2’s complement representation

## Slide 183
0 1 0 1
1 1 1 0
0 1 1 1
1 1 0 0
1 0 1 1
0 1 0 0
1 0 0 1
0 0 1 0
Negate these numbers stored in
2’s complement representation
= +5
= -5
= -2
= +2
= -4
= +4
= +7
= -7

## Slide 184
The number circle for 2's complement
[ Figure 3.11a from the textbook ]

## Slide 185
The number circle for 2's complement

## Slide 186
The number circle for 2's complement
line of “symmetry”
with respect to bit inversion

## Slide 187
The number circle for 2's complement

## Slide 188
The number circle for 2's complement
invert all bits

## Slide 189
The number circle for 2's complement
add one

## Slide 190
The number circle for 2's complement

## Slide 191
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0

## Slide 192
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
invert all the bits

## Slide 193
Circuit #2 for negating a number stored in 2’s complement representation
0
1
1
0
0
1
1
0
0
0
0
0
0
0
0
0
1
1
0
1
1
0
add 1 by setting the
c0 carry input to 1

## Slide 194
The number circle for 2's complement
line of “symmetry”
with respect to bit inversion

## Slide 195
The number circle for 2's complement

## Slide 196
The number circle for 2's complement
invert all bits

## Slide 197
The number circle for 2's complement
add one

## Slide 198
The number circle for 2's complement

## Slide 199
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
invert all the bits

## Slide 200
Circuit #2 for negating a number stored in 2’s complement representation
1
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
0
0
0
add 1 by setting the
c0 carry input to 1

## Slide 201: Addition of two numbers stored in 2’s complement representation

## Slide 202: There are four cases to consider
(+5) + (+2)
(-5) + (+2)
(+5) + (-2)
(-5) + (-2)

## Slide 203: There are four cases to consider
(+5) + (+2) positive plus positive
(-5) + (+2) negative plus positive
(+5) + (-2) positive plus negative
(-5) + (-2) negative plus negative

## Slide 204
A) Example of 2’s complement addition
[ Figure 3.9 from the textbook ]
+
0 1 1 1
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
7
+
(
)
+

## Slide 205
B) Example of 2’s complement addition
+
1 1 0 1
1 0 1 1
0 0 1 0
2
+
(
)
5
–
(
)
3
–
(
)
+
[ Figure 3.9 from the textbook ]

## Slide 206
C) Example of 2’s complement addition
+
0 0 1 1
0 1 0 1
1 1 1 0
1
ignore
5
+
(
)
3
+
(
)
+
2
–
(
)
[ Figure 3.9 from the textbook ]

## Slide 207
D) Example of 2’s complement addition
+
1 0 0 1
1 0 1 1
1 1 1 0
1
ignore
5
–
(
)
7
–
(
)
+
2
–
(
)
[ Figure 3.9 from the textbook ]

## Slide 209: Naming Ambiguity: 2's Complement
2's complement has two different meanings:
representation for signed integer numbers
algorithm for computing the 2's complement (regardless of the representation of the number)

## Slide 210: Naming Ambiguity: 2's Complement
2's complement has two different meanings:
representation for signed integer numbers
in 2's complement
algorithm for computing the 2's complement (regardless of the representation of the number)
take the 2's complement (or negate)

## Slide 211: Subtraction of two numbers stored in 2’s complement representation

## Slide 212: There are four cases to consider
(+5) - (+2)
(-5) - (+2)
(+5) - (-2)
(-5) - (-2)

## Slide 213: There are four cases to consider
(+5) - (+2) positive minus positive
(-5) - (+2) negative minus positive
(+5) - (-2) positive minus negative
(-5) - (-2) negative minus negative

## Slide 214: There are four cases to consider
(+5) - (+2)
(-5) - (+2)
(+5) - (-2)
(-5) - (-2)

## Slide 215: There are four cases to consider
(+5) - (+2) = (+5) + (-2)
(-5) - (+2) = (-5) + (-2)
(+5) - (-2) = (+5) + (+2)
(-5) - (-2) = (-5) + (+2)

## Slide 216: There are four cases to consider
(+5) - (+2) = (+5) + (-2)
(-5) - (+2) = (-5) + (-2)
(+5) - (-2) = (+5) + (+2)
(-5) - (-2) = (-5) + (+2)
We can change subtraction into addition ...

## Slide 217: There are four cases to consider
(+5) - (+2) = (+5) + (-2)
(-5) - (+2) = (-5) + (-2)
(+5) - (-2) = (+5) + (+2)
(-5) - (-2) = (-5) + (+2)
… if we negate the second number.

## Slide 218: There are four cases to consider
(+5) - (+2) = (+5) + (-2)
(-5) - (+2) = (-5) + (-2)
(+5) - (-2) = (+5) + (+2)
(-5) - (-2) = (-5) + (+2)
These are the four addition cases
(arranged in a shuffled order)

## Slide 219
Example of 2’s complement subtraction
–
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
3
+
(
)
–
1
ignore
+
0 0 1 1
0 1 0 1
1 1 1 0
[ Figure 3.10 from the textbook ]
means take the 2's complement (or negate)

## Slide 220
Example of 2’s complement subtraction
–
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
3
+
(
)
–
1
ignore
+
0 0 1 1
0 1 0 1
1 1 1 0
[ Figure 3.10 from the textbook ]
means take the 2's complement (or negate)
Notice that the minus changes to a plus.

## Slide 221
Example of 2’s complement subtraction
–
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
3
+
(
)
–
1
ignore
+
0 0 1 1
0 1 0 1
1 1 1 0
[ Figure 3.10 from the textbook ]

## Slide 222
Example of 2’s complement subtraction
–
0 1 0 1
0 0 1 0
5
+
(
)
2
+
(
)
3
+
(
)
–
1
ignore
+
0 0 1 1
0 1 0 1
1 1 1 0
[ Figure 3.10 from the textbook ]

## Slide 223
[ Figure 3.11 from the textbook ]
Graphical interpretation of four-bit
2’s complement numbers

## Slide 224
Example of 2’s complement subtraction
[ Figure 3.10 from the textbook ]
–
1 0 1 1
0 0 1 0
–
1
ignore
+
1 0 0 1
1 0 1 1
1 1 1 0
5
–
(
)
7
–
(
)
2
+
(
)

## Slide 225
Example of 2’s complement subtraction
–
0 1 0 1
1 1 1 0
5
+
(
)
7
+
(
)
–
+
0 1 1 1
0 1 0 1
0 0 1 0
2
–
(
)
[ Figure 3.10 from the textbook ]

## Slide 226
Example of 2’s complement subtraction
–
1 0 1 1
1 1 1 0
–
+
1 1 0 1
1 0 1 1
0 0 1 0
2
–
(
)
5
–
(
)
3
–
(
)
[ Figure 3.10 from the textbook ]

## Slide 227
decimal | b3 b2 b1 b0 | take the 2's complement | b3 b2 b1 b0 | decimal
+7 | 0111 |  | 1001 | -7
+6 | 0110 |  | 1010 | -6
+5 | 0101 |  | 1011 | -5
+4 | 0100 |  | 1100 | -4
+3 | 0011 |  | 1101 | -3
+2 | 0010 |  | 1110 | -2
+1 | 0001 |  | 1111 | -1
+0 | 0000 |  | 0000 | +0
-8 | 1000 |  | 1000 | -8
-7 | 1001 |  | 0111 | +7
-6 | 1010 |  | 0110 | +6
-5 | 1011 |  | 0101 | +5
-4 | 1100 |  | 0100 | +4
-3 | 1101 |  | 0011 | +3
-2 | 1110 |  | 0010 | +2
-1 | 1111 |  | 0001 | +1
Taking the 2’s complement negates the number

## Slide 228
decimal | b3 b2 b1 b0 | take the 2's complement | b3 b2 b1 b0 | decimal
+7 | 0111 |  | 1001 | -7
+6 | 0110 |  | 1010 | -6
+5 | 0101 |  | 1011 | -5
+4 | 0100 |  | 1100 | -4
+3 | 0011 |  | 1101 | -3
+2 | 0010 |  | 1110 | -2
+1 | 0001 |  | 1111 | -1
+0 | 0000 |  | 0000 | +0
-8 | 1000 |  | 1000 | -8
-7 | 1001 |  | 0111 | +7
-6 | 1010 |  | 0110 | +6
-5 | 1011 |  | 0101 | +5
-4 | 1100 |  | 0100 | +4
-3 | 1101 |  | 0011 | +3
-2 | 1110 |  | 0010 | +2
-1 | 1111 |  | 0001 | +1
Taking the 2’s complement negates the number
This is an
exception

## Slide 229
decimal | b3 b2 b1 b0 | take the 2's complement | b3 b2 b1 b0 | decimal
+7 | 0111 |  | 1001 | -7
+6 | 0110 |  | 1010 | -6
+5 | 0101 |  | 1011 | -5
+4 | 0100 |  | 1100 | -4
+3 | 0011 |  | 1101 | -3
+2 | 0010 |  | 1110 | -2
+1 | 0001 |  | 1111 | -1
+0 | 0000 |  | 0000 | +0
-8 | 1000 |  | 1000 | -8
-7 | 1001 |  | 0111 | +7
-6 | 1010 |  | 0110 | +6
-5 | 1011 |  | 0101 | +5
-4 | 1100 |  | 0100 | +4
-3 | 1101 |  | 0011 | +3
-2 | 1110 |  | 0010 | +2
-1 | 1111 |  | 0001 | +1
Taking the 2’s complement negates the number
And this
one too.

## Slide 230
–
1 0 1 1
1 0 0 0
–
+
1 0 0 1 1
1 0 1 1
1 0 0 0
8
–
(
)
5
–
(
)
3
+
(
)
ignore
But that exception does not matter

## Slide 231
But that exception does not matter
Add 8

## Slide 232
Subtract 8
But that exception does not matter

## Slide 233: Take-Home Message

## Slide 234: Take-Home Message
Subtraction can be performed by simply negating the second number and adding it to the first, regardless of the signs of the two numbers.
Thus, the same adder circuit can be used to perform both addition and subtraction !!!

## Slide 235
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Adder/subtractor unit

## Slide 236
XOR Tricks
y
control
out

## Slide 237
y
0
y
XOR as a repeater

## Slide 238
y
y
XOR as a repeater

## Slide 239
y
1
y
XOR as an inverter

## Slide 240
y
XOR as an inverter
y

## Slide 241
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Addition: when control = 0

## Slide 242
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Addition: when control = 0
0
0
0
0

## Slide 243
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Addition: when control = 0
0
0
0
0
yn-1
y1
y0
…

## Slide 244
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Subtraction: when control = 1

## Slide 245
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Subtraction: when control = 1
1
1
1
1

## Slide 246
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Subtraction: when control = 1
1
1
1
1
yn-1
y1
y0
…

## Slide 247
s
0
s
1
s
n
1
–
x
0
x
1
x
n
1
–
c
n
n
-bit adder
y
0
y
1
y
n
1
–
c
0
Add
¤
Sub
control
[ Figure 3.12 from the textbook ]
Subtraction: when control = 1
1
1
1
1
yn-1
y1
y0
…
1
carry for the
first column!

## Slide 248: Addition Examples: all inputs and outputs are given in 2’s complement representation

## Slide 249: Addition: 5 + 6 = 11
0
1
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
0
0
1
1
0
0
0
1
0
1

## Slide 250: Addition: 5 + 6 = 11
0
1
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
0
0
1
1
0
0
0
1
0
1

## Slide 251: Addition: 5 + 6 = 11
0
1
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
0
0
1
1
0
0
0
1
0
1

## Slide 252: Addition: 5 + 6 = 11
0
1
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
0
0
1
1
0
0
0
1
0
1
0
0
1
1
0

## Slide 253: Addition: 5 + 6 = 11
0
1
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
0
0
1
1
0
0
0
1
0
1
0
0
1
1
0
0
0 0 1 0 1
0 0 1 1 0
0 0 1 0 1 1
+

## Slide 255: Addition: 4 + (-7) = -3
1
1
1
0
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
1
1
0
0
1
0
0
1
0
0

## Slide 256: Addition: 4 + (-7) = -3
1
1
1
0
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
1
1
0
0
1
0
0
1
0
0
1
1
0
0
1

## Slide 257: Addition: 4 + (-7) = -3
1
1
1
0
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
0
0
1
1
0
0
1
0
0
1
0
0
1
1
0
0
1
0
0 0 1 0 0
1 1 0 0 1
0 1 1 1 0 1
+

## Slide 258: Subtraction Examples: all inputs and outputs are given in 2’s complement representation

## Slide 259: Subtraction: 7 - 3 = 4
0
0
1
0
0
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
0
0
0
1
1
0
0
1
1
1

## Slide 260: Subtraction: 7 - 3 = 4
0
0
1
0
0
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
0
0
0
1
1
0
0
1
1
1

## Slide 261: Subtraction: 7 - 3 = 4
0
0
1
0
0
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
0
0
0
1
1
0
0
1
1
1
1
1
1
0
0

## Slide 262: Subtraction: 7 - 3 = 4
0
0
1
0
0
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
0
0
0
1
1
0
0
1
1
1
1
1
1
0
0
1
0 0 1 1 1
1 1 1 0 0
1 0 0 1 0 0
+

## Slide 263: Subtraction: 7 - 3 = 4
0
0
1
0
0
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
0
0
0
1
1
0
0
1
1
1
1
1
1
0
0
1
0 0 1 1 1
1 1 1 0 0
1 0 0 1 0 0
+
Ignore
Ignore

## Slide 265: Subtraction: (–2) – (–5) = 3
0
0
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
1
1
0
1
1
1
1
1
1
0

## Slide 266: Subtraction: (–2) – (–5) = 3
0
0
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
1
1
0
1
1
1
1
1
1
0
0
0
1
0
0

## Slide 267: Subtraction: (–2) – (–5) = 3
0
0
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
1
1
0
1
1
1
1
1
1
0
0
0
1
0
0
1
1 1 1 1 0
0 0 1 0 0
1 0 0 0 1 1
+

## Slide 268: Subtraction: (–2) – (–5) = 3
0
0
0
1
1
x
0
c
5
5-bit adder
c
0
x
1
x
2
x
3
x
4
y
0
y
1
y
2
y
3
y
4
S
0
S
1
S
2
S
3
S
4
1
1
1
1
0
1
1
1
1
1
1
0
0
0
1
0
0
1
1 1 1 1 0
0 0 1 0 0
1 0 0 0 1 1
+
Ignore
Ignore

## Slide 269: Detecting Overflow

## Slide 270
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
[ Figure 3.13 from the textbook ]

## Slide 271
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
Include the carry bits: c4 c3 c2 c1 c0

## Slide 272
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
Include the carry bits: c4 c3 c2 c1 c0

## Slide 273
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
Include the carry bits: c4 c3 c2 c1 c0
c
4
0
=
c
3
1
=
c
4
1
=
c
3
1
=
c
4
0
=
c
3
0
=
c
4
1
=
c
3
0
=

## Slide 274
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
Overflow occurs only in these two cases.
c
4
0
=
c
3
1
=
c
4
1
=
c
3
1
=
c
4
0
=
c
3
0
=
c
4
1
=
c
3
0
=

## Slide 275
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
c
4
0
=
c
3
1
=
c
4
1
=
c
3
1
=
c
4
0
=
c
3
0
=
c
4
1
=
c
3
0
=
Overflow = c3c4 + c3c4

## Slide 276
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
0 1 1 0 0
0 0 0 0 0
1 0 0 0 0
1 1 1 0 0
c
4
0
=
c
3
1
=
c
4
1
=
c
3
1
=
c
4
0
=
c
3
0
=
c
4
1
=
c
3
0
=
Overflow = c3c4 + c3c4
XOR

## Slide 277
Calculating overflow for 4-bit numbers
with only three significant bits

## Slide 278
Calculating overflow for n-bit numbers
with only n-1 significant bits

## Slide 279
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
Detecting Overflow
-

## Slide 280
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
Detecting Overflow
(with one extra XOR)
overflow
-

## Slide 281
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
Detecting Overflow
(with one extra XOR)
overflow
-
This method detects overflow
for both addition and subtraction.

## Slide 282: Detecting Overflow (alternative method)

## Slide 283: Detecting Overflow (alternative method)
Used if you don’t have access to the internal carries of the adder.

## Slide 284
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
Detecting Overflow
(with one extra XOR)
overflow
-
If the adder is implemented on a chip,
then this line is not available.
So, the first method can’t be used.

## Slide 285
X= x3 x2 x1 x0
Y= y3 y2 y1 y0
S= s3 s2 s1 s0
+
Another way to look at the overflow issue

## Slide 286
X= x3 x2 x1 x0
Y= y3 y2 y1 y0
S= s3 s2 s1 s0
+
Another way to look at the overflow issue
If both numbers that we are adding have the same sign
but the sum does not, then we have an overflow.

## Slide 287
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow

## Slide 288
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow

## Slide 289
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
x
3
0
=
y
3
0
=
s
3
1
=
x
3
0
=
y
3
1
=
s
3
0
=
x
3
1
=
y
3
0
=
s
3
1
=
x
3
1
=
y
3
1
=
s
3
0
=

## Slide 290
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
x
3
0
=
y
3
0
=
s
3
1
=
x
3
0
=
y
3
1
=
s
3
0
=
x
3
1
=
y
3
0
=
s
3
1
=
x
3
1
=
y
3
1
=
s
3
0
=
In 2's complement, both +9 and -9 are not representable with 4 bits.

## Slide 291
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
x
3
0
=
y
3
0
=
s
3
1
=
x
3
0
=
y
3
1
=
s
3
0
=
x
3
1
=
y
3
0
=
s
3
1
=
x
3
1
=
y
3
1
=
s
3
0
=
Overflow occurs only in these two cases.

## Slide 292
+
+
1 0 1 1
1 0 0 1
0 0 1 0
1 0 0 1
0 1 1 1
0 0 1 0
7
+
(
)
2
+
(
)
9
+
(
)
+
+
+
0 1 1 1
1 0 0 1
1 1 1 0
0 1 0 1
0 1 1 1
1 1 1 0
7
+
(
)
5
+
(
)
+
2
–
(
)
1
1
2
+
(
)
7
–
(
)
5
–
(
)
+
7
–
(
)
9
–
(
)
+
2
–
(
)
Examples of determination of overflow
x
3
0
=
y
3
0
=
s
3
1
=
x
3
0
=
y
3
1
=
s
3
0
=
x
3
1
=
y
3
0
=
s
3
1
=
x
3
1
=
y
3
1
=
s
3
0
=
Overflow = x3 y3 s3 + x3 y3 s3

## Slide 293
X= x3 x2 x1 x0
Y= y3 y2 y1 y0
S= s3 s2 s1 s0
+
Another way to look at the overflow issue
If both numbers that we are adding have the same sign
but the sum does not, then we have an overflow.
Overflow = x3 y3 s3 + x3 y3 s3

## Slide 294: Overflow Detection
x
0
c
4
4-bit adder
c
0
x
1
x
2
x
3
y
0
y
1
y
2
y
3
S
0
S
1
S
2
S
3
Add
¤
Sub
control

## Slide 295: Overflow Detection
x
0
c
4
4-bit adder
c
0
x
1
x
2
x
3
y
0
y
1
y
2
y
3
S
0
S
1
S
2
S
3
overflow
Add
¤
Sub
control
x3 y3 s3 + x3 y3 s3

## Slide 296: Overflow Detection
x
0
c
4
4-bit adder
c
0
x
1
x
2
x
3
y
0
y
1
y
2
y
3
S
0
S
1
S
2
S
3
overflow
Add
¤
Sub
control
This must be taken after the XOR!

## Slide 297: Overflow Detection
x
0
c
4
4-bit adder
c
0
x
1
x
2
x
3
y
0
y
1
y
2
y
3
S
0
S
1
S
2
S
3
overflow
Add
¤
Sub
control
This method also detects overflow
for both addition and subtraction.

## Slide 298: Questions?

## Slide 299: THE END

## Slide 300: Additional Material

## Slide 301: Alternative Circuit #3 (not used in practice)

## Slide 302: Alternative Circuit #3 (not used in practice)
A former student came up with this
circuit during a midterm exam!

## Slide 303
Circuit #3 for negating a number stored in 2’s complement representation
0
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
0
0
1
1
0
1
0
1
1
0

## Slide 304
Circuit #3 for negating a number stored in 2’s complement representation
0
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
0
0
1
1
0
1
0
1
1
0
-1 =
(in 2’s complement)

## Slide 305
Circuit #3 for negating a number stored in 2’s complement representation
0
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
0
0
1
1
0
1
0
1
1
0
= +5
(in 2’s complement)

## Slide 306
Circuit #3 for negating a number stored in 2’s complement representation
0
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
0
0
1
1
0
1
0
1
1
0
c0 carry is now
always set to 0

## Slide 307
Circuit #3 for negating a number stored in 2’s complement representation
0
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
0
0
1
1
0
1
0
1
1
0
invert all sum bits

## Slide 308
Circuit #3 for negating a number stored in 2’s complement representation
0
1
1
1
1
1
1
1
1
1
0
1
0
0
1
1
0
0
1
1
0
1
0
1
1
0
= -5
(in 2’s complement)

## Slide 309
The number circle for 2's complement

## Slide 310
The number circle for 2's complement
First,
add (-1) …

## Slide 311
The number circle for 2's complement

## Slide 312
The number circle for 2's complement
Then, invert all bits …

## Slide 313
The number circle for 2's complement

## Slide 314
Circuit #3 for negating a number stored in 2’s complement representation
1
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
0
0
0
0
1
0
1
0
0
1

## Slide 315
Circuit #3 for negating a number stored in 2’s complement representation
1
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
0
0
0
0
1
0
1
0
0
1
-1 =
(in 2’s complement)

## Slide 316
Circuit #3 for negating a number stored in 2’s complement representation
1
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
0
0
0
0
1
0
1
0
0
1
= -4
(in 2’s complement)

## Slide 317
Circuit #3 for negating a number stored in 2’s complement representation
1
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
0
0
0
0
1
0
1
0
0
1
= +4
(in 2’s complement)

## Slide 318
The number circle for 2's complement

## Slide 319
The number circle for 2's complement
First,
add (-1) …

## Slide 320
The number circle for 2's complement
Then, invert all bits …

## Slide 321
The number circle for 2's complement