## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Multiplication
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
No HW is due today
HW 6 will be due on Monday Oct. 14.
Posted on the class web page.

## Slide 4: Administrative Stuff
Labs this week
Mini-Project
This is worth 3% of your grade (x2 labs)
https://www.ece.iastate.edu/~alexs/classes/ 2024_Fall_2810/labs/Project-Mini/

## Slide 5: Quick Review

## Slide 6: A ripple-carry adder

## Slide 7
FA
x
n –
1
c
n
c
n
1
y
n
1
–
s
n
1
–
FA
x
1
c
2
y
1
s
1
FA
c
1
x
0
y
0
s
0
c
0
How long does it take to compute all sum bits and all carry bits?
–
It takes 2n gate delays using a ripple-carry adder?

## Slide 8
Delays through the Full-Adder circuit
[ Figure 3.3c from the textbook ]
2 gate delays in total

## Slide 9
The Full-Adder Circuit
[ Figure 3.3c from the textbook ]

## Slide 10
The Full-Adder Circuit
[ Figure 3.3c from the textbook ]
Let's take a closer look at this.

## Slide 11
yi
xi
ci
ci+1 = xi yi + (xi + yi )ci
Another Way to Draw the Full-Adder Circuit

## Slide 12
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci

## Slide 13
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci

## Slide 14
Decomposing the Carry Expression
yi
xi
ci+1
ci
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci

## Slide 15
Another Way to Draw the Full-Adder Circuit
yi
xi
ci
ci+1
si
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci

## Slide 16
Another Way to Draw the Full-Adder Circuit
yi
xi
ci
ci+1
si
ci+1 = xi yi + (xi + yi )ci

## Slide 17
Another Way to Draw the Full-Adder Circuit
ci+1 = xi yi + (xi + yi )ci
yi
xi
ci
ci+1
si
gi
pi

## Slide 18
Another Way to Draw the Full-Adder Circuit
ci+1 = xi yi + (xi + yi )ci
yi
xi
ci
ci+1
si
gi
pi
gi
pi

## Slide 19
Yet Another Way to Draw It (Just Rotate It)
ci
ci+1
si
xi
yi
pi
gi

## Slide 20
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
Now we can Build a Ripple-Carry Adder
[ Figure 3.14 from the textbook ]

## Slide 21
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
Now we can Build a Ripple-Carry Adder
[ Figure 3.14 from the textbook ]

## Slide 22
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
The delay is 5 gates (1+2+2)

## Slide 23
x
1
y
1
g
1
p
1
s
1
Stage 1
x
0
y
0
g
0
p
0
s
0
Stage 0
c
0
c
1
c
2
n-bit ripple-carry adder: 2n+1 gate delays
. . .

## Slide 24
Decomposing the Carry Expression
ci+1 = xi yi + xi ci + yi ci
ci+1 = xi yi + (xi + yi )ci
gi
pi
ci+1 = gi + pi ci
ci+1 = gi + pi (gi-1 + pi-1 ci-1 )
= gi + pi gi-1 + pi pi-1 ci-1

## Slide 25
Carry for the first two stages
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0

## Slide 26
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
The first two stages of a carry-lookahead adder
[ Figure 3.15 from the textbook ]

## Slide 27
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
It takes 3 gate delays to generate c1

## Slide 28
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
It takes 3 gate delays to generate c2

## Slide 29
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
x
0
y
0
c
0
c
1
g
0
p
0
The first two stages of a carry-lookahead adder
2
c

## Slide 30
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
x
0
y
0
c
0
c
1
g
0
p
0
It takes 4 gate delays to generate s1
2
c

## Slide 31
It takes 4 gate delays to generate s2
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
s
2

## Slide 32: N-bit Carry-Lookahead Adder
It takes 3 gate delays to generate all carry signals
It takes 1 more gate delay to generate all sum bits
Thus, the total delay through an n-bit carry-lookahead adder is only 4 gate delays!

## Slide 33
Expanding the Carry Expression
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0
ci+1 = gi + pi ci
c3 = g2 + p2g1 + p2p1g0 + p2p1p0c0
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
. . .

## Slide 34
Expanding the Carry Expression
c1 = g0 + p0 c0
c2 = g1 + p1g0 + p1p0c0
ci+1 = gi + pi ci
c3 = g2 + p2g1 + p2p1g0 + p2p1p0c0
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
. . .
Even this takes
only 3 gate delays

## Slide 35
Block
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
3
Block
1
Block
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
x
23
16
–
y
23
16
–
s
23
16
–
Block
2

## Slide 36
Block
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
3
Block
1
Block
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
x
23
16
–
y
23
16
–
s
23
16
–
Block
2

## Slide 37
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
x
23
16
–
y
23
16
–
s
23
16
–

## Slide 38
Block
x
31
24
–
c
32
c
24
y
31
24
–
s
31
24
–
x
15
8
–
c
16
y
15
8
–
s
15
8
–
c
8
x
7
0
–
y
7
0
–
s
7
0
–
c
0
3
Block
1
Block
0
A hierarchical carry-lookahead adder with
ripple-carry between blocks
[ Figure 3.16 from the textbook ]

## Slide 39
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
[ Figure 3.17 from the textbook ]
A hierarchical carry-lookahead adder

## Slide 40
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
A hierarchical carry-lookahead adder
c
32

## Slide 41
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
A hierarchical carry-lookahead adder
c
32

## Slide 42
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
A hierarchical carry-lookahead adder
?
?
?
c
32

## Slide 43
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0

## Slide 44
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0

## Slide 45
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
G0
P0

## Slide 46
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
G0
P0
c8 = G0 + P0 c0

## Slide 47
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
c16 = g15 + p15g14 + p15p14g13 + p15p14p13g12
+ p15p14p13p12g11 + p15p14p13p12p11g10
+ p15p14p13p12p11p10g9+ p15p14p13p12p11p10p9g8
+ p15p14p13p12p11p10p9p8c8

## Slide 48
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
c16 = g15 + p15g14 + p15p14g13 + p15p14p13g12
+ p15p14p13p12g11 + p15p14p13p12p11g10
+ p15p14p13p12p11p10g9+ p15p14p13p12p11p10p9g8
+ p15p14p13p12p11p10p9p8c8
The same expression, just add 8 to all subscripts

## Slide 49
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
c16 = g15 + p15g14 + p15p14g13 + p15p14p13g12
+ p15p14p13p12g11 + p15p14p13p12p11g10
+ p15p14p13p12p11p10g9+ p15p14p13p12p11p10p9g8
+ p15p14p13p12p11p10p9p8c8
G0
P0
2-gate delays
3-gate delays

## Slide 50
The Hierarchical Carry Expression
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4
+ p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1+ p7p6p5p4p3p2p1g0
+ p7p6p5p4p3p2p1p0c0
c16 = g15 + p15g14 + p15p14g13 + p15p14p13g12
+ p15p14p13p12g11 + p15p14p13p12p11g10
+ p15p14p13p12p11p10g9+ p15p14p13p12p11p10p9g8
+ p15p14p13p12p11p10p9p8c8
G1
P1
2-gate delays
3-gate delays

## Slide 51
The Hierarchical Carry Expression
c8 = G0 + P0 c0
c16 = G1 + P1 c8
= G1 + P1 G0 + P1 P0 c0
c24 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 c0
c32 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0+ P3 P2 P1 P0 c0

## Slide 52
The Hierarchical Carry Expression
c8 = G0 + P0 c0
c16 = G1 + P1 c8
= G1 + P1 G0 + P1 P0 c0
c24 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 c0
c32 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0+ P3 P2 P1 P0 c0
4-gate delays
5-gate delays
5-gate delays
5-gate delays

## Slide 53
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
[ Figure 3.17 from the textbook ]
A hierarchical carry-lookahead adder

## Slide 54
Block
x
15
8
–
y
15
8
–
x
7
0
–
y
7
0
–
3
Block
1
Block
0
Second-level lookahead
c
0
s
7
0
–
P
0
G
0
P
1
G
1
P
3
G
3
s
15
8
–
s
31
24
–
c
8
c
16
c
32
x
31
24
–
y
31
24
–
c
24
[ Figure 3.17 from the textbook ]
A hierarchical carry-lookahead adder
c8 = G0 + P0 c0
c16 = G1 + P1 G0 + P1 P0 c0
c32 =G3+P3G2+P3P2G1 +P3 P2 P1 G0+P3 P2 P1 P0 c0

## Slide 55: Total Gate Delay Through a Hierarchical Carry-Lookahead Adder
The total delay is 8 gates:
  3 to generate all Gi and Pi signals
  +2 to generate c8, c16, c24, and c32
  +2 to generate internal carries in the blocks
  +1 to generate the sum bits (one extra XOR)

## Slide 56: Total Gate Delay Through a Hierarchical Carry-Lookahead Adder
The total delay is 8 gates:
  3 to generate all Gi and Pi signals
  +2 to generate c8, c16, c24, and c32
  +2 to generate internal carries in the blocks
  +1 to generate the sum bits (one extra XOR)

## Slide 57
x
1
y
1
g
1
p
1
s
1
x
0
y
0
s
0
c
2
x
0
y
0
c
0
c
1
g
0
p
0
c1 = g0 + p0 c0
2 more gate delays for the internal carries within a block

## Slide 58
x
9
y
9
g
9
p
9
s
1
x
0
y
0
s
0
c
10
x
8
y
8
c
8
c
9
g
8
p
8
c9 = g8 + p8 c8
2 more gate delays for the internal carries within a block

## Slide 59: Hierarchical CLA Adder Carry Logic
C8 – 4 gate delays C16 – 5 gate delays C24 – 5 Gate delays C32 – 5 Gate delays
c8
c16

## Slide 60: Hierarchical CLA Critical Path
C1 - 3 gate delays
C9 – 6 gate delays C17 – 7 gate delays C25 – 7 Gate delays
c17
c9
c1
c8
c16

## Slide 61: Total Gate Delay Through a Hierarchical Carry-Lookahead Adder
The total delay is 8 gates:
  3 to generate all Gi and Pi signals
  +2 to generate c8, c16, c24, and c32
  +2 to generate internal carries in the blocks
  +1 to generate the sum bits (one extra XOR)

## Slide 62: Multiplication and division by 10 in the decimal system

## Slide 63: Decimal Multiplication by 10
What happens when we multiply a number by 10?
  4 x 10 = ?
542 x 10 = ?
1245 x 10 = ?

## Slide 64: Decimal Multiplication by 10
What happens when we multiply a number by 10?
  4 x 10 = 40
542 x 10 = 5420
1245 x 10 = 12450

## Slide 65: Decimal Multiplication by 10
What happens when we multiply a number by 10?
  4 x 10 = 40
542 x 10 = 5420
1245 x 10 = 12450
You simply add a zero as the rightmost number

## Slide 66: Decimal Division by 10
What happens when we divide a number by 10?
  14 / 10 = ?
540 / 10 = ?
1240 / 10 = ?

## Slide 67: Decimal Division by 10
What happens when we divide a number by 10?
  14 / 10 = 1 //integer division
540 / 10 = 54
1240 / 10 = 124
You simply delete the rightmost number

## Slide 68: Multiplication and division by 2 in the binary system

## Slide 69: Binary Multiplication by 2
What happens when we multiply a number by 2?
  011 times 2 = ?
101 times 2 = ?
110011 times 2 = ?

## Slide 70: Binary Multiplication by 2
What happens when we multiply a number by 2?
  011 times 2 = 0110
101 times 2 = 1010
110011 times 2 = 1100110
You simply add a zero as the rightmost number

## Slide 71: Binary Multiplication by 4
What happens when we multiply a number by 4?
  011 times 4 = ?
101 times 4 = ?
110011 times 4 = ?

## Slide 72: Binary Multiplication by 4
What happens when we multiply a number by 4?
  011 times 4 = 01100
101 times 4 = 10100
110011 times 4 = 11001100
add two zeros in the last two bits and shift everything else to the left

## Slide 73: Binary Multiplication by 2N
What happens when we multiply a number by 2N?
  011 times 2N = 01100…0 // add N zeros
  101 times 4 = 10100…0 // add N zeros
  110011 times 4 = 11001100…0 // add N zeros

## Slide 74: Binary Division by 2
What happens when we divide a number by 2?
  0110 divided by 2 = ?
1010 divides by 2 = ?
110011 divides by 2 = ?

## Slide 75: Binary Division by 2
What happens when we divide a number by 2?
  0110 divided by 2 = 011
1010 divides by 2 = 101
110011 divides by 2 = 11001
You simply delete the rightmost number

## Slide 76: Multiplication of two unsigned binary numbers

## Slide 77: Decimal Multiplication By Hand
[http://www.ducksters.com/kidsmath/long_multiplication.php]

## Slide 78: Binary Multiplication By Hand
[Figure 3.34a from the textbook]

## Slide 79: Binary Multiplication By Hand
[Figure 3.34b from the textbook]

## Slide 80: Binary Multiplication By Hand
[Figure 3.34c from the textbook]

## Slide 81
Figure 3.35. A 4x4 multiplier circuit.

## Slide 82
Figure 3.35. A 4x4 multiplier circuit.

## Slide 83: Sign Extension

## Slide 84: Sign extension for positive numbers
If we want to represent the same positive number with more bits, we simply pad it on the left with zeros.
For example:
0110 (+6 with 4-bits)
00110 (+6 with 5-bits)
000110 (+6 with 6-bits)

## Slide 85: Sign extension for negative numbers
If we want to represent the same negative number with more bits, we simply pad it on the left with ones.
For example:
1011 (-5 with 4-bits)
11011 (-5 with 5-bits)
111011 (-5 with 6-bits)

## Slide 86: Multiplication of two signed binary numbers

## Slide 87: Positive Multiplicand Example
[Figure 3.36a in the textbook]

## Slide 88: Positive Multiplicand Example
[Figure 3.36a in the textbook]
add an extra bit
to avoid overflow

## Slide 89: Negative Multiplicand Example
[Figure 3.36b in the textbook]

## Slide 90: Negative Multiplicand Example
[Figure 3.36b in the textbook]
add an extra bit
to avoid overflow
but now it is 1

## Slide 91: What if the Multiplier is Negative?
Negate both numbers.
This will make the multiplier positive.
Then proceed as normal.
This will not affect the result.
Example: 5*(- 4) = (- 5)*(4)= - 20

## Slide 92: Arithmetic Comparison Circuits

## Slide 93
Truth table for a one-bit digital comparator
[http://en.wikipedia.org/wiki/Digital_comparator]

## Slide 94
[http://www.personal.psu.edu/users///c/w/cwb5096/Old%20Site/index_files/cmpenlab4.htm]
A one-bit digital comparator circuit

## Slide 95
Truth table for a two-bit digital comparator
[http://en.wikipedia.org/wiki/Digital_comparator]

## Slide 96
[http://forum.allaboutcircuits.com/showthread.php?t=10561]
A two-bit digital comparator circuit

## Slide 97
[ Figure 4.22 from the textbook ]
A four-bit comparator circuit

## Slide 98
[ Figure 3.45 from the textbook ]
Another four-bit comparator circuit

## Slide 99
[ Figure 3.45 from the textbook ]
Another four-bit comparator circuit

## Slide 100
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
Compare 6 with 5 by subtraction (6-5).

## Slide 101
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0

## Slide 102
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
0 1 1 0
1 0 1 0
1 0 0 0 1
+
1

## Slide 103
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
0 1 1 0
1 0 1 0
1 0 0 0 1
+
1
Ignore

## Slide 104
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
1
. . . 1
0 1 1 0
1 0 1 0
1 0 0 0 1
+

## Slide 105
Another four-bit comparator circuit
0
0
1
1
1
0
0
1
0
1
1
0
1
1
0
0
0
0
0
1
1
1
1
0
0
0
0
1
. . . 1
0 1 1 0
1 0 1 0
1 0 0 0 1
+

## Slide 106: Binary Coded Decimal (BCD)

## Slide 107
Table of Binary-Coded Decimal Digits

## Slide 108: Addition of BCD digits
[Figure 3.38a in the textbook]

## Slide 109: Addition of BCD digits
[Figure 3.38a in the textbook]
The result is greater than 9, which is not a valid BCD number

## Slide 110: Addition of BCD digits
[Figure 3.38a in the textbook]
add 6

## Slide 111: Addition of BCD digits
[Figure 3.38b in the textbook]

## Slide 112: Addition of BCD digits
[Figure 3.38b in the textbook]
The result is 1, but it should be 7

## Slide 113: Addition of BCD digits
[Figure 3.38b in the textbook]
add 6

## Slide 114: Why add 6?
Think of BCD addition as a mod 16 operation
Decimal addition is mod 10 operation

## Slide 115: BCD Arithmetic Rules
Z = X + Y
If Z <= 9, then S=Z and carry-out = 0
If Z > 9, then S=Z+6 and carry-out =1

## Slide 116
Block diagram for a one-digit BCD adder
[Figure 3.39 in the textbook]

## Slide 117: How to check if the number is > 9?
7 - 0111
8 - 1000
9 - 1001
10 - 1010
11 - 1011
12 - 1100
13 - 1101
14 - 1110
15 - 1111

## Slide 118
x1 | x2 | x3 | x4 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
A four-variable Karnaugh map
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 119
z3 | z2 | z1 | z0 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
How to check if the number is > 9?
z
3
z
2
z
1
z
0
0
00
01
11
10
0
1
0
0
0
1
0
0
0
1
1
0
0
1
1
00
01
11
10
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 120
z3 | z2 | z1 | z0 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
How to check if the number is > 9?
z
3
z
2
z
1
z
0
0
00
01
11
10
0
1
0
0
0
1
0
0
0
1
1
0
0
1
1
00
01
11
10
f = z3z2 + z3z1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 121
z3 | z2 | z1 | z0 | 
0 | 0 | 0 | 0 | m0
0 | 0 | 0 | 1 | m1
0 | 0 | 1 | 0 | m2
0 | 0 | 1 | 1 | m3
0 | 1 | 0 | 0 | m4
0 | 1 | 0 | 1 | m5
0 | 1 | 1 | 0 | m6
0 | 1 | 1 | 1 | m7
1 | 0 | 0 | 0 | m8
1 | 0 | 0 | 1 | m9
1 | 0 | 1 | 0 | m10
1 | 0 | 1 | 1 | m11
1 | 1 | 0 | 0 | m12
1 | 1 | 0 | 1 | m13
1 | 1 | 1 | 0 | m14
1 | 1 | 1 | 1 | m15
How to check if the number is > 9?
z
3
z
2
z
1
z
0
0
00
01
11
10
0
1
0
0
0
1
0
0
0
1
1
0
0
1
1
00
01
11
10
f = z3z2 + z3z1
In addition, also check if there was a carry
f = carry-out + z3z2 + z3z1
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1

## Slide 122
module
bcdadd(Cin,
X,
Y,
S, Cout);
input
Cin;
input
[3:0] X,
Y;
output
reg [3:0] S;
output
reg Cout;
reg
[4:0] Z;
always
@ (X,
Y,
Cin)
begin
Z
=
X
+
Y
+
Cin;
if
(Z
<
10)
{Cout,
S}
=
Z;
else
{Cout,
S}
=
Z
+
6;
end
endmodule
Verilog code for a one-digit BCD adder
[Figure 3.40 in the textbook]

## Slide 123
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder

## Slide 124
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
carry-out + z3z2 + z3z1

## Slide 125
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1

## Slide 126
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1

## Slide 127
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0

## Slide 128
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
add 6
implicit 0

## Slide 129
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?

## Slide 130
c
i
x
i
y
i
c
i
1
+
s
i
Simplification of the Full-Adder
circuit when xi=0
[ Figure 3.4b from the textbook ]

## Slide 131
c
i
y
i
c
i
1
+
s
i
Simplification of the Full-Adder
circuit when xi=0
0

## Slide 132
c
i
y
i
c
i
1
+
s
i
Simplification of the Full-Adder
circuit when xi=0
0
0
0

## Slide 133
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
0

## Slide 134
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
0
y
i

## Slide 135
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i

## Slide 136
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
It reduces to a half-adder.

## Slide 137
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
c
i
1
+
s
i
But if we only need the sum bit …

## Slide 138
Simplification of the Full-Adder
circuit when xi=0
c
i
y
i
s
i
… it reduces to an XOR.

## Slide 139
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
z3 z2 z1 z0

## Slide 140
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
1 1 0
z3 z2 z1 z0
+
z3 z2 z1 z0

## Slide 141
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
1 1 0
z3 z2 z1 z0
+
implicit 0
z3 z2 z1 z0

## Slide 142
[Figure 3.41 in the textbook]
Circuit for a one-digit BCD adder
1
1
1
1
0
?
1 1 0
z3 z2 z1 z0
+
carry 3
z3
c3
z3 z2 z1 z0

## Slide 143: Questions?

## Slide 144: THE END