## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Code Converters
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW 7 is out
It is due on Monday (Oct 21) @ 10pm
We will start with Chapter 5 on Friday.

## Slide 4
Quick Review

## Slide 5: Decoders

## Slide 6: 2-to-4 Decoder (Definition)
Has two inputs: w1 and w0
Has four outputs: y0 , y1 , y2 , and y3
If w1=0 and w0=0, then the output y0 is set to 1
If w1=0 and w0=1, then the output y1 is set to 1
If w1=1 and w0=0, then the output y2 is set to 1
If w1=1 and w0=1, then the output y3 is set to 1
Only one output is set to 1. All others are set to 0.

## Slide 7: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]

## Slide 8: Truth Table and Graphical Symbol for a 2-to-4 Decoder
[ Figure 4.13a-b from the textbook ]
The outputs are “one-hot” encoded

## Slide 9: Truth Logic Circuit for a 2-to-4 Decoder
[ Figure 4.13c from the textbook ]

## Slide 10: Adding an Enable Input
[ Figure 4.13c from the textbook ]
En

## Slide 11: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]

## Slide 12: Truth Table and Graphical Symbol for a 2-to-4 Decoder with an Enable Input
[ Figure 4.14a-b from the textbook ]
x indicates that it does not matter
what the value of these variable is
for this row of the truth table

## Slide 13: Graphical Symbol for a Binary n-to-2n Decoder with an Enable Input
[ Figure 4.14d from the textbook ]
A binary decoder with n inputs has 2n outputs
The outputs of an enabled binary decoder are “one-hot” encoded,
meaning that only a single bit is set to 1, i.e., it is hot.

## Slide 14
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]

## Slide 15
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
0
0
0
0
0
0

## Slide 16
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
1
0
0
0
0
0
1
0
0
0
1
0

## Slide 17
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
1
0
0
0
0
0
0
0
1
1
0
0
1
0

## Slide 18
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
1
0
0
0
0
0
0
1
0
1
0
1
0

## Slide 19
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
1
0
0
0
0
1
1
1
0
1
0

## Slide 20
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
0
1
0
1
0
0
1
0
1

## Slide 21
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
1
0
0
0
1
1
0
1
0
1

## Slide 22
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
1
0
0
1
0
1
1
0
1

## Slide 23
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
En
A 3-to-8 decoder using two 2-to-4 decoders
[ Figure 4.15 from the textbook ]
0
0
0
0
0
0
0
1
1
1
1
1
0
1

## Slide 24
A 4-to-16 decoder built using a decoder tree
[ Figure 4.16 from the textbook ]
w
0
En
y
0
w
1
y
1
y
2
y
3
y
8
y
9
y
10
y
11
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
w
0
En
y
0
w
1
y
1
y
2
y
3
y
12
y
13
y
14
y
15
w
0
En
y
0
w
1
y
1
y
2
y
3
w
3
En
w

## Slide 25
Let’s build a
5-to-32 decoder

## Slide 26
Let’s build a
5-to-32 decoder
y0 – y15
y16 – y31
En

## Slide 27
Let’s build a
5-to-32 decoder
y0 – y15
y16 – y31
En
w4
w0
w1
w0
w1
w2
w3
w2
w3

## Slide 28: Demultiplexers

## Slide 29: 1-to-4 Demultiplexer (Definition)
Has one data input line: D
Has two output select lines: w1 and w0
Has four outputs: y0 , y1 , y2 , and y3
If w1=0 and w0=0, then the output y0 is set to D
If w1=0 and w0=1, then the output y1 is set to D
If w1=1 and w0=0, then the output y2 is set to D
If w1=1 and w0=1, then the output y3 is set to D
Only one output is set to D. All others are set to 0.

## Slide 30
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
[ Figure 4.14c from the textbook ]

## Slide 31
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
[ Figure 4.14c from the textbook ]
output
select
lines
the
four
output
lines
data
input
line
D

## Slide 32
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
0
1
0
1
0
0
0

## Slide 33
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
0
0
0
0
0
0
0

## Slide 34
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
0
1
0
1
0
0
0

## Slide 35
D
A 1-to-4 demultiplexer
built with a 2-to-4 decoder with enable
1
1
0
0
1
0
0

## Slide 36: Multiplexers (Implemented with Decoders)

## Slide 37
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1
A 4-to-1 multiplexer
built using a 2-to-4 decoder
[ Figure 4.17 from the textbook ]

## Slide 38: Encoders

## Slide 39: Binary Encoders

## Slide 40: 4-to-2 Binary Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two outputs: y1 and y0
Only one input is set to 1 (“one-hot” encoded). All others are set to 0.
If w0=1 then y1=0 and y0=0
If w1=1 then y1=0 and y0=1
If w2=1 then y1=1 and y0=0
If w3=1 then y1=1 and y0=1

## Slide 41
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Truth table for a 4-to-2 binary encoder

## Slide 42
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Truth table for a 4-to-2 binary encoder
The inputs are “one-hot” encoded

## Slide 43
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
Circuit for a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 44
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
?
Circuit for a 4-to-2 binary encoder

## Slide 45
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
It is assumed that the
inputs are one hot encoded
Circuit for a 4-to-2 binary encoder

## Slide 46
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
0
1
0
0
0
Circuit for a 4-to-2 binary encoder

## Slide 47
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
0
1
0
0
0
Circuit for a 4-to-2 binary encoder
As this level of abstraction we
need that w0 input for this to be
a proper 4-to-2 binary encoder.

## Slide 48
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
0
1
0
0
0
Circuit for a 4-to-2 binary encoder

## Slide 49
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
1
0
0
1
0
0
Circuit for a 4-to-2 binary encoder

## Slide 50
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
0
1
0
0
1
0
Circuit for a 4-to-2 binary encoder

## Slide 51
w
1
w
0
y
0
w
2
w
3
y
1
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1
[ Figure 4.19 from the textbook ]
1
1
0
0
0
1
Circuit for a 4-to-2 binary encoder

## Slide 52
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 |  | 
0 | 1 | 1 | 0 |  | 
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 0 |  | 
1 | 1 | 1 | 1 |  | 
Expressions for 4-to-2 binary encoder
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1

## Slide 53
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
0
0
1
1
1
0
1
w
3
y
1
0
y
0
0
0
1
0
w
2
0
1
0
0
w
1
1
0
0
0
w
0
0
0
0
1

## Slide 54
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
w3 w2
d
00
01
11
10
0
d
1
0
d
d
d
d
d
d
d
1
d
d
d
00
01
11
10
w1 w0
y0 = (w1 + w3)
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 55
w3 | w2 | w1 | w0 | y1 | y0
0 | 0 | 0 | 0 | d | d
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | d | d
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | d | d
0 | 1 | 1 | 0 | d | d
0 | 1 | 1 | 1 | d | d
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | d | d
1 | 0 | 1 | 0 | d | d
1 | 0 | 1 | 1 | d | d
1 | 1 | 0 | 0 | d | d
1 | 1 | 0 | 1 | d | d
1 | 1 | 1 | 0 | d | d
1 | 1 | 1 | 1 | d | d
Expressions for 4-to-2 binary encoder
w3 w2
d
00
01
11
10
1
d
1
0
d
d
d
d
d
d
d
0
d
d
d
00
01
11
10
w1 w0
y1 = (w3 + w2)
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 56
2
n
inputs
w
0
w
2
n
1
–
y
0
y
n
1
–
n
outputs
A 2n-to-n binary encoder
[ Figure 4.18 from the textbook ]

## Slide 57: Priority Encoders

## Slide 58: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 )
y1=1 and y0=0 ( if w2=1 and w3=0 )
y1=1 and y0=1 ( if w3=1 )

## Slide 59: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 ) w0
y1=1 and y0=0 ( if w2=1 and w3=0 ) w0 , w1
y1=1 and y0=1 ( if w3=1 ) w0 , w1 , w2
these have lower priorities
and can be either 0 or 1.

## Slide 60: 4-to-2 Priority Encoder (Definition)
Has four inputs: w3 , w2 , w1 , and w0
Has two primary outputs: y1 and y0
Has one other output: z
The inputs are NOT “one-hot” encoded.
More than one input can be set to 1 but they have priorities associated with them: w3 – highest priority and w0 – lowest priority.
y1=0 and y0=0 ( if w0=1 and w3=w2=w1=0 )
y1=0 and y0=1 ( if w1=1 and w3=w2=0 )
y1=1 and y0=0 ( if w2=1 and w3=0 )
y1=1 and y0=1 ( if w3=1 )
z =0 if w3=w2=w1=w0=0; otherwise z=1.

## Slide 61
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)

## Slide 62
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
[ Figure 4.20 from the textbook ]
Truth table for a 4-to-2 priority encoder
(abbreviated version)

## Slide 63
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Truth table for a 4-to-2 priority encoder
1 x x x
0 1 x x
0 0 1 x
0 0 0 1
0 0 0 0

## Slide 64
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
w3 w2
d
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0
y1 = w3 + w2

## Slide 65
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
y0 = w3 + w1 w2
w3 w2
d
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0

## Slide 66
w3 | w2 | w1 | w0 | y1 | y0 | z
0 | 0 | 0 | 0 | d | d | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Expressions for 4-to-2 priority encoder
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0
z = w3 + w2 + w1 + w0

## Slide 67
Circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0

## Slide 68
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder

## Slide 69
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1

## Slide 70
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3

## Slide 71
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
The textbook derives a different circuit for the
4-to-2 priority encoder using a 4-to-2 binary encoder
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3
Try to prove that this is equivalent to the circuit that was derived above.

## Slide 72
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for z
z z = ?
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0

## Slide 73
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for z
z z = (w0 + w1 + w2 + w3)
w3 w2
0
00
01
11
10
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
00
01
11
10
w1 w0

## Slide 74
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y0
w3 w2
0
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0
y0 = ?

## Slide 75
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y0
w3 w2
0
00
01
11
10
0
1
1
0
0
1
1
1
0
1
1
1
0
1
1
00
01
11
10
w1 w0
y0 = w3 + w1 w2

## Slide 76
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y1
z y1 = ?
w3 w2
0
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0

## Slide 77
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Let’s prove this for y1
z y1 = w3 + w2
w3 w2
0
00
01
11
10
1
1
1
0
1
1
1
0
1
1
1
0
1
1
1
00
01
11
10
w1 w0

## Slide 78
d
0
0
1
0
1
0
w
0
y
1
d
y
0
1
1
0
1
1
1
1
z
1
x
x
0
x
w
1
0
1
x
0
x
w
2
0
0
1
0
x
w
3
0
0
0
0
1
Therefore, this circuit for the
4-to-2 priority encoder is equivalent to …
w
1
w
0
y
0
w
2
w
3
y
1
i0
i1
i2
i3
z
i0 + i1 + i2 + i3

## Slide 79
… this circuit for the 4-to-2 priority encoder
w3 w2 w1 w0
z
y1
y0

## Slide 80: Code Converters

## Slide 81: Code Converter (Definition)
Converts from one type of input encoding to a different type of output encoding.

## Slide 82: Code Converter (Definition)
Converts from one type of input encoding to a different type of output encoding.
A decoder does that as well, but its outputs are always one-hot encoded so the output code is really only one type of output code.
A binary encoder does that as well but its inputs are always one-hot encoded so the input code is really only one type of input code.

## Slide 83
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 84
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 85
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 86
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 87
[ Figure 4.21 from the textbook ]
A hex-to-7-segment display code converter

## Slide 88
What is the circuit for this code converter?
x3 x2 x1 x0

## Slide 89
What is the circuit for this code converter?
x3 x2 x1 x0
f(x1, x2, x3, x4) = Σ m(0, 2, 3, 5, 6, 7, 8, 9, 10, 12, 14, 15)

## Slide 90
What is the circuit for this code converter?
1
0
0
1
1
1
1
1
1
0
1
1
1
1
0
1
x3 x2 x1 x0
f(x1, x2, x3, x4) = Σ m(0, 2, 3, 5, 6, 7, 8, 9, 10, 12, 14, 15)

## Slide 91
What is the circuit for this code converter?
x3 x2 x1 x0

## Slide 92
What is the circuit for this code converter?
1
0
0
1
1
1
0
1
1
1
1
1
0
1
1
0
x3 x2 x1 x0
f(x1, x2, x3, x4) = Σ m(0, 2, 3, 5, 6, 8, 9, 11, 12, 13, 14)

## Slide 93: Example Problems from Chapter 4

## Slide 94: Example 1: SOP vs Decoders
Implement the function
f(w1, w2, w3) = Σ m(0, 1, 3, 4, 6, 7)
by using a 3-to-8 binary decoder and one OR gate.

## Slide 95
w3
w2
w1
w2
w1
w0
1
En
y0
y1
y2
y3
y5
y4
y6
y7
[ Figure 4.44 from the textbook ]
Solution Circuit
f(w1, w2, w3) = Σ m(0, 1, 3, 4, 6, 7)

## Slide 96
w3
w2
w1
w2
w1
w0
1
En
y0
y1
y2
y3
y5
y4
y6
y7
[ Figure 4.44 from the textbook ]
Solution Circuit
f(w1, w2, w3) = Σ m(0, 1, 3, 4, 6, 7)
Notice this swap
of variables in
the two lists.
Need to match the
least significant
with the least
significant in both.

## Slide 97: Example 2: Implement an 8-to-3 binary encoder
[ Figure 4.45 from the textbook ]

## Slide 98: Example 2: Implement an 8-to-3 binary encoder
[ Figure 4.45 from the textbook ]
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 99: Example 2: Implement an 8-to-3 binary encoder
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 100: Example 2: Implement an 8-to-3 binary encoder
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 101: Example 2: Implement an 8-to-3 binary encoder
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 102
Circuit for the 8-to-3 binary encoder
w7 w6 w5 w4 w3 w2 w1 w0
y2
y1
y0
y0 = w1 + w3 + w5 + w7
y1 = w2 + w3 + w6 + w7
y2 = w4 + w5 + w6 + w7

## Slide 103: Example 3: Implement an 8-to-3 priority encoder

## Slide 104: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x

## Slide 105: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x
0 0 0 0 0 0 0 0
d d d
z
1 1 1
1
1
1
1
1
0

## Slide 106: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x
0 0 0 0 0 0 0 0
d d d
z
1 1 1
1
1
1
1
1
0

## Slide 107: Example 3: Implement an 8-to-3 priority encoder
x x x x x x x
x x x x x x
x x x x x
x x x x
x x x
x x
x
0 0 0 0 0 0 0 0
d d d
z
1 1 1
1
1
1
1
1
0
z = i0+i1+i2+i3+i4+i5+i6+i7
i0 = w7 w6 w5 w4 w3 w2 w1 w0
i1 = w7 w6 w5 w4 w3 w2 w1
i2 = w7 w6 w5 w4 w3 w2
i3 = w7 w6 w5 w4 w3
i4 = w7 w6 w5 w4
i5 = w7 w6 w5
i6 = w7 w6
i7 = w7

## Slide 108
Circuit for the 8-to-3 binary encoder
w7 w6 w5 w4 w3 w2 w1 w0
y2
y1
y0

## Slide 109
Circuit for the 8-to-3 priority encoder
w7 w6 w5 w4 w3 w2 w1 w0
y2
y1
y0
z
i7 i6 i5 i4 i3 i2 i1 i0

## Slide 110: Example 4:Circuit implementation using a multiplexer
Implement the function
f(w1, w2, w3, w4, w5) = w1w2w4w5 + w1w2 + w1w3 + w1w4 + w3w4w5
using a 4-to-1 multiplexer

## Slide 111: Some Boolean Algebra Leads To
w1w2w4w5 + w1w2 + w1w3 + w1w4 + w3w4w5
w1w4 (w5 w2) + w4 (w3w5) + w1 (w2 + w3) + w1w4 (1)
w1w4 (w5 w2) + ( w1+w1)w4 (w3w5) + w1( w4+w4) (w2 + w3) + w1w4 (1)
w1w4 (w5 w2) + w1w4 (w3w5) + w1w4 (w2 + w3) + w1w4 ( w3w5 + (w2+w3) + 1)
w1w4 (w5 w2) + w1w4 (w3w5) + w1w4 (w2 + w3) + w1w4 (1)
Note that the split is by w1 and w4, not w1 and w2

## Slide 112
[ Figure 4.46 from the textbook ]
Solution Circuit
01
00
10
11

## Slide 113
Some Final Things from Chapter 4

## Slide 114: Shifter Circuit

## Slide 115
[ Figure 4.50 from the textbook ]
Hold / Shift-Right Circuit

## Slide 116
[ Figure 4.50 from the textbook ]
Hold / Shift-Right Circuit
4-bit input
4-bit output

## Slide 117
No shift if the control signal is 0
0

## Slide 118
No shift if the control signal is 0
0

## Slide 119
No shift if the control signal is 0
0
w3
w2
w1
w0
No shift in this case.

## Slide 120
No shift if the control signal is 0
0
w3
w2
w1
w0
No shift in this case.
0

## Slide 121
Shift right if the control signal is 1
1

## Slide 122
Shift right if the control signal is 1
1

## Slide 123
Shift right if the control signal is 1
1
0
w3
w2
w1
Shift to the right by 1 bit

## Slide 124
A shifter circuit
1
0
w3
w2
w1
Shift to the right by 1 bit
w0

## Slide 125: Barrel Shifter

## Slide 126
[ Figure 4.51 from the textbook ]
A barrel shifter circuit

## Slide 127
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
0
w3
w2
w1
w0

## Slide 128
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 129
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 130
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 131
[ Figure 4.51 from the textbook ]
A barrel shifter circuit
0
1
w0
w3
w2
w1

## Slide 132
[ Figure 4.51 from the textbook ]
A barrel shifter circuit

## Slide 133: Arithmetic Logic Unit (ALU)

## Slide 134: Shifter Circuit of the i281 CPU

## Slide 135
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 136
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
Write
Select
Read
Select
Read
Select
Write
Select
Write Enable
Write Enable
Write Enable
Write Enable
Write Enable
Write
Select
Port0 Read Select
Port1 Read Select
ALU Select
PC Mux
DMEM Input Mux
REG Writeback Mux
ALU Result Mux
ALU Source Mux
Input
Input
Input

## Slide 137
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 138
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Arithmetic Logic Unit

## Slide 139: The ALU
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 140: The Shifter Circuit
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 141: The i281 CPU Shifter Circuit
Select
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 142
0
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 143
1
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 144: Shift Left
0
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 145: Shift Left
0
1 0
1
1 0
0
1 0
1
1 0
1
1 0
0
1 0
0
1 0
1
1 0
1
1 0
0
1
1
0
0
1
1
0
1
i281 CPU

## Slide 146: Shift Right
1
1 0
Shift_Out
1 0
O0
1 0
O1
1 0
O2
1 0
O3
1 0
O4
1 0
O5
1 0
O6
1 0
O7
I0
I1
I2
I3
I4
I5
I6
I7
i281 CPU

## Slide 147: Shift Right
1
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1 0
1
1
0
0
1
1
0
1
1
1
0
0
1
1
0
1
0
i281 CPU

## Slide 148: Bus Multiplexer

## Slide 149: Bus Analogy
[https://atlanta.curbed.com/2018/10/8/17949734/study-evening-rush-hour-slows-traffic-23-percent]

## Slide 150: Bus Analogy
[https://atlanta.curbed.com/2018/10/8/17949734/study-evening-rush-hour-slows-traffic-23-percent]
8-bit bus

## Slide 151: Bus Analogy
[https://atlanta.curbed.com/2018/10/8/17949734/study-evening-rush-hour-slows-traffic-23-percent]
8-bit bus
For each lane:
every car is a 1,
every gap is a 0.
A7 A6 A5 A4 A3 A2 A1 A0
Time

## Slide 152: Bus Multiplexer Analogy
[https://www.researchgate.net/figure/An-example-of-traffic-jam-around-a-junction-where-several-lanes-join_fig1_221567960 ]

## Slide 153: Bus Multiplexer Analogy
A1 A0
B1 B0
F1 F0
select

## Slide 154: Bus Multiplexer Analogy
A1 A0
B1 B0
F1 F0
select
One restriction of digital
multiplexers is that they
cannot mix bits from A and B
when outputting F. At each time
step it is only A or only B.

## Slide 155: The Internal ALU Bus Multiplexer
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 156: 2-to-1 Bus Multiplexer (with 8-bit lines)
0
1
Z7 … Z0
U7 … U0
V7 … V0
8
8
c12
8

## Slide 157
0
1
Z2
U2
V2
0
1
Z3
U3
V3
0
1
Z4
U4
V4
0
1
Z5
U5
V5
0
1
Z6
U6
V6
0
1
Z7
U7
V7
0
1
Z1
U1
V1
0
1
Z0
U0
V0
c12

## Slide 158
0
1
Z2
U2
V2
0
1
Z3
U3
V3
0
1
Z4
U4
V4
0
1
Z5
U5
V5
0
1
Z6
U6
V6
0
1
Z7
U7
V7
0
1
Z1
U1
V1
0
1
Z0
U0
V0
c12
0

## Slide 159
0
1
Z2
U2
V2
0
1
Z3
U3
V3
0
1
Z4
U4
V4
0
1
Z5
U5
V5
0
1
Z6
U6
V6
0
1
Z7
U7
V7
0
1
Z1
U1
V1
0
1
Z0
U0
V0
c12
1

## Slide 160: 2-to-1 Multiplexer
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 161: 2-to-1 Multiplexer
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 162: 2-to-1 Multiplexer
input_0
input_1
select

## Slide 163: The adder/subtractor of the i281 CPU

## Slide 164
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Arithmetic Logic Unit

## Slide 165: The Adder / Subtractor
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
i281 CPU

## Slide 166: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
add / sub
This is an 8-bit ripple-carry adder. Note that the X and Y lines are swapped.
i281 CPU

## Slide 167: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
carry
overflow
add / sub
i281 CPU

## Slide 168: The Adder / Subtractor
c8
S7
FA
c7
Y7
X7
S6
FA
c6
Y6
X6
S5
FA
c5
Y5
X5
S4
FA
c4
Y4
X4
S3
FA
c3
Y3
X3
S2
FA
c2
Y2
X2
S1
FA
c1
Y1
X1
S0
FA
c0
Y0
X0
carry
overflow
add / sub
negative
zero
negative and zero can be
computed here as well
i281 CPU

## Slide 169: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)

## Slide 170: Abbreviations for the Flags
Carry Flag (CF)
Overflow Flag (OF)
Negative Flag (NF)
Zero Flag (ZF)
In some CPU architectures the carry flag
means borrow. And it could be inverted
relative to the previous diagram.

## Slide 171: The flag calculator of the i281 CPU

## Slide 172: The ALU Flag Calculator
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8

## Slide 173: The ALU Flag Calculator
I0
I1
I2
I3
I4
I5
I6
I7
negative
zero

## Slide 174: ALU Outputs to the Flags Register
0
1
0
1
0
1
flag
calculator
8-bit adder
add / sub
carry
overflow
8-bit shifter
L / R
shift out
ALU_SELECT1
ALU_SELECT0
carry
overflow
negative
zero
ALU_RESULT
8
8
8
8
8
8
8
8
8
8
8
4 Outputs to the
Flags Register

## Slide 175: Questions?

## Slide 176: THE END