## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
T Flip-Flops
&
JK Flip-Flops
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
Homework 8 is due on Monday Oct 28 @ 10pm.
Homework 9 is due on Monday Nov 4@ 10pm.
The second midterm exam is next week (Friday Nov 1).

## Slide 4: Administrative Stuff
Midterm Exam #2
When: Friday, November 1 @ 4:20pm.
Where: This room
What: Chapters 1, 2, 3, 4 and 5
The exam will be closed book but open notes (you can bring up to 3 pages of handwritten notes).

## Slide 5: Midterm 2: Format
The exam will be out of 130 points
You need 95 points to get an A for this exam
It will be great if you can score more than 100 points.
  but you can’t roll over your extra points 

## Slide 6: Midterm 2: Topics
K-maps for 2, 3, and 4 variables
Binary Numbers and Hexadecimal Numbers
1’s complement and 2’s complement representation
Addition and subtraction of binary numbers
Circuits for adders and fast adders, delay calculation
Single and Double precision IEEE floating point formats
Converting a real number to the IEEE format
Converting a floating point number to base 10
Multiplexers (circuits and function)
Synthesis of logic functions using multiplexers
Shannon’s Expansion Theorem

## Slide 7: Midterm 2: Topics
Decoders (circuits and function)
Demultiplexers
Encoders (binary and priority)
Code Converters and Comparison Circuits
Synthesis of logic circuits using adders, multiplexers, encoders, decoders, and basic logic gates
Synthesis of logic circuits given constraints on the available building blocks that you can use
Latches (circuits, behavior, timing diagrams)
Flip-Flops (circuits, behavior, timing diagrams)
Registers and Register Files
Counters
Something from Star Wars

## Slide 8
Quick Review

## Slide 9
Gated D Latch

## Slide 10
[ Figure 5.7a from the textbook ]
Circuit Diagram for the Gated D Latch

## Slide 11
[ Figure 5.7a,c from the textbook ]
Circuit Diagram and Graphical Symbol
for the Gated D Latch

## Slide 12
Circuit Diagram for the Gated D Latch
(with the latch implemented using NORs)
[https://en.wikibooks.org/wiki/Digital_Circuits/Latches]
Clk
S
R

## Slide 13
[https://en.wikibooks.org/wiki/Digital_Circuits/Latches]
Circuit Diagram for the Gated D Latch
(with the latch implemented using NORs)
[ Figure 5.7a from the textbook ]
Clk
S
R

## Slide 14
[https://en.wikibooks.org/wiki/Digital_Circuits/Latches]
Circuit Diagram for the Gated D Latch
(with the latch implemented using NORs)
[ Figure 5.7a from the textbook ]
Clk
S
R
The NOT gate is now in a different place.
Also, S and R are swapped.

## Slide 15
Master-Slave D Flip-Flop

## Slide 16
Constructing a Master-Slave D Flip-Flop
From Two D Latches
Master
Slave

## Slide 17
Constructing a Master-Slave D Flip-Flop
From Two D Latches
Master
Slave

## Slide 18
Constructing a Master-Slave D Flip-Flop
From Two D Latches
Master
Slave

## Slide 19
Constructing a Master-Slave D Flip-Flop
From Two D Latches
[ Figure 5.9a from the textbook ]

## Slide 20
Clock is used for the D Flip-Flop
[ Figure 5.9a from the textbook ]

## Slide 21
Clock is used for the D Flip-Flop,
but Clk is used for each D Latch
[ Figure 5.9a from the textbook ]

## Slide 22
Constructing a Master-Slave D Flip-Flop
From one D Latch and one Gated SR Latch
(This version uses one less NOT gate)
Master
Slave

## Slide 23
Constructing a Master-Slave D Flip-Flop
From one D Latch and one Gated SR Latch
(This version uses one less NOT gate)
Master
Slave

## Slide 24
Edge-Triggered D Flip-Flops

## Slide 25: Motivation
In some cases, we need to use a memory storage device
that can change its state no more than once during
each clock cycle.

## Slide 26
D
Q
Q
[ Figure 5.9c from the textbook ]
Graphical Symbol for the Master-Slave D Flip-Flop

## Slide 27
D
Q
Q
[ Figure 5.9c from the textbook ]
Graphical Symbol for the Master-Slave D Flip-Flop
The > means that this is edge-triggered
The small circle means that is is the negative edge

## Slide 28
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Negative-Edge-Triggered Master-Slave D Flip-Flop
Positive-Edge-Triggered Master-Slave D Flip-Flop
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk

## Slide 29
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Negative-Edge-Triggered Master-Slave D Flip-Flop
Positive-Edge-Triggered Master-Slave D Flip-Flop
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
negative edge
(of the Clock)
positive edge
(of the Clock)

## Slide 30
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Negative-Edge-Triggered Master-Slave D Flip-Flop
Positive-Edge-Triggered Master-Slave D Flip-Flop
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
D
Q
Q
D
Q
Q

## Slide 31
Negative-Edge-Triggered Master-Slave D Flip-Flop
Positive-Edge-Triggered Master-Slave D Flip-Flop
D
Q
Q
D
Q
Q

## Slide 32
Flip-Flop Analogy
(Airlock)

## Slide 33
[https://en.wikipedia.org/wiki/Quest_Joint_Airlock]

## Slide 34
[https://www.allposters.com/-sp/Astronaut-Ingresses-the-Airlock-Hatch-on-the-International-Space-Station-Posters_i12684251_.htm]

## Slide 35
[https://www.spaceflightinsider.com/missions/iss/astronauts-install-high-definition-cameras-outside-international-space-station/]

## Slide 36
[https://en.wikipedia.org/wiki/Quest_Joint_Airlock]

## Slide 38: Airlock on Earth
[https://www.maglocks.com/sdc-two-door-airlockmantrapcleanroom-level-1-kit.html]

## Slide 39
[https://www.nortechcontrol.com/solutions/people/door-interlock/]
D Flip-Flop Analogy

## Slide 40
[https://www.insafe.com/activa-pro-interlock/]

## Slide 41
Master
Slave
D Flip-Flop Analogy

## Slide 42
D Flip-Flop:
A Double Door Analogy

## Slide 43
Positive-Edge-Triggered
Master-Slave D Flip-Flop
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
1
1
0
D

## Slide 44
Positive-Edge-Triggered
Master-Slave D Flip-Flop
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
1
1
0
D

## Slide 45
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Positive-Edge-Triggered
Master-Slave D Flip-Flop
1
1
1
D

## Slide 46
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Positive-Edge-Triggered
Master-Slave D Flip-Flop
1
1
1
D

## Slide 47
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Positive-Edge-Triggered
Master-Slave D Flip-Flop
1
1
1
D

## Slide 48
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Positive-Edge-Triggered
Master-Slave D Flip-Flop
0
0
1
D

## Slide 49
Clock
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
Clk
Clk
Positive-Edge-Triggered
Master-Slave D Flip-Flop
0
0
0
D

## Slide 50
Positive-edge-triggered D flip-flop with Clear and Preset

## Slide 51
Positive-edge-triggered D flip-flop with Clear_n and Preset_n

## Slide 52
[ Figure 5.13c from the textbook ]
Positive-edge-triggered D flip-flop
with Synchronous Clear
The output Q can be cleared only on the positive clock edge.

## Slide 53
The Complete Wiring Diagram for
a Positive-Edge-Triggered D Flip-Flop
D
Clock
Q
Q

## Slide 54
Adding an Asynchronous Clear
D
Clock
Q
Q
clear_n

## Slide 55
D
Clock
Q
Q
preset_n
Adding an Asynchronous Preset

## Slide 56
Positive-Edge-Triggered D Flip-Flop
with Asynchronous Clear and Preset
D
Clock
Q
Q
preset_n
clear_n

## Slide 57
How does clear work?

## Slide 58
How does clear work?
D
Clock
Q
Q
preset_n
clear_n

## Slide 59
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0

## Slide 60
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
1

## Slide 61
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
1
1
1
1

## Slide 62
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
1
1
1
1
1
At this point we need to consider two cases: Clock=1 v.s. Clock =0

## Slide 63
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
0
0
1
1
1
1
1
1
1
Clock=1

## Slide 64
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
0
0
1
1
1
1
1
1
1
1
1
Clock=1
0

## Slide 65
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
0
0
1
1
1
1
0
1
1
1
1
1
Clock=1
0

## Slide 66
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
0
0
1
1
1
1
0
1
1
1
1
1
1
Clock=1
0

## Slide 67
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
0
0
1
1
1
1
0
1
0
1
1
1
1
1
Clock=1
0

## Slide 68
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
1
0
0
1
1
1
1
0
1
0
1
1
1
1
1
Clock=1
0
Note that the value of D does not matter, because the outputs
of these two NAND gates can be computed without it.

## Slide 70
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0

## Slide 71
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0

## Slide 72
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D

## Slide 73
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D
D
D
_

## Slide 74
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D
_
D
D
D
_
D

## Slide 75
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D
_
D
D
D
D
_
D

## Slide 76
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D
_
D
D
1
1
D
D
_
D

## Slide 77
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D
_
D
D
1
0
1
D
D
_
D

## Slide 78
How does clear work?
D
Clock
Q
Q
preset_n
clear_n
0
0
0
1
1
0
1
1
1
1
1
Clock=0
1
1
0
0
D
_
D
D
1
0
1
Once again, the value of D does not matter, because the outputs
of these two NAND gates can be computed without it due to their zero inputs.
D
D
_
D

## Slide 79
[ Figure 5.13b from the textbook ]
Positive-edge-triggered D flip-flop
with asynchronous Clear and Preset

## Slide 80
[ Figure 5.13b from the textbook ]
For normal operation both must be set to 1
1
1

## Slide 81
[ Figure 5.13b from the textbook ]
A zero on clear_n drives the output Q to zero
0
1
0
1

## Slide 82
[ Figure 5.13b from the textbook ]
A zero on preset_n drives the output Q to one
1
0
1
0

## Slide 83
[ Figure 5.13b from the textbook ]
The output is indeterminate if both are zero
0
0
?
?
don’t ever
use this one

## Slide 84
[ Figure 5.12 from the textbook ]
Negative-Edge-Triggered D flip-flop
with asynchronous Clear and Preset

## Slide 85: Flip-Flop Timing Parameters

## Slide 86
[ Figure 5.14 from the textbook ]
Flip-Flop Timing Parameters
Setup time
Hold time
clock-to-Q
propagation delay

## Slide 87
[ Figure 5.14 from the textbook ]
Flip-Flop Timing Parameters
Setup time
Hold time
clock-to-Q
propagation delay
D should not change here

## Slide 88
An alternative D Flip-Flop Design

## Slide 89
The Complete Wiring Diagram for
a Positive-Edge-Triggered D Flip-Flop
D
Clock
Q
Q

## Slide 90
D
Clock
P4
P3
P1
P2
5
6
1
2
3
(a) Circuit
D
Q
Q
(b) Graphical symbol
Clock
Q
Q
4
[ Figure 5.11 from the textbook ]
A positive-edge-triggered D flip-flop

## Slide 91
D
Clock
P4
P3
P1
P2
5
6
1
2
3
(a) Circuit
D
Q
Q
(b) Graphical symbol
Clock
Q
Q
4
[ Figure 5.11 from the textbook ]
A positive-edge-triggered D flip-flop
This circuit behaves like a positive-edge-triggered
D flip-flop, but it uses only 6 NAND gates.
Thus, it can be implemented with fewer transistors
than the master-slave D flip-flop.

## Slide 92
[ Figure 5.13a from the textbook ]
Positive-edge-triggered D flip-flop
with asynchronous Clear and Preset

## Slide 93
T Flip-Flop

## Slide 94: Motivation
A slight modification of the D flip-flop that can be used for some nice applications (e.g., counters).
In this case, T stands for Toggle.

## Slide 95
[ Figure 5.15a from the textbook ]
T Flip-Flop

## Slide 96
[ Figure 5.15a from the textbook ]
T Flip-Flop
Positive-edge-triggered
D Flip-Flop

## Slide 97
[ Figure 5.15a from the textbook ]
T Flip-Flop
What is this?

## Slide 98
What is this?
Q
Q
T
D

## Slide 99
It is a 2-to-1 Multiplexer
Q
Q
T
D
Q
Q
T
D

## Slide 100
What is this?
+
= ?
Q
Q
T
D

## Slide 101
T
0
1
D
Q
Q
Clock
It is a T Flip-Flop

## Slide 102
T
0
1
D
Q
Q
Clock
It is a T Flip-Flop
Q
Q
Note that the two inputs to the multiplexer are inverses of each other.

## Slide 103
T
0
1
D
Q
Q
Clock
Another Way to Draw This
Q
Q

## Slide 104
T
0
1
D
Q
Q
Clock
Another Way to Draw This
Q
Q
What is this?

## Slide 105
What is this?
Q
T
D

## Slide 106
What is this?
Q
T
D
D = QT + QT

## Slide 107
It is an XOR
Q
T
D
D = Q + T

## Slide 108
D
Q
T
It is an XOR
D = Q + T

## Slide 109
What is this?
+
= ?

## Slide 110
T
D
Q
Q
Clock
It is a T Flip-Flop too

## Slide 111
T | Q | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
T
D
Q
Q
Clock
It is a T Flip-Flop too

## Slide 112
T
D
Q
Q
Clock
It is a T Flip-Flop too
T | Q | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Q
Q

## Slide 113
If T=0 then it stays in its current state.
If T=1 then it reverses its current state.
In other words, the circuit “toggles” its state
when T=1. This is why it is called T flip-flop.
T Flip-Flop (how it works)

## Slide 114
[ Figure 5.15a,b from the textbook ]
T Flip-Flop (circuit and truth table)

## Slide 115
[ Figure 5.15a,c from the textbook ]
T Flip-Flop (circuit and graphical symbol)

## Slide 116
[ Figure 5.15d from the textbook ]
T Flip-Flop (Timing Diagram)
1
1
0
0
1
1
1
0
1
1
1

## Slide 117
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
Decision Point
T Flip-Flop (Timing Diagram)
0
1
1

## Slide 118
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
Decision Point
T Flip-Flop (Timing Diagram)
0
1
1
0
1
1
0
1
0
1

## Slide 119
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
Decision Point
T Flip-Flop (Timing Diagram)
0
1
1
0
1
1
0
1
0
1
Current state
Future state

## Slide 120
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
Decision Point
T Flip-Flop (Timing Diagram)
1
0
1
0
1
0
1
0
0
0

## Slide 121
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
Decision Point
T Flip-Flop (Timing Diagram)
1
0
0
1
0
0
1
1
1
0

## Slide 122
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
1
0
0
1
0
0
1
1
1
0
Current state
Future state

## Slide 123
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
1
0
0
1
0
0
1
1
1
0

## Slide 124
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
1
0
1
0
1
0
1
0
0
0

## Slide 125
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
1
0
1
0
1
0
1
0
0
0
Current state
Future state

## Slide 126
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
0
1
1
0
1
1
0
1
0
1

## Slide 127
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
0
1
0
1
0
1
0
0
0
0

## Slide 128
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
0
1
0
1
0
1
0
0
0
0

## Slide 129
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
0
1
1
0
1
1
0
1
0
1
Current state
Future state

## Slide 130
[ Figure 5.15d from the textbook ]
1
1
0
0
1
1
1
0
1
1
0
1
T Flip-Flop (Timing Diagram)
1
0
1
0
1
0
1
0
0
0

## Slide 131
JK Flip-Flop

## Slide 132
[ Figure 5.16a from the textbook ]
JK Flip-Flop
D = JQ + KQ

## Slide 133
[ Figure 5.16 from the textbook ]
JK Flip-Flop
J
Q
Q
K
0
1
Q
t
1
+
(
)
Q
t
(
)
0
(b) Truth table
(c) Graphical symbol
J
0
0
0
1
1
1
Q
t
(
)
1
K
D
Q
Q
Q
Q
J
Clock
(a) Circuit
K
Hold
Reset
Set
Toggle

## Slide 134: JK Flip-Flop (how it works)
A more versatile flip-flop.
If J=0 and K=0 it stays in the same state.
If J=1 and K=0 it sets the output Q to 1.
If J=0 and K=1 it resets the output Q to 0.
If J=1 and K=1 it toggles the output Q.
If J=K then it behaves like a T flip-flop.

## Slide 135: JK Flip-Flop (timing diagram)

## Slide 136: JK Flip-Flop (timing diagram)

## Slide 137: JK Flip-Flop (timing diagram)

## Slide 138: JK Flip-Flop (timing diagram)

## Slide 139: JK Flip-Flop (timing diagram)

## Slide 140: JK Flip-Flop (timing diagram)
[https://en.wikipedia.org/wiki/Flip-flop_(electronics)]

## Slide 141: JK Flip-Flop (timing diagram)
[https://en.wikipedia.org/wiki/Flip-flop_(electronics)]

## Slide 142
Complete Wiring Diagrams

## Slide 143
Positive-Edge-Triggered D Flip-Flop

## Slide 144
Negative-Edge-Triggered D Flip-Flop

## Slide 145: Complete Wiring Diagrams

## Slide 146
The Complete Wiring Diagram for
a Positive-Edge-Triggered D Flip-Flop
D
Clock
Q
Q

## Slide 147
The Complete Wiring Diagram for
a Negative-Edge-Triggered D Flip-Flop
Q
Q
D
Clock

## Slide 148
The Complete Wiring Diagram for
a Negative-Edge-Triggered D Flip-Flop
Q
Q
D
Clock

## Slide 149
T
D
Q
Q
Clock
Positive-Edge-Triggered T Flip-Flop

## Slide 150
Negative-Edge-Triggered T Flip-Flop
T
D
Q
Q
Clock

## Slide 151
The Complete Wiring Diagram for
a Positive-Edge-Triggered T Flip-Flop
T
Clock
Q
Q

## Slide 152
The Complete Wiring Diagram for
a Negative-Edge-Triggered T Flip-Flop
T
Clock
Q
Q

## Slide 153
D
Q
Q
Q
Q
J
Clock
K
Positive-Edge-Triggered JK Flip-Flop

## Slide 154
D
Q
Q
Q
Q
J
Clock
K
Negative-Edge-Triggered JK Flip-Flop

## Slide 155
The Complete Wiring Diagram for
a Positive-Edge-Triggered JK Flip-Flop
Q
Q
Clock
J
K

## Slide 156
The Complete Wiring Diagram for
a Negative-Edge-Triggered JK Flip-Flop
Q
Q
Clock
J
K

## Slide 157: Complete the Timing diagrams (for positive-edge-triggered F-F)

## Slide 164: Complete the Timing diagrams (for negative-edge-triggered F-F)

## Slide 171: Questions?

## Slide 172: THE END