## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
State Minimization
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
Homework 11 is due on Monday Nov 18 @ 10pm
Homework 12 will be due on Monday Dec 2 @ 10pm

## Slide 4
“Two states Si and Sj are said to be equivalent if and only if for every possible input sequence, the same output sequence will be produced regardless of whether Si or Sj is the initial state.”
Equivalence of states
[ Page 374 in the textbook ]

## Slide 5: Partition Minimization Procedure

## Slide 6: 0-successor
Assuming that we have only one input signal w
S2 is a 0-successor of S1
S1
S2
w = 0

## Slide 7: 0-successor
Assuming that we have only one input signal w
S2 is a 0-successor of S1
S1
S2
w = 0
S5
w = 0
S2 is a 0-successor of S5

## Slide 8: 1-successor
Assuming that we have only one input signal w
S4 is a 1-successor of S3
S3
S4
w = 1

## Slide 9: 1-successor
Assuming that we have only one input signal w
S4 is a 1-successor of S3
S3
S4
w = 1
S6
w = 1
S4 is a 1-successor of S6

## Slide 10: 1-successor
Assuming that we have only one input signal w
S4 is a 1-successor of S3
S3
S4
w = 1
S6
w = 1
S4 is a 1-successor of S6
S7
S7 is a 1-successor of S4
w = 1

## Slide 11: k-successors of a State
Assuming that we have only one input signal w,
then k can only be equal to 0 or 1.

## Slide 12: k-successors of a State
Assuming that we have only one input signal w,
then k can only be equal to 0 or 1.
In other words, this is the familiar 0-successor
or 1-successor case.
S2 is a 0-successor of S1
S1
S2
w = 0
S3
w = 1
S3 is a 1-successor of S1

## Slide 13: k-successors of a State
If we have two input signals, e.g., w0 and w1,
then k can only be equal to 0,1, 2, or 3.

## Slide 14: k-successors of a State
If we have two input signals, e.g., w0 and w1,
then k can only be equal to 0,1, 2, or 3.
S1 is a 3-successor of S2
S2
S1
w0=1, w1 = 1
S4
S4 is a 3-successor of S2
w0=1, w1 = 1

## Slide 15
“If states Si and Sj are equivalent, then their corresponding k-successors (for all k) are also equivalent.”
Equivalence of states
[ Page 374 in the textbook ]

## Slide 16: Partition
“A partition consists of one or more blocks, where each block comprises a subset of states that may be equivalent, but the states in a given block are definitely not equivalent to the states in other blocks.”
[ Page 374 in the textbook ]

## Slide 17
Present
Next state
Output
state
w
=
0
w
=
1
z
A
B
C
1
B
D
F
1
C
F
E
0
D
B
G
1
E
F
C
0
F
E
D
0
G
F
G
0
State Table for This Example
[ Figure 6.51 from the textbook ]

## Slide 18
A
B
C
D
E
F
G
State Diagram
(just the states)

## Slide 19
A
B
C
D
E
F
G
State Diagram
(transitions when w=0)

## Slide 20
A
B
C
D
E
F
G
State Diagram
(transitions when w=1)

## Slide 21
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Outputs

## Slide 22
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #1
(All states in the same partition)

## Slide 23
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #1
(ABCDEFG)

## Slide 24
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #2
(based on outputs)
z=1
z=0

## Slide 25
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #2
(ABD)(CEFG)
z=1
z=0

## Slide 26
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3.1
(Examine the 0-successors of ABD)

## Slide 27
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3.1
(Examine the 1-successors of ABD)

## Slide 28
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3.2
(Examine the 0-successors of CEFG)

## Slide 29
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3.2
(Examine the 1-successors of CEFG)

## Slide 30
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3.2
(Examine the 1-successors of CEFG)
This needs to be
in a new block

## Slide 31
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3
(ABD)(CEG)(F)

## Slide 32
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #3
(ABD)(CEG)(F)

## Slide 33
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #4.1
(Examine the 0-successors of ABD)

## Slide 34
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #4.1
(Examine the 1-successors of ABD)

## Slide 35
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #4.1
(Examine the 1-successors of ABD)
This needs to be
in a new block

## Slide 36
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #4
(AD)(B)(CEG)(F)

## Slide 37
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #4
(AD)(B)(CEG)(F)

## Slide 38
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.1
(Examine the 0-successors of AD)

## Slide 39
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.1
(Examine the 1-successors of AD)

## Slide 40
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.2
(Examine the 0-successors of B)

## Slide 41
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.2
(Examine the 1-successors of B)

## Slide 42
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.3
(Examine the 0-successors of CEG)

## Slide 43
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.3
(Examine the 1-successors of CEG)

## Slide 44
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.4
(Examine the 0-successors of F)

## Slide 45
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
Partition #5.4
(Examine the 1-successors of F)

## Slide 46
Partition #5
(AD)(B)(CEG)(F)
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0

## Slide 47
Partition #4
(AD)(B)(CEG)(F)
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0

## Slide 48
Partition #5
(This is the same as #4 so we can stop here)
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0

## Slide 49
Stop Here …
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0

## Slide 50
… and Relabel All Partitions
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
A
B
C
F

## Slide 51
… and Relabel All Partitions
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
A
B
C
F

## Slide 52
Merge the states in the same partition
A
B
C
D
E
F
G
z=1
z=1
z=1
z=0
z=0
z=0
z=0
A
B
C
F
these two are
now called A

## Slide 53
Merge the states in the same partition
A
B
C
E
F
G
z=1
z=1
z=0
z=0
z=0
z=0
B
C
F

## Slide 54
Merge the states in the same partition
A
B
C
E
F
G
z=1
z=1
z=0
z=0
z=0
z=0
B
C
F
this is
still B

## Slide 55
Merge the states in the same partition
A
B
C
E
F
G
z=1
z=1
z=0
z=0
z=0
z=0
C
F

## Slide 56
Merge the states in the same partition
A
B
C
E
F
G
z=1
z=1
z=0
z=0
z=0
z=0
C
F
these three are
now called C

## Slide 57
Merge the states in the same partition
A
B
C
F
z=1
z=1
z=0
z=0
F

## Slide 58
Merge the states in the same partition
A
B
C
F
z=1
z=1
z=0
z=0
F
this is
still F

## Slide 59
Merge the states in the same partition
A
B
C
F
z=1
z=1
z=0
z=0

## Slide 60
Merge the transitions too
A
B
C
F
z=1
z=1
z=0
z=0

## Slide 61
The Minimized Graph
A
B
C
F
z=1
z=1
z=0
z=0

## Slide 62
Present
Nextstate
Output
state
w
=
0
w
=
1
z
A
B
C
1
B
A
F
1
C
F
C
0
F
C
A
0
[ Figure 6.52 from the textbook ]
Minimized state table

## Slide 63: To Summarize

## Slide 64
A
B
C
D
E
F
G
Original State Diagram

## Slide 65
Minimized State Diagram
A
B
C
F
z=1
z=1
z=0
z=0

## Slide 66
Minimized State Diagram
A
B
C
F
z=1
z=1
z=0
z=0
w = 0
w = 0
w = 0
w = 0
w = 1
w = 1
w = 1
w = 1

## Slide 67
Minimized State Diagram
A
B
C
F
z=1
z=1
z=0
z=0
w = 0
w = 0
w = 0
w = 0
w = 1
w = 1
w = 1
w = 1

## Slide 68
Present
Nextstate
Output
state
w
=
0
w
=
1
z
A
B
C
1
B
A
F
1
C
F
C
0
F
C
A
0
[ Figure 6.52 from the textbook ]
Minimized state table

## Slide 69: Vending Machine Example (Moore-Type)

## Slide 70: Vending Machine Example
The machine accepts nickels and dimes
It takes 15 cents for a piece of candy to be released from the machine
If 20 cents is deposited, the machine will not return the change, but it will credit the buyer with 5 cents and wait for the buyer to make a second purchase.

## Slide 71
sense
N
sense
D
Clock
N
D
[ Figure 6.53.a from the textbook ]
Signals for the vending machine
(a) Timing diagram

## Slide 72
sense
N
sense
D
Clock
N
D
[ Figure 6.53 from the textbook ]
Signals for the vending machine
The nickel sensor will be ON
for several clock cycles
while the coin is falling down.

## Slide 73
sense
N
sense
D
Clock
N
D
[ Figure 6.53 from the textbook ]
Signals for the vending machine
But the FSM needs a nickel signal (N)
that is ON for only one clock cycle.

## Slide 74
sense
N
sense
D
Clock
N
D
[ Figure 6.53 from the textbook ]
Signals for the vending machine
Similarly, for the dime sensor
and the dime signal (D).

## Slide 75
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
0
0
0
1
1
0
0

## Slide 76
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
1
0
0
1
1
0
0

## Slide 77
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
1
1
1
1
1
1
0

## Slide 78
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
1
1
1
0
0
0
1

## Slide 79
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
1
1
1
0
0
0
1

## Slide 80
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
0
1
1
0
0
0
1

## Slide 81
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
0
0
0
0
0
0
1

## Slide 82
D
Q
Q
sense
N
D
Q
Q
Clock
N
sense
N
sense
D
Clock
N
D
(a) Timing diagram
(b) Circuit that generates
N
[ Figure 6.53 from the textbook ]
Signals for the vending machine
0
0
0
1
1
0
0

## Slide 83
S1
0
¤
S7
1
¤
DN
D
N
S3
0
¤
S6
0
¤
S9
1
¤
S8
1
¤
S2
0
¤
S5
1
¤
S4
1
¤
DN
DN
DN
DN
DN
DN
DN
D
D
N
D
N
DN
N
Reset
[ Figure 6.54 from the textbook ]
State Diagram for the vending machine

## Slide 84
S1
0
¤
S7
1
¤
DN
D
N
S3
0
¤
S6
0
¤
S9
1
¤
S8
1
¤
S2
0
¤
S5
1
¤
S4
1
¤
DN
DN
DN
DN
DN
DN
DN
D
D
N
D
N
DN
N
Reset
[ Figure 6.54 from the textbook ]
State Diagram for the vending machine
10c
5c
15c
20c
0c
15c
10c
15c
20c

## Slide 85
Present
Next state
Output
state
DN
=00
01
10
11
z
S1
S1
S3
S2
0
S2
S2
S4
S5
0
S3
S3
S6
S7
0
S4
S1
1
S5
S3
1
S6
S6
S8
S9
0
S7
S1
1
S8
S1
1
S9
S3
1
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
[ Figure 6.55 from the textbook ]
State Table for the vending machine
Incompletely specified state table

## Slide 86
Present
Next state
Output
state
DN
=00
01
10
11
z
S1
S1
S3
S2
0
S2
S2
S4
S5
0
S3
S3
S6
S7
0
S4
S1
1
S5
S3
1
S6
S6
S8
S9
0
S7
S1
1
S8
S1
1
S9
S3
1
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
[ Figure 6.55 from the textbook ]
State Table for the vending machine
Incompletely specified state table
We cannot insert both a nickel and a dime at the same time.

## Slide 87
Present
Next state
Output
state
DN
=00
01
10
11
z
S1
S1
S3
S2
0
S2
S2
S4
S5
0
S3
S3
S6
S7
0
S4
S1
1
S5
S3
1
S6
S6
S8
S9
0
S7
S1
1
S8
S1
1
S9
S3
1
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
[ Figure 6.55 from the textbook ]
State Table for the vending machine
Incompletely specified state table
The machine is in S4 and S5 for only 1 clock cycle. Which is shorter than the time it takes for the coin to fall down. It is physically impossible for another coin to be inserted at that time.

## Slide 88
S1
0
¤
S7
1
¤
DN
D
N
S3
0
¤
S6
0
¤
S9
1
¤
S8
1
¤
S2
0
¤
S5
1
¤
S4
1
¤
DN
DN
DN
DN
DN
DN
DN
D
D
N
D
N
DN
N
Reset
[ Figure 6.54 from the textbook ]
State Diagram for the vending machine
10c
5c
15c
20c
0c
15c
10c
15c
20c

## Slide 89
Present
Next state
Output
state
DN
=00
01
10
11
z
S1
S1
S3
S2
0
S2
S2
S4
S5
0
S3
S3
S6
S7
0
S4
S1
1
S5
S3
1
S6
S6
S8
S9
0
S7
S1
1
S8
S1
1
S9
S3
1
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
–
[ Figure 6.55 from the textbook ]
State Table for the vending machine
Incompletely specified state table
The machine is in states S7, S8, and S9 for only 1 clock cycle. Which is shorter than the time it takes for the coin to fall down.

## Slide 90
S1
0
¤
S7
1
¤
DN
D
N
S3
0
¤
S6
0
¤
S9
1
¤
S8
1
¤
S2
0
¤
S5
1
¤
S4
1
¤
DN
DN
DN
DN
DN
DN
DN
D
D
N
D
N
DN
N
Reset
[ Figure 6.54 from the textbook ]
State Diagram for the vending machine
10c
5c
15c
20c
0c
15c
10c
15c
20c

## Slide 91
Present state | Next state |  |  |  | Output
 | 00 | 01 | 10 | 11 | z
S1 | S1 | S3 | S2 | - | 0
S3 | S3 | S6 | S7 | - | 0
S2 | S2 | S4 | S5 | - | 0
S6 | S6 | S8 | S9 | - | 0
S4 | S1 | - | - | - | 1
S7 | S1 | - | - | - | 1
S8 | S1 | - | - | - | 1
S5 | S3 | - | - | - | 1
S9 | S3 | - | - | - | 1
P1=(S1,S2,S3,S4,S5,S6,S7,S8,S9)
Partition for Vending Machine FSM

## Slide 92
Present state | Next state |  |  |  | Output
 | 00 | 01 | 10 | 11 | z
S1 | S1 | S3 | S2 | - | 0
S3 | S3 | S6 | S7 | - | 0
S2 | S2 | S4 | S5 | - | 0
S6 | S6 | S8 | S9 | - | 0
S4 | S1 | - | - | - | 1
S7 | S1 | - | - | - | 1
S8 | S1 | - | - | - | 1
S5 | S3 | - | - | - | 1
S9 | S3 | - | - | - | 1
P1=(S1,S2,S3,S4,S5,S6,S7,S8,S9)
P2=(S1,S2,S3,S6) (S4,S5,S7,S8,S9)
Partition for Vending Machine FSM
partition based on
common output

## Slide 93
Present state | Next state |  |  |  | Output
 | 00 | 01 | 10 | 11 | z
S1 | S1 | S3 | S2 | - | 0
S3 | S3 | S6 | S7 | - | 0
S2 | S2 | S4 | S5 | - | 0
S6 | S6 | S8 | S9 | - | 0
S4 | S1 | - | - | - | 1
S7 | S1 | - | - | - | 1
S8 | S1 | - | - | - | 1
S5 | S3 | - | - | - | 1
S9 | S3 | - | - | - | 1
P1=(S1,S2,S3,S4,S5,S6,S7,S8,S9)
P2=(S1,S2,S3,S6) (S4,S5,S7,S8,S9)
P3=(S1) (S3) (S2,S6) (S4,S5,S7,S8,S9)
Partition for Vending Machine FSM

## Slide 94
Present state | Next state |  |  |  | Output
 | 00 | 01 | 10 | 11 | z
S1 | S1 | S3 | S2 | - | 0
S3 | S3 | S6 | S7 | - | 0
S2 | S2 | S4 | S5 | - | 0
S6 | S6 | S8 | S9 | - | 0
S4 | S1 | - | - | - | 1
S7 | S1 | - | - | - | 1
S8 | S1 | - | - | - | 1
S5 | S3 | - | - | - | 1
S9 | S3 | - | - | - | 1
P1=(S1,S2,S3,S4,S5,S6,S7,S8,S9)
P2=(S1,S2,S3,S6) (S4,S5,S7,S8,S9)
P3=(S1) (S3) (S2,S6) (S4,S5,S7,S8,S9)
P4=(S1) (S3) (S2,S6) (S4,S7,S8) (S5,S9)
Partition for Vending Machine FSM

## Slide 95
Present state | Next state |  |  |  | Output
 | 00 | 01 | 10 | 11 | z
S1 | S1 | S3 | S2 | - | 0
S3 | S3 | S6 | S7 | - | 0
S2 | S2 | S4 | S5 | - | 0
S6 | S6 | S8 | S9 | - | 0
S4 | S1 | - | - | - | 1
S7 | S1 | - | - | - | 1
S8 | S1 | - | - | - | 1
S5 | S3 | - | - | - | 1
S9 | S3 | - | - | - | 1
P1=(S1,S2,S3,S4,S5,S6,S7,S8,S9)
P2=(S1,S2,S3,S6) (S4,S5,S7,S8,S9)
P3=(S1) (S3) (S2,S6) (S4,S5,S7,S8,S9)
P4=(S1) (S3) (S2,S6) (S4,S7,S8) (S5,S9)
P5=(S1) (S3) (S2,S6) (S4,S7,S8) (S5,S9)
Partition for Vending Machine FSM

## Slide 96
Present state | Next state |  |  |  | Output
 | 00 | 01 | 10 | 11 | z
S1 | S1 | S3 | S2 | - | 0
S3 | S3 | S6 | S7 | - | 0
S2 | S2 | S4 | S5 | - | 0
S6 | S6 | S8 | S9 | - | 0
S4 | S1 | - | - | - | 1
S7 | S1 | - | - | - | 1
S8 | S1 | - | - | - | 1
S5 | S3 | - | - | - | 1
S9 | S3 | - | - | - | 1
P1=(S1,S2,S3,S4,S5,S6,S7,S8,S9)
P2=(S1,S2,S3,S6) (S4,S5,S7,S8,S9)
P3=(S1) (S3) (S2,S6) (S4,S5,S7,S8,S9)
P4=(S1) (S3) (S2,S6) (S4,S7,S8) (S5,S9)
P5=(S1) (S3) (S2,S6) (S4,S7,S8) (S5,S9)
Partition for Vending Machine FSM

## Slide 97
Present
Next state
Output
state
DN
=00
01
10
11
z
S1
S1
S3
S2
0
S2
S2
S4
S5
0
S3
S3
S2
S4
0
S4
S1
1
S5
S3
1
–
–
–
–
–
–
–
–
–
[ Figure 6.56 from the textbook ]
Minimized State Table for the vending machine

## Slide 98
Present
Next state
Output
state
DN
=00
01
10
11
z
S1
S1
S3
S2
0
S2
S2
S4
S5
0
S3
S3
S2
S4
0
S4
S1
1
S5
S3
1
–
–
–
–
–
–
–
–
–
[ Figure 6.56 from the textbook ]
Minimized State Table for the vending machine
S1
0
¤
S5
1
¤
DN
DN
DN
DN
DN
D
D
D
N
N
N
S3
0
¤
S2
¤
0
S4
1
¤
[ Figure 6.57 from the textbook ]

## Slide 99
S1
0
¤
S5
1
¤
DN
DN
DN
DN
DN
D
D
D
N
N
N
S3
0
¤
S2
¤
0
S4
1
¤
[ Figure 6.57 from the textbook ]
Minimized State Diagram for the vending machine

## Slide 100
S1
0
¤
S5
1
¤
DN
DN
DN
DN
DN
D
D
D
N
N
N
S3
0
¤
S2
¤
0
S4
1
¤
[ Figure 6.57 from the textbook ]
Minimized State Diagram for the vending machine
10c
5c
15c
20c
0c

## Slide 101: Vending Machine Example (Mealy-Type)

## Slide 102
S3
S2
D
0
¤
S1
D
1
¤
D
1
¤
N
1
¤
N
0
¤
N
0
¤
DN
0
¤
DN
0
¤
DN
0
¤
[ Figure 6.58 from the textbook ]
Mealy-type FSM for the vending machine

## Slide 103
S3
S2
D
0
¤
S1
D
1
¤
D
1
¤
N
1
¤
N
0
¤
N
0
¤
DN
0
¤
DN
0
¤
DN
0
¤
[ Figure 6.58 from the textbook ]
Mealy-type FSM for the vending machine
5c
0c
10c

## Slide 105
Present
Next state
Output
z
state
w
=
0
w
=
1
w
=
0
w
=
1
A
B
C
0
0
B
D
0
C
F
E
0
1
D
B
G
0
0
E
F
C
0
1
F
E
D
0
1
G
F
0
–
–
–
–
[ Figure 6.59 from the textbook ]
Another Example of
Incompletely specified state table

## Slide 106: Questions?

## Slide 107: THE END