## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2: Assembly Language
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Assembly Language (for the i281 CPU)
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 4
[http://en.wikipedia.org/wiki/Intel_8086]
Intel 8086
Example

## Slide 5
[http://en.wikipedia.org/wiki/Intel_8086]
Memory Address
Intel 8086
Example

## Slide 6
[http://en.wikipedia.org/wiki/Intel_8086]
Machine
Language
Intel 8086
Example

## Slide 7
[http://en.wikipedia.org/wiki/Intel_8086]
Assembly
Language
Intel 8086
Example

## Slide 8
Comments
[http://en.wikipedia.org/wiki/Intel_8086]
Intel 8086
Example

## Slide 9: i281 CPU Architecture

## Slide 10
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 11
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 12
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
0 0 0 0
c14
Flags
Write
Select
Read
Select
Read
Select
Write
Select
Write Enable
Write Enable
Write Enable
Write Enable
Write Enable
Write
Select
Port0 Read Select
Port1 Read Select
ALU Select
PC Mux
DMEM Input Mux
REG Writeback Mux
ALU Result Mux
ALU Source Mux
Input
Input
Input

## Slide 13
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 14: i281 Simulator

## Slide 15: i281 Simulator
To try the simulator, go to the class web page and follow the link.

## Slide 16: i281 Example: Add the numbers from 1 to 5

## Slide 17: i281 Example: Add the numbers from 1 to 5 C Language v.s. Assembly Language

## Slide 18: C Version
// C Version
//
// Add the numbers from 1 to 5 using a for loop.
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++)
sum+=i;
// printf("%d\n", sum);
}

## Slide 19: i281 Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; update the memory for sum
; Register allocation:
; A: i
; B: sum
; C: <not used>
; D: N

## Slide 20: i281 Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; update the memory for sum
; Register allocation:
; A: i
; B: sum
; C: <not used>
; D: N

## Slide 21: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 22: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 23: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 24: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 25: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 26: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=1

## Slide 27: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
Load the value of N into register D.
This has no analog in the C version,
which is written in a high-level language.
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 28: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 29: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 30: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 31: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 32: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=2

## Slide 33: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 34: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 35: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 36: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=3

## Slide 37: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 38: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 39: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 40: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=4

## Slide 41: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 42: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 43: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 44: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=5

## Slide 45: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 46: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 47: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 48: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=6

## Slide 49: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 50: i281 Example: Add the numbers from 1 to 5 Assembly Language v.s. Machine Language

## Slide 51: i281 Assembly Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; update the memory for sum

## Slide 52: i281 Assembly Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B

## Slide 53: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
0011010000000000
0011000000000001
1000110000000000
1101001100000000
1111001000000011
0100010000000000
0101000000000001
1110000011111011
1010010000000010
Machine Language

## Slide 54: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
0000 0101
0000 0000
0000 0000
Code Memory:
0011 0100 0000 0000
0011 0000 0000 0001
1000 1100 0000 0000
1101 0011 0000 0000
1111 0010 0000 0011
0100 0100 0000 0000
0101 0000 0000 0001
1110 0000 1111 1011
1010 0100 0000 0010
Machine Language
in Binary

## Slide 55: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
0 5
0 0
0 0
Code Memory:
3 4 0 0
3 0 0 1
8 C 0 0
D 3 0 0
F 2 0 3
4 4 0 0
5 0 0 1
E 0 F B
A 4 0 2
Machine Language
in Binary

## Slide 56: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
05
00
00
Code Memory:
34 00
30 01
8C 00
D3 00
F2 03
44 00
50 01
E0 FB
A4 02
Machine Language
in Hexadecimal

## Slide 57: i281 Example: Add the numbers from 1 to 5 Preview of OPCODEs

## Slide 58: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
0011010000000000
0011000000000001
1000110000000000
1101001100000000
1111001000000011
0100010000000000
0101000000000001
1110000011111011
1010010000000010
Machine Language

## Slide 59: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
00110100_00000000
00110000_00000001
10001100_00000000
11010011_00000000
11110010_00000011
01000100_00000000
01010000_00000001
11100000_11111011
10100100_00000010
Machine Language

## Slide 60: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010
Machine Language

## Slide 61: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 62: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 63: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 64: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 65: OPCODE Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 66: OPCODE Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 67: Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 68: Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 69: Second Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 70: Second Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 71: Value / Address / Offset Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 72: Value / Address / Offset Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 73: “Don’t care” bits …
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_dd_00000000
0011_00_dd_00000001
1000_11_dd_00000000
1101_00_11_dddddddd
1111_dd_10_00000011
0100_01_00_dddddddd
0101_00_dd_00000001
1110_dd_dd_11111011
1010_01_dd_00000010

## Slide 74: … are mapped to 0 by the Assembler
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 75: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 76
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 77
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 78
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 79
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 80
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 81
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 82: The Assembly Language Instructions

## Slide 83: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 84: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 85: The OPCODEs

## Slide 86: There are only 26 OPCODEs
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI
LOADP
SHIFTL
SHIFTR
CMP
JUMP
BRE
BRZ
BRNE
BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF

## Slide 87: There are only 26 OPCODEs
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI
LOADP
SHIFTL
SHIFTR
CMP
JUMP
BRE
BRZ
BRNE
BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
All of these are available in the assembly language for this processor.
However, three pairs are aliased at the machine language level.

## Slide 88: There are only 26 OPCODEs
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI
LOADP
SHIFTL
SHIFTR
CMP
JUMP
BRE
BRZ
BRNE
BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
these two
are aliased
They have a different meaning in the assembly language, but the
assembler maps them to the same machine language OPCODE.
25

## Slide 89: There are only 26 OPCODEs
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP
SHIFTL
SHIFTR
CMP
JUMP
BRE
BRZ
BRNE
BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
25

## Slide 90: There are only 26 OPCODEs
SHIFTL
SHIFTR
CMP
JUMP
BRE
BRZ
BRNE
BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
these two
are aliased
24
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP

## Slide 91: There are only 26 OPCODEs
SHIFTL
SHIFTR
CMP
JUMP
BRE
BRZ
BRNE
BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
these two
are aliased
23
these two
are aliased
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP

## Slide 92: There are only 23 OPCODEs
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP
SHIFTL
SHIFTR
CMP
JUMP
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF

## Slide 93: The OPCODEs
( Mapped to Machine Language )

## Slide 94: The OPCODEs
0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d | d | d | d | d
NOOP
0 | 0 | 0 | 1 | d | d | 0 | 0 | C | A | D | D | R | E | S | S
INPUTC
0 | 0 | 0 | 1 | R | X | 0 | 1 | C | A | D | D | R | E | S | S
INPUTCF
0 | 0 | 0 | 1 | d | d | 1 | 0 | D | A | D | D | R | E | S | S
INPUTD
0 | 0 | 0 | 1 | R | X | 1 | 1 | D | A | D | D | R | E | S | S
INPUTDF
0 | 0 | 1 | 0 | R | X | R | Y | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
MOVE
0 | 0 | 1 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
LOADI/LOADP

## Slide 95: The OPCODEs
0 | 1 | 0 | 0 | R | X | R | Y | d | d | d | d | d | d | d | d
ADD
0 | 1 | 0 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
ADDI
0 | 1 | 1 | 0 | R | X | R | Y | d | d | d | d | d | d | d | d
SUB
0 | 1 | 1 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
SUBI
1 | 0 | 0 | 0 | R | X | d | d | D | A | D | D | R | E | S | S
LOAD
1 | 0 | 0 | 1 | R | X | R | Y | D | A | D | D | R | E | S | S
LOADF
1 | 0 | 1 | 0 | R | X | d | d | D | A | D | D | R | E | S | S
STORE
1 | 0 | 1 | 1 | R | X | R | Y | D | A | D | D | R | E | S | S
STOREF

## Slide 96: The OPCODEs
1 | 1 | 0 | 0 | R | X | d | 0 | d | d | d | d | d | d | d | d
SHIFTL
1 | 1 | 0 | 0 | R | X | d | 1 | d | d | d | d | d | d | d | d
SHIFTR
1 | 1 | 0 | 1 | R | X | R | Y | d | d | d | d | d | d | d | d
CMP
1 | 1 | 1 | 0 | d | d | d | d | P | C | O | F | F | S | E | T
JUMP
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
BRE/BRZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
BRNE/BRNZ
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
BRG
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
BRGE

## Slide 97: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 98
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Don’t do anything for one clock cycle:
NOOP NO OPeration

## Slide 100
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Read from the value provided by the used on the external switches and store that value in code memory.
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset

## Slide 101
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Read from the value provided by the used on the external switches and store that value in data memory.
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset

## Slide 102
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Instructions that change the value of the Program Counter based on the contents of the Flags register that were set during the most recent previous arithmetic instruction. If the condition is met the offset in the instruction is added to the Program counter.
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 103
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Instruction that changes the value of the Program Counter by adding a number stored as part of the instruction. This is unconditional, does not depend on the Flags register.
JUMP JUMP unconditionally to a specified address

## Slide 105
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Arithmetic operations with two registers
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
CMP CoMPare the values in two registers

## Slide 106
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Arithmetic operations with only one register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register

## Slide 108
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Read from the data memory into a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register

## Slide 109
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Write from a register to an address in data memory:
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register

## Slide 111
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Load a constant (immediate value) into a register
LOADI LOAD Immediate value

## Slide 112
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Copy one register into another register
MOVE MOVE the contents of one register into another

## Slide 113: The OPCODEs
( With More Details)

## Slide 114: NOOP
Full name:
NO OPeration
Description:
Do nothing for one clock cycle, i.e., idle.
Assembly Example:
NOOP
0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d | d | d | d | d
Instruction Layout:

## Slide 115: ADD
Full name:
ADD two registers
Description:
Add the values stored in two registers. The result of the addition is stored in the first register.
The flags are updated.
Assembly Example:
ADD A, C
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:

## Slide 116: ADD
Full name:
ADD two registers
Description:
Add the values stored in two registers. The result of the addition is stored in the first register.
The flags are updated.
Assembly Example:
ADD A, C
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:
 |  | Register
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 117: ADD
Full name:
ADD two registers
Description:
Add the values stored in two registers. The result of the addition is stored in the first register.
The flags are updated.
Assembly Example:
ADD A, C
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:
 |  | Register
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 118: MOVE
Full name:
MOVE
Description:
  Move (i.e., copy) the contents of the second register into the first register, overwriting the first register.
  This is implemented as A=B+0. Thus, the mandatory zeros in the last 8 bits, which must go through the ALU.
  The flags are not updated.
Assembly Example:
MOVE A, B
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 119: SUB
Full name:
SUBtract two registers
Description:
    Subtract the values stored in two registers. This is done by subtracting the second register from the first register. The result of the subtraction is stored in the first register. The flags are updated.
Assembly Example:
SUB B, C
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:

## Slide 120: CMP
Full name:
CoMPare the values stored in two registers
Description:
Compare two registers by subtracting the second register from the first register. The result of the subtraction is not stored. Only the flags are updated.
Assembly Example:
CMP D, C
1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:

## Slide 121: CMP
Full name:
CoMPare the values stored in two registers
Description:
Compare two registers by subtracting the second register from the first register. The result of the subtraction is not stored. Only the flags are updated.
Assembly Example:
CMP D, C
1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:
 |  | Register
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 122: CMP
Full name:
CoMPare the values stored in two registers
Description:
Compare two registers by subtracting the second register from the first register. The result of the subtraction is not stored. Only the flags are updated.
Assembly Example:
CMP D, C
1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
Instruction Layout:
 |  | Register
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 123: SHIFTL
Full name:
SHIFT Left
Description:
Shift left all bits in a register. The bit that is shifted out is stored in the carry flag. The LSB is set 0.
Update the flags based on the final value.
Assembly Example:
SHIFTL B
1 | 1 | 0 | 0 | 0 | 1 | d | 0 | d | d | d | d | d | d | d | d
Instruction Layout:

## Slide 124: SHIFTR
Full name:
SHIFT Right
Description:
Shift right all bits in a register. The bit that is shifted out is stored in the carry flag. The MSB is set 0.
Update the flags based on the final value.
Assembly Example:
SHIFTR C
1 | 1 | 0 | 0 | 1 | 0 | d | 1 | d | d | d | d | d | d | d | d
Instruction Layout:

## Slide 125: JUMP
Full name:
JUMP
Description:
Unconditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
JUMP End
1 | 1 | 1 | 0 | d | d | d | d | P | C | O | F | F | S | E | T
Instruction Layout:

## Slide 126: BRE
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
Instruction Layout:
Full name:
BRanch if Equal
Description:
Conditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
BRE Start

## Slide 127: BRZ
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
Instruction Layout:
Full name:
BRanch if Zero (identical to BRE)
Description:
Conditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
BRZ Start

## Slide 128: BRNE
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
Instruction Layout:
Full name:
BRanch if Not Equal
Description:
Conditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
BRNE Loop

## Slide 129: BRNZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
Instruction Layout:
Full name:
BRanch if Not Zero (identical to BRNE)
Description:
Conditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
BRNZ Loop

## Slide 130: BRG
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
Instruction Layout:
Full name:
BRanch if Greater
Description:
Conditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
BRG InnerLoop

## Slide 131: BRGE
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
Instruction Layout:
Full name:
BRanch if Greater
Description:
Conditional jump to the specified address, which is
given as a label for some row of the assembly program, but converted to a PC offset in the machine code.
Assembly Example:
BRGE OuterLoop

## Slide 133: ADDI
Full name:
ADD an Immediate value to a register
Description:
  Add the immediate value, which is stored in the last 8 bits of the instruction in the code memory, to the register.
  The result of the addition is stored in the same register.
  The flags are updated.
Assembly Example:
ADDI A, 3
0 | 1 | 0 | 1 | 0 | 0 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Instruction Layout:

## Slide 134: SUBI
Full name:
  SUBtract an Immediate value from a register
Description:
  Subtract the immediate value, which is stored in the last 8 bits of the instruction in the code memory, from the register.
  The result of the subtraction is stored in the same register.
  The flags are updated.
Assembly Example:
SUBI C, 5
0 | 1 | 1 | 1 | 1 | 0 | d | d | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
Instruction Layout:

## Slide 135: LOADI
Full name:
  LOAD an Immediate value into a register
Description:
  Load the immediate value, which is stored in the last 8 bits of the instruction in the code memory, into the register.
  The old value of the register is overwritten.
Assembly Example:
LOADI B, 6
0 | 0 | 1 | 1 | 0 | 1 | d | d | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Instruction Layout:

## Slide 137: LOADP
Full name:
  LOAD a Pointer address into a register
Description:
  Load the address of a data memory location into a register. The address is specified by the label for that memory cell, surrounded by curly brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
M BYTE 3 ; this is stored at address 0
N BYTE 5 ; this is stored at address 1
.code
LOADP A, {M}
0 | 0 | 1 | 1 | 0 | 0 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 138: LOADP
Full name:
  LOAD a Pointer address into a register
Description:
  Load the address of a data memory location into a register. The address is specified by the label for that memory cell, surrounded by curly brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
M BYTE 3 ; this is stored at address 0
N BYTE 5 ; this is stored at address 1
.code
LOADP A, {M+1} ; +1 is an optional additive constant
0 | 0 | 1 | 1 | 0 | 0 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Instruction Layout:

## Slide 140: LOAD
Full name:
  LOAD the value from a data memory address into a register
Description:
  Load the contents of a data memory cell into a register. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
N BYTE 3 ; this is stored at address 0
array BYTE 4, 7, 1 ; this is stored at addresses 1, 2, 3
.code
LOAD C, [array]
1 | 0 | 0 | 0 | 1 | 0 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Instruction Layout:

## Slide 141: LOAD
Full name:
  LOAD the value from a data memory address into a register
Description:
  Load the contents of a data memory cell into a register. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
N BYTE 3 ; this is stored at address 0
array BYTE 4, 7, 1 ; this is stored at addresses 1, 2, 3
.code
LOAD C, [array+2] ; +2 is an optional offset constant
1 | 0 | 0 | 0 | 1 | 0 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Instruction Layout:

## Slide 143: LOADF
Instruction Layout:
Full name:
  LOAD but with an oFfset specified by another register
Description:
  Load the contents of a data memory cell into a register. The address of the cell is specified by a label plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address from which the value is loaded.
Assembly Example:
.data
N BYTE 3 ; this is stored at address 0
array BYTE 4, 7, 1 ; this is stored at addresses 1, 2, 3
.code
LOADI B, 1
LOADF C, [array + B] ; this will load into C the value 7
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 144: LOADF
Instruction Layout:
Full name:
  LOAD but with an oFfset specified by another register
Description:
  Load the contents of a data memory cell into a register. The address of the cell is specified by a label plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address from which the value is loaded.
Assembly Example:
.data
N BYTE 3 ; this is stored at address 0
array BYTE 4, 7, 1 ; this is stored at addresses 1, 2, 3
.code
LOADI B, 1
LOADF C, [array + B + 1] ; this will load into C the value 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0

## Slide 146: STORE
Full name:
  STORE a register value into a data memory location
Description:
  Store the value of a register into a data memory cell. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
N BYTE 3 ; this is stored at address 0
array BYTE 4, 7, 1 ; this is stored at addresses 1, 2, 3
.code
LOADI D, 5 ; set register D to 5
STORE [array], D ; this will replace the 4 with 5 in array
1 | 0 | 1 | 0 | 1 | 1 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Instruction Layout:

## Slide 147: STORE
Full name:
  STORE a register value into a data memory location
Description:
  Store the value of a register into a data memory cell. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
N BYTE 3 ; this is stored at address 0
array BYTE 4, 7, 1 ; this is stored at addresses 1, 2, 3
.code
LOADI D, 5 ; set register D to 5
STORE [array+2], D ; this will replace the 1 with 5 in array
1 | 0 | 1 | 0 | 1 | 1 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Instruction Layout:

## Slide 149: STOREF
Full name:
  STORE but with an oFfset specified by another register
Description:
  Store the value of a register into a data memory cell. The address of the cell is specified by a label plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address at which the value is stored.
Assembly Example:
.data
array BYTE 4, 7, 8 ; this is stored at addresses 0, 1, 2
.code
LOADI B, 1 ; register B is set to 1
LOADI D, 6 ; register D is set to 6
STOREF [array + B], D ; this will replace the 7 with 6 in array
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 150: STOREF
Full name:
  STORE but with an oFfset specified by another register
Description:
  Store the value of a register into a data memory cell. The address of the cell is specified by a label plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address at which the value is stored.
Assembly Example:
.data
array BYTE 4, 7, 8 ; this is stored at addresses 0, 1, 2
.code
LOADI B, 1 ; register B is set to 1
LOADI D, 6 ; register D is set to 6
STOREF [array + B +1], D ; this will replace the 8 with 6 in array
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Instruction Layout:

## Slide 152
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 153
These 16 switches are used for input into the Code Memory.

## Slide 154
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0

## Slide 155
These 8 switches are used for input into the Data Memory.

## Slide 156
0 1 0 0 0 0 0 0

## Slide 157: INPUTC
Full name:
  INPUT into Code memory
Description:
  Read a 16-bit value (from switches SW15-SW0) and store it in the code memory at the given address. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
zero BYTE ? ; this is stored at address 0 in DMEM
.code
INPUTC [zero] ; store the value @ address 0 in the CMEM
; Hack to get around a compiler issue.
; Currently the CMEM address can only be
; given as a label to a DMEM location.
0 | 0 | 0 | 1 | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 158: INPUTC
Full name:
  INPUT into Code memory
Description:
  Read a 16-bit value (from switches SW15-SW0) and store it in the code memory at the given address. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
zero BYTE ? ; this is stored at address 0 in DMEM
.code
INPUTC [zero+32] ; store the value @ address 32 in the CMEM
; Hack to get around a compiler issue.
; Currently the CMEM address can only be
; given as a label to a DMEM location.
0 | 0 | 0 | 1 | d | d | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 160: INPUTCF
Full name:
  INPUT into Code memory with oFfset
Description:
  Read a 16-bit value (from switches SW15-SW0) and store it in the code memory at the given address. The address is specified by a label plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address at which the value is stored.
Assembly Example:
.data
zero BYTE ? ; this is stored at address 0 in DMEM
.code
LOADI D, 5
INPUTCF [zero + D] ; store the value @ address 5 in the CMEM
0 | 0 | 0 | 1 | d | d | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 161: INPUTCF
Full name:
  INPUT into Code memory with oFfset
Description:
  Read a 16-bit value (from switches SW15-SW0) and store it in the code memory at the given address. The address is specified by a label plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address at which the value is stored.
Assembly Example:
.data
zero BYTE ? ; this is stored at address 0 in DMEM
.code
LOADI D, 5
INPUTCF [zero + D + 32] ; store @ address 37 in the CMEM
0 | 0 | 0 | 1 | d | d | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Instruction Layout:

## Slide 163: INPUTD
Full name:
  INPUT into Data memory
Description:
  Read an 8-bit value (from switches SW7-SW0) and store it in the data memory at the given address. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
M BYTE 1 ; this is stored at address 0 in DMEM
N BYTE ? ; this is at address 1 in DMEM
.code
INPUTD [N] ; store the value @ address 1 in the DMEM
0 | 0 | 0 | 1 | d | d | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Instruction Layout:

## Slide 164: INPUTD
Full name:
  INPUT into Data memory
Description:
  Read an 8-bit value (from switches SW7-SW0) and store it in the data memory at the given address. The address is specified by the label for that memory location, surrounded by square brackets. The compiler computes the address and stores it in the last 8 bits of the instruction.
Assembly Example:
.data
M BYTE 1 ; this is stored at address 0 in DMEM
X BYTE ?,?,? ; this is at addresses 1, 2, 3 in DMEM
.code
INPUTD [X+2] ; store the value @ address 3 in the DMEM
0 | 0 | 0 | 1 | d | d | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Instruction Layout:

## Slide 166: INPUTDF
Full name:
  INPUT into Data memory with oFfset
Description:
  Read an 8-bit value (from switches SW7-SW0) and store it in the data memory at the given address. The address is specified by the label for that memory location plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address at which the value from the switches is stored.
Assembly Example:
.data
M BYTE 1 ; this is stored at address 0 in DMEM
X BYTE ?,?,?,? ; this is at addresses 1, 2, 3, 4 in DMEM
.code
LOADI B, 2
INPUTDF [X + B] ; store the value @ address 3 in the DMEM
0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Instruction Layout:

## Slide 167: INPUTDF
Full name:
  INPUT into Data memory with oFfset
Description:
  Read an 8-bit value (from switches SW7-SW0) and store it in the data memory at the given address. The address is specified by the label for that memory location plus an offset value stored in a register, surrounded by square brackets. The compiler computes the address of the label and stores it in the last 8 bits of the instruction. The offset is added at runtime to compute the effective address at which the value from the switches is stored.
Assembly Example:
.data
M BYTE 1 ; this is stored at address 0 in DMEM
X BYTE ?,?,?,? ; this is at addresses 1, 2, 3, 4 in DMEM
.code
LOADI B, 2
INPUTDF [X + B + 1] ; store the value @ address 4 in the DMEM
0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Instruction Layout:

## Slide 168: How many unique assembly instructions are there? (examples for some of the instructions)

## Slide 169: There is only one NOOP instruction
NOOP

## Slide 170: There is only one NOOP instruction
0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d | d | d | d | d
NOOP
Because these 12 bits are don’t cares, however, there are 212 = 4096 possible ways to map the
assembly instruction NOOP to machine language.
The hardware ignores the don’t care bits.
So, any one of these 4096 mappings leads to
a valid machine language command.
The compiler, however, maps all d bits to zero.
Thus, mapping NOOP to 16 zeros.

## Slide 171: There are 4096 ways to map the assembly NOOP instruction to machine language
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
. . .
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 172: The compiler from assembly to machine language uses only this one by default
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
. . .
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 173: There are 16 possible ADD instructions
ADD B, D
ADD B, C
ADD B, B
ADD B, A
ADD A, D
ADD A, C
ADD A, B
ADD A, A
ADD D, D
ADD D, C
ADD D, B
ADD D, A
ADD C, D
ADD C, C
ADD C, B
ADD C, A

## Slide 174: There are 16 possible ADD instructions
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | d | d | d | d | d | d | d | d
ADD B, D
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
ADD B, C
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | d | d | d | d | d | d | d | d
ADD B, B
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | d | d | d | d | d | d | d | d
ADD B, A
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | d | d | d | d | d | d | d | d
ADD A, D
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
ADD A, C
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | d | d | d | d | d | d | d | d
ADD A, B
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d
ADD A, A

## Slide 175: There are 16 possible ADD instructions
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | d | d | d | d | d | d | d | d
ADD D, D
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
ADD D, C
0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | d | d | d | d | d | d | d | d
ADD D, B
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | d | d | d | d | d | d | d | d
ADD D, A
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | d | d | d | d | d | d | d | d
ADD C, D
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
ADD C, C
0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | d | d | d | d | d | d | d | d
ADD C, B
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | d | d | d | d | d | d | d | d
ADD C, A

## Slide 176: The last 8 bits could be set to anything
0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | d | d | d | d | d | d | d | d
ADD C, D
Because these 8 bits are don’t cares, however, there are 28 = 256 possible ways to map the
assembly instruction ADD C,D to machine language.
The hardware ignores the don’t care bits.
So any one of these 256 mappings leads to
a valid machine language command.
The compiler, however, maps all d bits to zero.

## Slide 177: There are 16 possible SUB instructions
SUB B, D
SUB B, C
SUB B, B
SUB B, A
SUB A, D
SUB A, C
SUB A, B
SUB A, A
SUB D, D
SUB D, C
SUB D, B
SUB D, A
SUB C, D
SUB C, C
SUB C, B
SUB C, A

## Slide 178: There are 16 possible SUB instructions
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | d | d | d | d | d | d | d | d
SUB B, D
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
SUB B, C
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | d | d | d | d | d | d | d | d
SUB B, B
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | d | d | d | d | d | d | d | d
SUB B, A
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | d | d | d | d | d | d | d | d
SUB A, D
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
SUB A, C
0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | d | d | d | d | d | d | d | d
SUB A, B
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d
SUB A, A

## Slide 179: There are 16 possible SUB instructions
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | d | d | d | d | d | d | d | d
SUB D, D
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | d | d | d | d | d | d | d | d
SUB D, C
0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | d | d | d | d | d | d | d | d
SUB D, B
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | d | d | d | d | d | d | d | d
SUB D, A
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | d | d | d | d | d | d | d | d
SUB C, D
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | d | d | d | d | d | d | d | d
SUB C, C
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | d | d | d | d | d | d | d | d
SUB C, B
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | d | d | d | d | d | d | d | d
SUB C, A

## Slide 180: There are 4 possible SHIFTL instructions
SHIFTL D
SHIFTL C
SHIFTL B
SHIFTL A

## Slide 181: There are 4 possible SHIFTL instructions
1 | 1 | 0 | 0 | 0 | 0 | d | 0 | d | d | d | d | d | d | d | d
SHIFTL A
1 | 1 | 0 | 0 | 0 | 1 | d | 0 | d | d | d | d | d | d | d | d
SHIFTL B
1 | 1 | 0 | 0 | 1 | 0 | d | 0 | d | d | d | d | d | d | d | d
SHIFTL C
1 | 1 | 0 | 0 | 1 | 1 | d | 0 | d | d | d | d | d | d | d | d
SHIFTL D

## Slide 182: There are 4 possible SHIFTL instructions
1 | 1 | 0 | 0 | 0 | 1 | d | 0 | d | d | d | d | d | d | d | d
SHIFTL B
Because these 9 bits are don’t cares, however, there are 29 = 512 possible ways to map the
assembly instruction SHIFTL B to machine language.
The hardware ignores the don’t care bits.
So, any one of these 512 mappings leads to
a valid machine language command.
The compiler, however, maps all d bits to zero.

## Slide 183: There are 4 possible SHIFTR instructions
SHIFTR D
SHIFTR C
SHIFTR B
SHIFTR A

## Slide 184: There are 4 possible SHIFTR instructions
1 | 1 | 0 | 0 | 0 | 0 | d | 1 | d | d | d | d | d | d | d | d
SHIFTR A
1 | 1 | 0 | 0 | 0 | 1 | d | 1 | d | d | d | d | d | d | d | d
SHIFTR B
1 | 1 | 0 | 0 | 1 | 0 | d | 1 | d | d | d | d | d | d | d | d
SHIFTR C
1 | 1 | 0 | 0 | 1 | 1 | d | 1 | d | d | d | d | d | d | d | d
SHIFTR D

## Slide 185: There are many possible JUMP instructions (at the assembly language level)
JUMP End
JUMP OuterLoop
JUMP InnerLoop
JUMP Start
The second word must be an unique label. The number of possible commands
depends on the maximum length of the label supported by the compiler.

## Slide 186: There are many possible JUMP instructions
1 | 1 | 1 | 0 | d | d | d | d | P | C | O | F | F | S | E | T
JUMP Label

## Slide 187: There are many possible JUMP instructions
1 | 1 | 1 | 0 | d | d | d | d | P | C | O | F | F | S | E | T
JUMP Label
These 8 bits specify an offset for the program counter (PC).
The offset is encoded in 2’s complement representation
and can be either positive or negative.

## Slide 188: There are many possible JUMP instructions
1 | 1 | 1 | 0 | d | d | d | d | d | d | O | F | F | S | E | T
JUMP Label
Because the code memory of the i281 CPU has space for only
64 instructions, however, the hardware uses only the last 6 bits.
That is, it uses 6-bit adders to compute addresses.
Therefore, the possible range of offset values ranges from -32 to +31.
However, due to an implicit +1 offset implemented by the hardware
in the PC update logic, the actual effective range is -31 to +32.
The compiler emits 6-bit numbers that are then sign extended to 8-bit.

## Slide 189
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 190
i281 CPU
6
6
16
16
8 high
6 low
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6-bit adder
6-bit adder
1
0
6
6
6
c3
100000
PC
c2
6
6
6
6
6
6
0 0 0 0 0 1
Clock
Clock
c0
The implicit +1 comes from here.
More about this later.
c0
The offset comes from here (last 6 bits).

## Slide 191: Possible Offsets with +1 Correction
i281 CPU

## Slide 192: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 193: Quick Review: Decoders

## Slide 194
w
0
y
0
y
1
En
1-to- 2 decoder

## Slide 195
1-to- 2 decoder
En
1-to-2 decoder
w0
y0
y1

## Slide 196
[ Figure 4.14c from the textbook ]
En
2-to- 4 decoder

## Slide 197
2-to- 4 decoder
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3

## Slide 198
4-to-16 decoder built using a decoder tree
[ Figure 4.16 from the textbook ]
w
0
En
y
0
w
1
y
1
y
2
y
3
y
8
y
9
y
10
y
11
w
2
w
0
y
0
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
w
0
En
y
0
w
1
y
1
y
2
y
3
y
4
y
5
y
6
y
7
w
1
w
0
En
y
0
w
1
y
1
y
2
y
3
y
12
y
13
y
14
y
15
w
0
En
y
0
w
1
y
1
y
2
y
3
w
3
En
w

## Slide 199
4-to-16 decoder
En
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15

## Slide 200
4-to-16 decoder
En
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
The outputs are
one-hot encoded
when En=1

## Slide 201: OPCODE Decoding Circuit

## Slide 202
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
The OpCode Decoder

## Slide 203
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
2
2
ADDR/VAL/OFFSET
RY
RX

## Slide 204
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0

## Slide 205
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15

## Slide 206
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
1
always enabled
En
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15

## Slide 207
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
1
En
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15

## Slide 208
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15

## Slide 209
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
INPUT??
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFT?
CMP
JUMP
BR??

## Slide 210
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
INPUT??
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFT?
CMP
JUMP
BR??
This represents
4 OPCODEs

## Slide 211
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFT?
CMP
JUMP
BR??
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF

## Slide 212
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFT?
CMP
JUMP
BR??
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF

## Slide 213
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFT?
CMP
JUMP
BR??
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
This represents
2 OPCODEs

## Slide 214
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
BR??
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1

## Slide 215
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
BR??
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
This represents
4 OPCODEs

## Slide 216
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1

## Slide 217
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
These 6 bits represent the OPCODEs

## Slide 218
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
These 6 bits represent the OPCODEs

## Slide 219
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
ADDR/VAL/OFFSET

## Slide 220
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
ADDR/VAL/OFFSET
RX
2

## Slide 221
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
ADDR/VAL/OFFSET
RX
2
These 2 bits
are shared

## Slide 222
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
2
2
ADDR/VAL/OFFSET
RY
RX
Sometimes
they encode
the register RY

## Slide 223
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
2
2
ADDR/VAL/OFFSET
RY
RX

## Slide 224
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
8
2
2
ADDR/VAL/OFFSET
RY
RX

## Slide 225: The OPCODE decoder outputs are one-hot encoded

## Slide 226
0 | 0 | 0 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
NOOP

## Slide 227
0 | 0 | 0 | 1 | ? | ? | 0 | 0 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
INPUTC

## Slide 228
0 | 0 | 0 | 1 | ? | ? | 0 | 1 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
INPUTCF

## Slide 229
0 | 0 | 0 | 1 | ? | ? | 1 | 0 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
INPUTD

## Slide 230
0 | 0 | 0 | 1 | ? | ? | 1 | 1 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
INPUTDF

## Slide 231
0 | 0 | 1 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
MOVE

## Slide 232
0 | 0 | 1 | 1 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
LOADI/LOADP

## Slide 233
0 | 1 | 0 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
ADD

## Slide 234
0 | 1 | 0 | 1 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
ADDI

## Slide 235
0 | 1 | 1 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
SUB

## Slide 236
0 | 1 | 1 | 1 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
SUBI

## Slide 237
1 | 0 | 0 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
LOAD

## Slide 238
1 | 0 | 0 | 1 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
LOADF

## Slide 239
1 | 0 | 1 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
STORE

## Slide 240
1 | 0 | 1 | 1 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
STOREF

## Slide 241
1 | 1 | 0 | 0 | ? | ? | ? | 0 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
1
0
SHIFTL

## Slide 242
1 | 1 | 0 | 0 | ? | ? | ? | 1 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
1
SHIFTR

## Slide 243
1 | 1 | 0 | 1 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
CMP

## Slide 244
1 | 1 | 1 | 0 | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
JUMP

## Slide 245
1 | 1 | 1 | 1 | ? | ? | 0 | 0 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
1
0
0
0
0
0
BRE/BRZ

## Slide 246
1 | 1 | 1 | 1 | ? | ? | 0 | 1 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
0
0
0
BRNE/BRNZ

## Slide 247
1 | 1 | 1 | 1 | ? | ? | 1 | 0 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
1
0
0
0
BRG

## Slide 248
1 | 1 | 1 | 1 | ? | ? | 1 | 1 | ? | ? | ? | ? | ? | ? | ? | ?
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
1
0
0
BRGE

## Slide 250
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8 | I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0
8
2
2
ADDR/VAL/OFFSET
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1

## Slide 251
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8 | I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0
8
2
2
ADDR/VAL/OFFSET
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
The second instruction byte
is NOT routed through
the OPCODE decoder.

## Slide 252
2
2
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 253
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 254
2
2
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
These 4 bits
pass through,
but don’t go
through the
decoder tree.
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 255
2
2
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 256
Y0
Y1
X0
X1
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
These are their
names used in the
hardware design.
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 257
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 258
En
1
OPCODE decoder
w4
w7
w6
w5
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFTL
SHIFTR
CMP
JUMP
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
X1
X0
Y1
Y0
y16
y17
y18
y19
y20
y21
y22
y23
y24
y25
y26
w0
w3
w2
w1
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 259
En
1
OPCODE decoder
w4
w7
w6
w5
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFTL
SHIFTR
CMP
JUMP
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
X1
X0
Y1
Y0
y16
y17
y18
y19
y20
y21
y22
y23
y24
y25
y26
w0
w3
w2
w1
23 one-hot
encoded
outputs
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 260
En
1
OPCODE decoder
w4
w7
w6
w5
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
INPUTC
INPUTCF
INPUTD
INPUTDF
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
SHIFTL
SHIFTR
CMP
JUMP
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
X1
X0
Y1
Y0
y16
y17
y18
y19
y20
y21
y22
y23
y24
y25
y26
w0
w3
w2
w1
These 4 are NOT
one-hot encoded
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8

## Slide 261
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
23 + 4

## Slide 262: The Control Table

## Slide 264
23 one-hot
encoded
OPCODEs

## Slide 265
23 one-hot
encoded
OPCODEs
18 control lines

## Slide 266
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
X1 X0
Taken from
these bits of the
instruction

## Slide 267
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
X1 X0
Taken from
these bits of the
instruction

## Slide 268
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
Y1 Y0
Taken from
these bits of the
instruction

## Slide 269
C15 | C14 | C13 | C12 | C11 | C10 | C9 | C8 | C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
Y1 Y0
Taken from
these bits of the
instruction

## Slide 271
computed using
the flags register
Zero Flag (ZF)
Negative Flag (NF)
Overflow Flag (OF)

## Slide 272: Sample Assembly Programs for the i281 CPU

## Slide 273: The OPCODEs
( Mapped to Machine Language )

## Slide 274: The OPCODEs
0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d | d | d | d | d
NOOP
0 | 0 | 0 | 1 | d | d | 0 | 0 | C | A | D | D | R | E | S | S
INPUTC
0 | 0 | 0 | 1 | R | X | 0 | 1 | C | A | D | D | R | E | S | S
INPUTCF
0 | 0 | 0 | 1 | d | d | 1 | 0 | D | A | D | D | R | E | S | S
INPUTD
0 | 0 | 0 | 1 | R | X | 1 | 1 | D | A | D | D | R | E | S | S
INPUTDF
0 | 0 | 1 | 0 | R | X | R | Y | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
MOVE
0 | 0 | 1 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
LOADI/LOADP

## Slide 275: The OPCODEs
0 | 1 | 0 | 0 | R | X | R | Y | d | d | d | d | d | d | d | d
ADD
0 | 1 | 0 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
ADDI
0 | 1 | 1 | 0 | R | X | R | Y | d | d | d | d | d | d | d | d
SUB
0 | 1 | 1 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
SUBI
1 | 0 | 0 | 0 | R | X | d | d | D | A | D | D | R | E | S | S
LOAD
1 | 0 | 0 | 1 | R | X | R | Y | D | A | D | D | R | E | S | S
LOADF
1 | 0 | 1 | 0 | R | X | d | d | D | A | D | D | R | E | S | S
STORE
1 | 0 | 1 | 1 | R | X | R | Y | D | A | D | D | R | E | S | S
STOREF

## Slide 276: The OPCODEs
1 | 1 | 0 | 0 | R | X | d | 0 | d | d | d | d | d | d | d | d
SHIFTL
1 | 1 | 0 | 0 | R | X | d | 1 | d | d | d | d | d | d | d | d
SHIFTR
1 | 1 | 0 | 1 | R | X | R | Y | d | d | d | d | d | d | d | d
CMP
1 | 1 | 1 | 0 | d | d | d | d | P | C | O | F | F | S | E | T
JUMP
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
BRE/BRZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
BRNE/BRNZ
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
BRG
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
BRGE

## Slide 277: Do Loop

## Slide 278: C Version
// Add the numbers from 1 to 5 using a do loop.
int N=5;
int main()
{
int i, sum;
i=0;
sum=0;
do
{
i++;
sum+=i;
}while( i < N );
}

## Slide 279: Assembly Version
; Add the numbers from 1 to 5 using a do loop.
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0 ; i = 0
LOADI B, 0 ; sum=0
LOAD D, [N] ; register D = N
Do: ADDI A, 1 ; i++
ADD B, A ; sum+=i
CMP D, A ; N > i ? (register ordering is swapped)
BRG Do ; if true, jump to Do
End: STORE [sum], B ; store sum to memory
; Register allocation:
; A: i (the variable i is optimized to register A)
; B: sum
; C: <not used>
; D: N

## Slide 280: Machine Code Version
Data Memory:
00000101
00000000
Code Memory:
0011000000000000
0011010000000000
1000110000000000
0101000000000001
0100010000000000
1101110000000000
1111001011111100
1010010000000001

## Slide 281: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011000000000000
0011010000000000
1000110000000000
0101000000000001
0100010000000000
1101110000000000
1111001011111100
1010010000000001

## Slide 282: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
00110000_00000000
00110100_00000000
10001100_00000000
01010000_00000001
01000100_00000000
11011100_00000000
11110010_11111100
10100100_00000001

## Slide 283: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 284: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 285: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 286: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 287: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 288: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 289: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 290: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_dd_00000000
0011_01_dd_00000000
1000_11_dd_00000000
0101_00_dd_00000001
0100_01_00_dddddddd
1101_11_00_dddddddd
1111_dd_10_11111100
1010_01_dd_00000001

## Slide 291: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 292: Bubble Sort

## Slide 293: C Version
int array[] = {7, 3, 2, 1, 6, 4, 5, 8};
int last = 7; // last valid index in the array
int temp;
int i, j;
int main()
{
for (i = 0; i < last; i++)
for (j = 0; j < last-i; j++)
if (array[j] > array[j+1]){
temp = array[j];
array[j] = array[j+1];
array[j+1] = temp;
}
//for(i = 0; i < N; i++){
// printf("%d, ", array[i]);
//}
}

## Slide 294: C Version
int array[] = {7, 3, 2, 1, 6, 4, 5, 8};
int last = 7; // last valid index in the array
int temp;
int i, j;
int main()
{
for (i = 0; i < last; i++)
for (j = 0; j < last-i; j++)
if (array[j] > array[j+1]){
temp = array[j];
array[j] = array[j+1];
array[j+1] = temp;
}
//for(i = 0; i < N; i++){
// printf("%d, ", array[i]);
//}
}

## Slide 295: Assembly Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0 ; i = 0;
Outer: LOAD D, [last] ; Load last into D
LOADI B, 0 ; j = 0;
CMP A, D ; i < last
BRGE End ; If i >= last break out of the outer loop
Inner: LOAD D, [last] ; Re-Load last into D (this register is shared)
SUB D, A ; D = D - A (i.e., D = last - i)
CMP B, D ; j < last - i
BRGE Iinc ; If j >= last-i branch to Iinc
If: LOADF C, [array+B] ; C = array[j]
LOADF D, [array+B+1] ; D = array[j+1] (compiler adds 1 to addr. of array)
CMP D, C ; if array[j+1] < array[j] (switched direction)
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1 ; j++
JUMP Inner
Iinc: ADDI A, 1 ; i++
JUMP Outer
End: NOOP ; Do nothing
; Register allocation:
; A: i
; B: j
; C: array[j]
; D: last, array[j+1]
; Notes: i and j are optimized away. They exist only in registers, not in the main memory.

## Slide 296: Assembly Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0 ; i = 0;
Outer: LOAD D, [last] ; Load last into D
LOADI B, 0 ; j = 0;
CMP A, D ; i < last
BRGE End ; If i >= last break out of the outer loop
Inner: LOAD D, [last] ; Re-Load last into D (this register is shared)
SUB D, A ; D = D - A (i.e., D = last - i)
CMP B, D ; j < last - i
BRGE Iinc ; If j >= last-i branch to Iinc
If: LOADF C, [array+B] ; C = array[j]
LOADF D, [array+B+1] ; D = array[j+1] (compiler adds 1 to addr. of array)
CMP D, C ; if array[j+1] < array[j] (switched direction)
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1 ; j++
JUMP Inner
Iinc: ADDI A, 1 ; i++
JUMP Outer
End: NOOP ; Do nothing
; Register allocation:
; A: i
; B: j
; C: array[j]
; D: last, array[j+1]
; Notes: i and j are optimized away. They exist only in registers, not in the main memory.

## Slide 298: Machine Code Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 299: Machine Code Version
Data Memory:
00000111
00000011
00000010
00000001
00000110
00000100
00000101
00001000
00000111
00000000
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 300: Machine Code Version
Data Memory:
00000111 //array[0]
00000011 //array[1]
00000010 //array[2]
00000001 //array[3]
00000110 //array[4]
00000100 //array[5]
00000101 //array[6]
00001000 //array[7]
00000111 //last
00000000 //temp
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 301: Machine Code Version
Data Memory:
00000111 //array[0]
00000011 //array[1]
00000010 //array[2]
00000001 //array[3]
00000110 //array[4]
00000100 //array[5]
00000101 //array[6]
00001000 //array[7]
00000111 //last
00000000 //temp
Address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 302: Machine Code Version
Data Memory:
00000111 //array[0]
00000011 //array[1]
00000010 //array[2]
00000001 //array[3]
00000110 //array[4]
00000100 //array[5]
00000101 //array[6]
00001000 //array[7]
00000111 //last
00000000 //temp
00000000
00000000
00000000
00000000
00000000
00000000
Address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 303: Machine Code Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 304: Machine Code Version
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 305: Machine Code Version
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
Address
100000
100001
100010
100011
100100
100101
100110
100111
101000
101001
101010
101011
101100
101101
101110
101111
110000
110001
110010
110011
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 306: Machine Code Version
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
0000000000000000
. . .
0000000000000000
0000000000000000
Address
100000
100001
100010
100011
100100
100101
100110
100111
101000
101001
101010
101011
101100
101101
101110
101111
110000
110001
110010
110011
110100
. . .
111110
111111
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 308: Assembly v.s. Machine Code
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 309: Assembly v.s. Machine Code
Code Memory:
00110000_00000000
10001100_00001000
00110100_00000000
11010011_00000000
11110011_00001110
10001100_00001000
01101100_00000000
11010111_00000000
11110011_00001000
10011001_00000000
10011101_00000001
11011110_00000000
11110011_00000010
10111101_00000000
10111001_00000001
01010100_00000001
11100000_11110100
01010000_00000001
11100000_11101110
00000000_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 310: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 311: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 312: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 313: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 314: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 315: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 316: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 317: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 318: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 319: Assembly v.s. Machine Code
Code Memory:
0011_00_dd_00000000
1000_11_dd_00001000
0011_01_dd_00000000
1101_00_11_dddddddd
1111_dd_11_00001110
1000_11_dd_00001000
0110_11_00_dddddddd
1101_01_11_dddddddd
1111_dd_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_dddddddd
1111_dd_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_dd_00000001
1110_dd_dd_11110100
0101_00_dd_00000001
1110_dd_dd_11101110
0000_dd_dd_dddddddd
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 320: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 321: Questions?

## Slide 322: THE END