## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2
Latches
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW 7 is due on Monday (Oct 20) @ 10pm
Midterm grades submitted to the registrar’s office

## Slide 4: Administrative Stuff
Midterm 2 is in two weeks
Sample exams are posted on the class web page

## Slide 5: Administrative Stuff
Midterm Exam #2
When: Friday October 31 @ 4:20pm.
Where: This room
What: Chapters 1, 2, 3, 4 and 5
The exam will be closed book but open notes (you can bring up to 3 sheets of handwritten notes).

## Slide 6
Chapter 5

## Slide 7
Memory
element
Alarm
Sensor
Reset
Set
On
Off
¤
[ Figure 5.1 from the textbook ]
Control of an alarm system

## Slide 8: Motivation
So far, our circuits have been converting inputs to outputs without storing any data.
To do more advanced things (e.g., to build computers) we need components that can store data.
Can we make a component that “remembers” using the components that we know already?

## Slide 9
A
B
[ Figure 5.2 from the textbook ]
A simple memory element

## Slide 10
A simple memory element with NOT Gates
x
x
x
_

## Slide 11
A simple memory element with NOT Gates
1
x
x
_

## Slide 12
A simple memory element with NOT Gates
1
x
0

## Slide 13
A simple memory element with NOT Gates
1
1
0
The circuit will stay in this state indefinitely.

## Slide 14
A simple memory element with NOT Gates
0
x
x
_

## Slide 15
A simple memory element with NOT Gates
0
x
1

## Slide 16
A simple memory element with NOT Gates
0
1
0
The circuit will stay in this state indefinitely.

## Slide 17
A Strange Loop
[http://animalsiadmire.blogspot.com/2011/07/stupid-snake-eating-itself.html]

## Slide 18
This circuit can be in two possible states
0
1
0
1
1
0

## Slide 19
This circuit can be in two possible states
0
1
0
1
1
0
used to store a 1
used to store a 0
output
output

## Slide 20
This circuit can be in two possible states
0
1
0
1
1
0
output
output

## Slide 21: Building a NOT gate with a NAND gate
x
x
0
1
1
0
x
x | x | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
impossible
combinations
Thus, the two truth tables are equal!
x
_
x
x
_

## Slide 22
A simple memory element with NAND Gates
x
x
x
_

## Slide 23: Building a NOT gate with a NOR gate
x
x
0
1
1
0
x | x | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
impossible
combinations
Thus, the two truth tables are equal!
x
x
_
x
x
_

## Slide 24
A simple memory element with NOR Gates
x
x
x
_

## Slide 25
Basic Latch

## Slide 26: What is a latch?
http://luxuriahardware.com/images/detailed/13/P111408_m.jpg

## Slide 27
A simple memory element with NOR Gates

## Slide 28
A simple memory element with NOR Gates

## Slide 29
A simple memory element with NOR Gates
Reset
Set

## Slide 30
Reset
Set
Q
[ Figure 5.3 from the textbook ]
A memory element with NOR gates

## Slide 31
[ Figure 5.3 & 5.4 from the textbook ]
Two Different Ways to Draw the Same Circuit

## Slide 32
[ Figure 5.3 & 5.4 from the textbook ]
Two Different Ways to Draw the Same Circuit
a
b
Q
R
S

## Slide 33
Before We Analyze the Basic Latch
Let's Look at Two Simpler
Examples with Feedback

## Slide 34
Let’s Try to Analyze This Circuit
x
f

## Slide 35
Let’s Try to Analyze This Circuit
Control Line
Data Line
x
f

## Slide 36
Let’s Try to Analyze This Circuit
x | ft | ft+1
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
ft+1
ft
x

## Slide 37
Let’s Try to Analyze This Circuit
x | ft | ft+1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
ft+1
ft
x

## Slide 38
Let’s Try to Analyze This Circuit
x | ft | ft+1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
ft
ft+1
ft
x

## Slide 39
Let’s Try to Analyze This Circuit
x | ft | ft+1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
ft
If x = 0, then f is negated.
If x = 1, then f is driven to 0.
ft+1
ft
x

## Slide 40
If a NOR’s control line is 0, then that NOR just negates its data line. If the control line is 1, then the NOR's output is driven to 0, ignoring its data line.
Key Observation
f
x

## Slide 41
Let’s Try to Analyze This Circuit
x
g

## Slide 42
Let’s Try to Analyze This Circuit
x | gt | gt+1
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
gt+1
gt
x

## Slide 43
Let’s Try to Analyze This Circuit
x | gt | gt+1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
gt+1
gt
x

## Slide 44
Let’s Try to Analyze This Circuit
x | gt | gt+1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
If x = 0, then g is driven to one.
If x = 1, then g is negated.
1
gt
gt+1
gt
x

## Slide 45
If a NAND’s control line is 1, then that NAND just negates its data line. If the control line is 0, then the NAND's output is driven to 1, ignoring its data line.
Key Observation
x
g

## Slide 46
Output Oscillations
What would happen to g if we keep x=1 for a long time?
x
g

## Slide 47
Output Oscillations
What would happen to g if we keep x=1 for a long time?
1
0
Time
x
g

## Slide 48
Output Oscillations
What would happen to g if we keep x=1 for a long time?
1
0
Time
tpd
tpd
tpd is the propagation delay through the NAND gate,
which is small, but not zero.
x
g

## Slide 49
Back to the Basic Latch

## Slide 50
Q
[ Figure 5.3 from the textbook ]
The Basic Latch

## Slide 51
Q
[ Figure 5.3 from the textbook ]
The Basic Latch
Control Lines
Data Lines

## Slide 52
R
S
Qa
Analyzing The Basic Latch
S | Qa | Qb = NOR (S, Qa)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Qb
R | Qb | Qa = NOR (R, Qb)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 53
R
S
Qa
Analyzing The Basic Latch
S | Qa | Qb = NOR (S, Qa)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Qb
R | Qb | Qa = NOR (R, Qb)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 54
R
S
Qa
Analyzing The Basic Latch
S | Qa | Qb = NOR (S, Qa)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Qb
R | Qb | Qa = NOR (R, Qb)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Qa
0
Qb
0

## Slide 55
Analyzing The Basic Latch
R
S
Qa
Qb
S | Qb
0 | Qa
1 | 0
R | Qa
0 | Qb
1 | 0

## Slide 56
R
S
Q
Behavior of the Basic Latch
S | R | Qt+1
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 57
R
S
Q
Behavior of the Basic Latch
S | R | Qt+1
0 | 0 | Qt
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 58
Behavior of the Basic Latch
S | R | Qa(t+1) | Qb(t+1)
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
R
S
Qa
Qb

## Slide 59
Behavior of the Basic Latch
S | R | Qa(t+1) | Qb(t+1)
0 | 0 | Qa(t) | Qb(t)
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
R
S
Qa
Qb

## Slide 60
Behavior of the Basic Latch
S | R | Qa(t+1) | Qb(t+1)
0 | 0 | Qa(t) | Qb(t)
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
R
S
Qa
Qb
Latch
Reset
Set
Undesirable

## Slide 61
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Q
a
Q
b
R
S
(no change)
Circuit and Characteristic Table
[ Figure 5.4a,b from the textbook ]
x1 | x2 | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR Gate
NOR Gate Truth table

## Slide 62
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Q
a
Q
b
R
S
(no change)
Circuit and Characteristic Table
[ Figure 5.4a,b from the textbook ]
x1 | x2 | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR Gate
NOR Gate Truth table
A truth table should take the state into account.
A characteristic table takes only the inputs into account.

## Slide 63
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Q
a
Q
b
R
S
(no change)
Circuit and Characteristic Table
[ Figure 5.4a,b from the textbook ]
x1 | x2 | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR Gate
NOR Gate Truth table
Note that Qa and Qb are
inverses of each other!

## Slide 64: Oscillations and Undesirable States
When S=1 and R=1 both outputs of the latch are equal to 0, i.e., Qa=0 and Qb=0.
Thus, the two outputs are no longer complements of each other.
This is undesirable as many of the circuits that we will build later with these latches rely on the assumption that the two outputs are always complements of each other.
(This is obviously not the case for the basic latch, but we will patch it later to eliminate this problem).

## Slide 65: Oscillations and Undesirable States
An even bigger problem occurs when we transition from S=R=1 to S=R=0.
When S=R=1 we have Qa=Qb=0. After the transition to S=R=0, however, we get Qa=Qb=1, which would immediately cause Qa=Qb=0, and so on.
If the gate delays and the wire lengths are identical, then this oscillation will continue forever.
In practice, the oscillation dies down and the output settles into either Qa=1 and Qb=0 or Qa=0 and Qb=1.
The problem is that we can't predict which one of these two it will settle into.

## Slide 66
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]

## Slide 67
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]

## Slide 68
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates

## Slide 69
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
0
1
0
1

## Slide 70
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
0
1
0
1
1
0
0
1

## Slide 71
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
0
0
0
1
0
0
0
1

## Slide 72
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
0
0
0
1
0
0
0
1
1
0

## Slide 73
1
0
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
0
0
0
0
0
1
1
0

## Slide 74
1
0
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
1
0
0
1
0
1
1
0

## Slide 75
0
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
1
0
0
0
1
0
0
For a brief moment the latch
goes through the undesirable
state Qa=0 and Qb=0.
1
0

## Slide 76
0
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
1
0
0
0
1
0
0
0
0
But these zeros loop around ...

## Slide 77
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
1
0
1
0
0
1
1
0
... and set it to Qa=1 and Qb=0.
0
0

## Slide 78
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
1
0
1
0
0
1
1
0
0
1
The new values also loop around ...

## Slide 79
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
1
0
1
0
0
1
1
0
0
1
... but they leave the outputs the same.

## Slide 81
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]

## Slide 82
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
1
0
0
0
0
0
1
0

## Slide 83
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
1
0
1
0
1
0
1
0

## Slide 84
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
1
0
1
0
1
0
1
0
0
1

## Slide 85
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
0
0
1
0
1
0
0
0
0
1
For a brief moment the latch
goes through the undesirable
state Qa=0 and Qb=0.

## Slide 86
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
0
1
1
0
0
0
0
0
But these zeros loop around ...
0
0

## Slide 87
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
0
0
1
1
1
0
0
1
0
0
... and set it to Qa=0 and Qb=1.

## Slide 88
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
0
1
1
0
0
1
1
0
The new values also loop around ...
0
1

## Slide 89
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
(c) Timing diagram
0
1
1
0
0
1
1
0
... but they leave the outputs the same.
0
1

## Slide 91
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]

## Slide 92
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]
1
1

## Slide 93
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]
1
1
0
0

## Slide 94
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Characteristic table
Time
1
0
1
0
1
0
1
0
R
S
Q
a
Q
b
Q
a
Q
b
?
?
(c) Timing diagram
R
S
t
1
t
2
t
3
t
4
t
5
t
6
t
7
t
8
t
9
t
10
(no change)
Timing Diagram for the Basic Latch with NOR Gates
[ Figure 5.4 from the textbook ]
A transition from
S=R=1 to
S=R=0
causes oscillations
of the two output
values Qa and Qb.
1
1
0
0

## Slide 95
Basic Latch with NAND Gates

## Slide 96: Circuit for the Basic Latch with NAND Gates

## Slide 97: Basic Latch (with NOR Gates)
Basic Latch (with NAND Gates)
Notice that in the NAND case the two inputs are swapped and negated.
The labels of the outputs are the same in both cases.

## Slide 98: Basic Latch (with NOR Gates)
Basic Latch (with NAND Gates)
SR Latch
SR Latch

## Slide 99
(a) Circuit
(b) Characteristic table
(version 1)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
1
1
(no change)
Circuit and Characteristic Table
x1 | x2 | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND Gate
NAND Gate Truth table
Q
a
Q
b
S
R
(c) Characteristic table
(version 2)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
1
0
0
1
(no change)
1
1

## Slide 100: Basic Latch (with NOR Gates)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
1
1
(no change)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(no change)
Basic Latch (with NAND Gates)

## Slide 101: Basic Latch (with NOR Gates)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
1
1
(no change)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(no change)
Basic Latch (with NAND Gates)
Latch
Reset
Set
Undesirable
Latch
Reset
Set
Undesirable

## Slide 102: Basic Latch (with NOR Gates)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
1
1
(no change)
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
0
1
1
0
0
0
(no change)
Basic Latch (with NAND Gates)
Latch
Reset
Set
Undesirable
Latch
Reset
Set
Undesirable
The two characteristic tables are the same
(except for the last row, which is the undesirable configuration).

## Slide 103: Oscillations and Undesirable States
The basic latch with NAND gates also suffers form oscillation problems, similar to the basic latch implemented with NOR gates.
Try to do this analysis on your own.

## Slide 104
Gated SR Latch

## Slide 105: Motivation
The basic latch changes its state when the input signals change.
It is hard to control when these input signals will change and thus it is hard to know when the latch may change its state.
We want to have something like an Enable input.
In this case it is called the “Clock” input because it is desirable for the state changes to be synchronized

## Slide 106
[ Figure 5.5a from the textbook ]
Circuit Diagram for the Gated SR Latch

## Slide 107
Circuit Diagram for the Gated SR Latch
This is the “gate”
of the gated latch

## Slide 108
Circuit Diagram for the Gated SR Latch
This is the “snake”
of the gated latch

## Slide 109
Circuit Diagram for the Gated SR Latch
The outputs are complements of
each other

## Slide 110
[ Figure 5.5a-b from the textbook ]
Circuit Diagram and Characteristic Table
for the Gated SR Latch

## Slide 111
[ Figure 5.5a-b from the textbook ]
Circuit Diagram and Characteristic Table
for the Gated SR Latch
0
0
0
When Clk = 0 this circuit holds the previous output values,
regardless of the current inputs S and R because S’ and R’ are 0.

## Slide 112
[ Figure 5.5a-b from the textbook ]
Circuit Diagram and Characteristic Table
for the Gated SR Latch
1
When Clk = 1 this circuit behaves like a basic latch.
R
S

## Slide 113
[ Figure 5.5a-b from the textbook ]
Circuit Diagram and Characteristic Table
for the Gated SR Latch
1
R
S
When Clk = 1 this circuit behaves like a basic latch.
As if this part in gray were not even there.

## Slide 114
[ Figure 5.5a,c from the textbook ]
Circuit Diagram and Graphical Symbol
for the Gated SR Latch

## Slide 115
[ Figure 5.5c from the textbook ]
Timing Diagram for the Gated SR Latch

## Slide 116
[ Figure 5.5c from the textbook ]
Timing Diagram for the Gated SR Latch
The outputs Q and Q
cannot change
in these intervals.

## Slide 117
[ Figure 5.5c from the textbook ]
Timing Diagram for the Gated SR Latch
The outputs Q and Q
may change only
in these intervals.

## Slide 118
[ Figure 5.6 from the textbook ]
Gated SR latch with NAND gates
S
R
Clk
Q
Q

## Slide 119
Gated SR latch with NAND gates
In this case, the “gate” is constructed using NAND gates! Not AND gates.
S
R
Clk
Q
Q

## Slide 120
Gated SR latch with NAND gates
The “snake” is also constructed with NANDs.
S
R
Clk
Q
Q

## Slide 121
Gated SR latch with NAND gates
Also, notice that the positions of S and R are now swapped.
S
R
Clk
Q
Q

## Slide 122
Gated SR latch with NAND gates
S
R
Notice that when Clk=1 this turns into the
basic latch with NAND gates, i.e., the SR Latch.
1
1
S
R
Clk
Q
Q
1
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
1
0
0
1
(no change)
1
1

## Slide 123
Gated SR latch with NAND gates
1
1
When Clk=0 this circuit holds the previous output values.
0
0
S
R
Clk
Q
Q
0
S
R
Q
a
Q
b
0
0
0
1
1
0
1
1
0/1 1/0
1
0
0
1
(no change)
1
1

## Slide 124
S
R
Clk
Q
Q
Gated SR latch with NOR gates
Gated SR latch with NAND gates

## Slide 125
S
R
Clk
Q
Q
Gated SR latch with NOR gates
Gated SR latch with NAND gates
Graphical symbols are the same

## Slide 126
Gated SR latch with NOR gates
Gated SR latch with NAND gates
Characteristic tables are the same
(undesirable)
(undesirable)
S
R
Clk
Q
Q

## Slide 127
Gated D Latch

## Slide 128: Motivation
Dealing with two inputs (S and R) could be messy. For example, we may have to reset the latch before some operations in order to store a specific value but the reset may not be necessary depending on the current state of the latch.
Why not have just one input and call it D.
The D latch can be constructed using a simple modification of the SR latch.

## Slide 129
[ Figure 5.7a from the textbook ]
Circuit Diagram for the Gated D Latch

## Slide 130
[ Figure 5.7a from the textbook ]
Circuit Diagram for the Gated D Latch
This is the only
new thing here.

## Slide 131
[ Figure 5.7a,b from the textbook ]
Circuit Diagram and Characteristic Table
for the Gated D Latch
Note that it is now impossible to have S=R=1.

## Slide 132
[ Figure 5.7a,b from the textbook ]
Circuit Diagram and Characteristic Table
for the Gated D Latch
When Clk=1 the output follows the D input.
When Clk=0 the output cannot be changed.

## Slide 133
[ Figure 5.7a,c from the textbook ]
Circuit Diagram and Graphical Symbol
for the Gated D Latch

## Slide 134
[ Figure 5.7d from the textbook ]
Timing Diagram for the Gated D Latch

## Slide 135
t
su
t
h
Clk
D
Q
[ Figure 5.8 from the textbook ]
Setup and hold times
Setup time (tsu) – the minimum time that the D signal must be stable
prior to the negative edge of the Clock signal.
Hold time (th) – the minimum time that the D signal must remain stable
after the negative edge of the Clock signal.

## Slide 136
Circuit Diagram for the Gated D Latch
(with the latch implemented using NORs)
[https://en.wikibooks.org/wiki/Digital_Circuits/Latches]
Clk
S
R

## Slide 137
[https://en.wikibooks.org/wiki/Digital_Circuits/Latches]
Circuit Diagram for the Gated D Latch
(with the latch implemented using NORs)
[ Figure 5.7a from the textbook ]
Clk
S
R

## Slide 138
[https://en.wikibooks.org/wiki/Digital_Circuits/Latches]
Circuit Diagram for the Gated D Latch
(with the latch implemented using NORs)
[ Figure 5.7a from the textbook ]
Clk
S
R
The NOT gate is now in a different place.
Also, S and R are swapped.

## Slide 139
Some Practical Examples

## Slide 140
Different Types of Switches
http://www.industrial-electronics.com/Electricity-Refrigeration-Heating-Air-Conditioning_5b.html

## Slide 141
Different Types of Switches
http://www.industrial-electronics.com/Electricity-Refrigeration-Heating-Air-Conditioning_5b.html
If you are building a circuit with latches
you’ll need to use this type of switch.

## Slide 142
[http://electronicsclub.info/images/swabc.gif]
Single Pole, Double Throw = SPDT

## Slide 143
[http://www.cubisteffects.com/images/MIY/Pt3_Throw.jpg]
Single Pole, Double Throw = SPDT

## Slide 144
Single-pole—single-throw manual switch
http://www.industrial-electronics.com/Electricity-Refrigeration-Heating-Air-Conditioning_5b.html

## Slide 145
Double-pole—double-throw manual switch
http://www.industrial-electronics.com/Electricity-Refrigeration-Heating-Air-Conditioning_5b.html

## Slide 146: The following examples came from this book

## Slide 147
A Simple Circuit
[ Platt 2009 ]

## Slide 148
[ Platt 2009 ]
Let’s Take a Closer Look at This

## Slide 149
[ Platt 2009 ]
A Similar Example with NAND Gates

## Slide 150: Questions?

## Slide 151: THE END