## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2: The Intersection Between Hardware and Software
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
The FINAL exam is scheduled for
Wednesday Dec 17 @ 2:15 – 4:15 PM

## Slide 4: Final Exam Format
The exam will cover: Chapter 1 to Chapter 6, and Sections 7.1-7.2, register machines, and i281 CPU
Emphasis will be on Chapter 5, 6, and 7
The exam will be closed book but open notes.
You can bring up to 5 sheets of handwritten or typed notes.

## Slide 5: Final Exam Format
The exam will be out of 135 points
You need 95 points to get an A on this exam
It will be great if you can score more than 100 points.
  but you can’t roll over your extra points 

## Slide 6: Topics for the Final Exam
K-maps for 2, 3, and 4 variables
Multiplexers (circuits and function)
Synthesis of logic functions using multiplexers
Shannon’s Expansion Theorem
1’s complement and 2’s complement representation
Addition and subtraction of binary numbers
Circuits for adding and subtracting
Serial adder
Latches (circuits, behavior, timing diagrams)
Flip-Flops (circuits, behavior, timing diagrams)
Counters (up, down, synchronous, asynchronous)
Registers and Register Files

## Slide 7: Topics for the Final Exam
Synchronous Sequential Circuits
FSMs
Moore Machines
Mealy Machines
State diagrams, state tables, state-assigned tables
State minimization
Designing a counter
Arbiter Circuits
Reverse engineering a circuit
ASM Charts
Register Machines and programs for them
ALU, PC, and control for a simple processor (i281 CPU)
Assembly and machine language (i281 assembly)
Something from Star Wars

## Slide 8
Writing and Running a Program
C Program
Assembly
Program
Machine
Code
Run on the
Hardware

## Slide 9
Writing and Running a Program
C Program
Assembly
Program
Machine
Code
Run on the
Hardware
compiler
assembler
loader

## Slide 10
Writing and Running a Program
C Program
Assembly
Program
Machine
Code
Run on the
Hardware
compiler
assembler
loader
The programmer
only writes this
in a text editor.

## Slide 11
Writing and Running a Program
C Program
Assembly
Program
Machine
Code
Run on the
Hardware
compiler
assembler
loader
Nerds skip the
first step and
start here.

## Slide 12
Writing and Running a Program
C Program
Assembly
Program
Machine
Code
Run on the
Hardware
compiler
assembler
loader
CPU designers
start here.

## Slide 13: i281 Example: Add the numbers from 1 to 5

## Slide 14: i281 Example: Add the numbers from 1 to 5 C Language v.s. Assembly Language

## Slide 15: C Version
// C Version
//
// Add the numbers from 1 to 5 using a for loop.
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++)
sum+=i;
// printf("%d\n", sum);
}

## Slide 16: i281 Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; update the memory for sum
; Register allocation:
; A: i
; B: sum
; C: <not used>
; D: N

## Slide 17: i281 Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; update the memory for sum
; Register allocation:
; A: i
; B: sum
; C: <not used>
; D: N

## Slide 18: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 19: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 20: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 21: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 22: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 23: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=1

## Slide 24: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
Load the value of N into register D.
This has no analog in the C version,
which is written in a high-level language.
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 25: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 26: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 27: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 28: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 29: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=2

## Slide 30: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 31: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 32: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 33: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=3

## Slide 34: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 35: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 36: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 37: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=4

## Slide 38: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 39: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 40: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 41: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=5

## Slide 42: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 43: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 44: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 45: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
i=6

## Slide 46: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 47: i281 Example: Add the numbers from 1 to 5 Assembly Language v.s. Machine Language

## Slide 48: i281 Assembly Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; update the memory for sum

## Slide 49: i281 Assembly Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B

## Slide 50: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
0011010000000000
0011000000000001
1000110000000000
1101001100000000
1111001000000011
0100010000000000
0101000000000001
1110000011111011
1010010000000010
Machine Language

## Slide 51: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
0000 0101
0000 0000
0000 0000
Code Memory:
0011 0100 0000 0000
0011 0000 0000 0001
1000 1100 0000 0000
1101 0011 0000 0000
1111 0010 0000 0011
0100 0100 0000 0000
0101 0000 0000 0001
1110 0000 1111 1011
1010 0100 0000 0010
Machine Language
in Binary

## Slide 52: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
0 5
0 0
0 0
Code Memory:
3 4 0 0
3 0 0 1
8 C 0 0
D 3 0 0
F 2 0 3
4 4 0 0
5 0 0 1
E 0 F B
A 4 0 2
Machine Language
in Binary

## Slide 53: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
05
00
00
Code Memory:
34 00
30 01
8C 00
D3 00
F2 03
44 00
50 01
E0 FB
A4 02
Machine Language
in Hexadecimal

## Slide 54: i281 Example: Add the numbers from 1 to 5 Bit Mapping for OPCODEs

## Slide 55: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
0011010000000000
0011000000000001
1000110000000000
1101001100000000
1111001000000011
0100010000000000
0101000000000001
1110000011111011
1010010000000010
Machine Language

## Slide 56: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
00110100_00000000
00110000_00000001
10001100_00000000
11010011_00000000
11110010_00000011
01000100_00000000
01010000_00000001
11100000_11111011
10100100_00000010
Machine Language

## Slide 57: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Assembly Language
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010
Machine Language

## Slide 58: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 59: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 60: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 61: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 62: OPCODE Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 63: OPCODE Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 64: Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 65: Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 66: Second Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 67: Second Register Parameter Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 68: Value / Address / Offset Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 69: Value / Address / Offset Mapping
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 70: “Don’t care” bits …
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_dd_00000000
0011_00_dd_00000001
1000_11_dd_00000000
1101_00_11_dddddddd
1111_dd_10_00000011
0100_01_00_dddddddd
0101_00_dd_00000001
1110_dd_dd_11111011
1010_01_dd_00000010

## Slide 71: … are mapped to 0 by the Assembler
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 72: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 73: Loading the Program into Memory

## Slide 74
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 75
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
Write
Select
Read
Select
Read
Select
Write
Select
Write Enable
Write Enable
Write Enable
Write Enable
Write Enable
Write
Select
Port0 Read Select
Port1 Read Select
ALU Select
PC Mux
DMEM Input Mux
REG Writeback Mux
ALU Result Mux
ALU Source Mux
Input
Input
Input

## Slide 76
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 77
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 78
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 79
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 80
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 81
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 82: The CPU Control Logic

## Slide 83
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
The Control Logic

## Slide 84
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Control Signal #1

## Slide 85
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Control Signal #1

## Slide 86
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Control Signal #2

## Slide 87
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Control Signal #2

## Slide 88
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Control Signal #18

## Slide 89
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
Control Signal #18

## Slide 90
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
All Control Signals

## Slide 91
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
Write Enable
Write Enable
Write Enable
Write Enable
Write Enable
Write
Select
Port0 Read Select
Port1 Read Select
ALU Select
PC Mux
DMEM Input Mux
REG Writeback Mux
ALU Result Mux
ALU Source Mux

## Slide 92
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 93: The OPCODEs for this CPU
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 95
23 one-hot
encoded
OPCODEs
18 control lines
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18

## Slide 96
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18

## Slide 97: The Wiring Diagram for c11

## Slide 98
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18

## Slide 99: The Wiring Diagram for c12

## Slide 100
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18

## Slide 101: The Wiring Diagram for c13

## Slide 102
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18

## Slide 103
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
LOADI affects only
c3 , c8 , c9 , c10 , and c15
All others are set to zero.

## Slide 104
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
c8 and c9 depend
on the instruction and
the register that it uses.

## Slide 105
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
C8 | C9 | Register
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 106: Simulation of the Program Execution

## Slide 107: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum

## Slide 108: Mapping Assembly to Machine Code
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0
LOADI A, 1
LOAD D, [N]
Loop: CMP A, D
BRG End
Add: ADD B, A
ADDI A, 1
JUMP Loop
End: STORE [sum], B
Data Memory:
00000101
00000000
00000000
Code Memory:
0011_01_00_00000000
0011_00_00_00000001
1000_11_00_00000000
1101_00_11_00000000
1111_00_10_00000011
0100_01_00_00000000
0101_00_00_00000001
1110_00_00_11111011
1010_01_00_00000010

## Slide 109
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 110
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOADI B, 0

## Slide 111
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 0 1 1 0 0 0 0 1 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOADI B, 0 (equivalent to B=0)

## Slide 112
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 0 1 1 0 0 0 0 1 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOADI B, 0 (equivalent to B=0)

## Slide 113
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 0 1 1 0 0 0 0 1 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOADI B, 0 (equivalent to B=0)

## Slide 115
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 0 0 1 0 0 0 0 1 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100001
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOADI A, 1 (equivalent to A=1)

## Slide 117
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 1 1 1 0 0 0 0 1 0 0 1
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100010
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOAD D, [N] (D = contents of memory cell N)

## Slide 118
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 1 1 1 0 0 0 0 1 0 0 1
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100010
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
0000
0001
0010
0011
0100
0101
0110
0111
LOAD D, [N] (D = contents of memory cell N
at address 0000)

## Slide 119
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 1 1 1 0 0 0 0 1 0 0 1
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100010
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
LOAD D, [N]
0000
0001
0010
0011
0100
0101
0110
0111

## Slide 121
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
CMP A, D

## Slide 122
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
CMP A, D (compare A and D by subtraction)

## Slide 123
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
CMP A, D
00000001
00000101

## Slide 124
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
CMP A, D
SUB/CMP
1-5
00000001
00000101

## Slide 125
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
CMP A, D
SUB/CMP
set negative flag
1-5
00000001
00000101

## Slide 126
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
0
1
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
CMP A, D
SUB/CMP
set negative flag
1-5
0000
0001
0010
0011
0100
0101
0110
0111
this will
read out
address
1100
1100
11111100
00000001
00000101

## Slide 127
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
CMP A, D
SUB/CMP
set negative flag
1-5
0000
0001
0010
0011
0100
0101
0110
0111

## Slide 128
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
CMP A, D
SUB/CMP
set negative flag
1-5
0000
0001
0010
0011
0100
0101
0110
0111
write disabled
write disabled
write disabled

## Slide 129
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
CMP A, D
SUB/CMP
set negative flag
1-5

## Slide 130
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 1 1 0 0 0 0 1 1 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
CMP A, D
The only effect
of this operation

## Slide 132
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100100
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 1 0
c14
Flags
BRG End
branch not taken:
PC=PC+1
1
5

## Slide 133
c4
c5
A
B
C
D
00000110
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100100
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
BRG End
branch taken:
PC=PC+1+Offset
6
5

## Slide 135
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 1 0 0 0 1 1 0 1 0 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
ADD B, A (equivalent to B=B+A )

## Slide 136
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 1 0 0 0 1 1 0 1 0 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
00000000
00000001
1 0 (add)
00000001
ADD B, A (equivalent to B=B+A )

## Slide 137
c4
c5
A
B
C
D
00000001
A
00000000
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 1 0 0 0 1 1 0 1 0 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
00000000
00000001
1 0 (add)
00000001
ADD B, A (equivalent to B=B+A )

## Slide 138
c4
c5
A
B
C
D
00000001
A
00000001
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 1 0 0 0 1 1 0 1 0 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
ADD B, A (equivalent to B=B+A )
00000000
00000001
1 0 (add)
00000001

## Slide 139
c4
c5
A
B
C
D
00000001
A
00000001
B
00000000
C
00000101
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 1 0 1 0 0 0 1 1 0 1 0 1 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100011
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags
ADD B, A (equivalent to B=B+A )
00000000
00000001
1 0 (add)
00000001
set the flags

## Slide 140: For more examples try the i281 simulator

## Slide 141: i281 Simulator
To try the simulator, go to the class web page and follow the link.

## Slide 142: Questions?

## Slide 143: THE END