## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 2810: Digital Logic

## Slide 2: Assembly Examples
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Assembly Examples (for the i281 CPU)
CprE 2810: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 4
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 5
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 6
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
0 0 0 0
c14
Flags
Write
Select
Read
Select
Read
Select
Write
Select
Write Enable
Write Enable
Write Enable
Write Enable
Write Enable
Write
Select
Port0 Read Select
Port1 Read Select
ALU Select
PC Mux
DMEM Input Mux
REG Writeback Mux
ALU Result Mux
ALU Source Mux
Input
Input
Input

## Slide 7
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
0 0 0 0
c14
Flags

## Slide 8: The Assembly Language Instructions

## Slide 9: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 10: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 11: The OPCODEs
( Mapped to Machine Language )

## Slide 12: The OPCODEs
0 | 0 | 0 | 0 | d | d | d | d | d | d | d | d | d | d | d | d
NOOP
0 | 0 | 0 | 1 | d | d | 0 | 0 | C | A | D | D | R | E | S | S
INPUTC
0 | 0 | 0 | 1 | R | X | 0 | 1 | C | A | D | D | R | E | S | S
INPUTCF
0 | 0 | 0 | 1 | d | d | 1 | 0 | D | A | D | D | R | E | S | S
INPUTD
0 | 0 | 0 | 1 | R | X | 1 | 1 | D | A | D | D | R | E | S | S
INPUTDF
0 | 0 | 1 | 0 | R | X | R | Y | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
MOVE
0 | 0 | 1 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
LOADI/LOADP

## Slide 13: The OPCODEs
0 | 1 | 0 | 0 | R | X | R | Y | d | d | d | d | d | d | d | d
ADD
0 | 1 | 0 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
ADDI
0 | 1 | 1 | 0 | R | X | R | Y | d | d | d | d | d | d | d | d
SUB
0 | 1 | 1 | 1 | R | X | d | d | I | M | M | E | D | V | A | L
SUBI
1 | 0 | 0 | 0 | R | X | d | d | D | A | D | D | R | E | S | S
LOAD
1 | 0 | 0 | 1 | R | X | R | Y | D | A | D | D | R | E | S | S
LOADF
1 | 0 | 1 | 0 | R | X | d | d | D | A | D | D | R | E | S | S
STORE
1 | 0 | 1 | 1 | R | X | R | Y | D | A | D | D | R | E | S | S
STOREF

## Slide 14: The OPCODEs
1 | 1 | 0 | 0 | R | X | d | 0 | d | d | d | d | d | d | d | d
SHIFTL
1 | 1 | 0 | 0 | R | X | d | 1 | d | d | d | d | d | d | d | d
SHIFTR
1 | 1 | 0 | 1 | R | X | R | Y | d | d | d | d | d | d | d | d
CMP
1 | 1 | 1 | 0 | d | d | d | d | P | C | O | F | F | S | E | T
JUMP
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
BRE/BRZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
BRNE/BRNZ
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
BRG
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
BRGE

## Slide 15: Sample Assembly Programs for the i281 CPU

## Slide 16: Sample Assembly Programs for the i281 CPU (most of these are available in the simulator)

## Slide 17: Arithmetic 1

## Slide 18: C Version
// Arithmetic1
//
// C version
int main()
{
int x=2;
int z;
z = x+3;
// printf("%d\n", z);
}

## Slide 19: Assembly Version
; Assembly version
.data
x BYTE 2
z BYTE ?
.code
LOAD A, [x]
MOVE C, A ; z=x;
ADDI C, 3 ; z+=3;
STORE [z], C ; update the memory for z
; Register allocation
;
; A: x
; B: <not used>
; C: z
; D: <not used>

## Slide 20: C vs. Assembly
// Arithmetic1
//
// C version
int main()
{
int x=2;
int z;
z = x+3;
// printf("%d\n", z);
}
; Assembly version
.data
x BYTE 2
z BYTE ?
.code
LOAD A, [x]
MOVE C, A ; z=x;
ADDI C, 3 ; z+=3;
STORE [z], C ; update the
; memory for z

## Slide 21: Arithmetic 2

## Slide 22: C Version
// Arithmetic 2
//
// C version
int main()
{
int x=2;
int y=3;
int z;
z = x+y;
// printf("%d\n", z);
}

## Slide 23: Assembly Version
; Arithmetic 2
; Assembly version
.data
x BYTE 2
y BYTE 3
z BYTE ?
.code
LOAD A, [x]
LOAD B, [y]
MOVE C, A ; z=x;
ADD C, B ; z+=y;
STORE [z], C
; Register allocation
;
; A: x
; B: y
; C: z
; D: <not used>

## Slide 24: C vs. Assembly
// Arithmetic 2
//
// C version
int main()
{
int x=2;
int y=3;
int z;
z = x+y;
// printf("%d\n", z);
}
; Arithmetic 2
; Assembly version
.data
x BYTE 2
y BYTE 3
z BYTE ?
.code
LOAD A, [x]
LOAD B, [y]
MOVE C, A ; z=x;
ADD C, B ; z+=y;
STORE [z], C

## Slide 25: User Input from the Switches (arithmetic example)

## Slide 26
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
000000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags
user input
from the switches

## Slide 27: C vs. Assembly
#include<stdio.h>
int x = 2;
int y;
int result;
// Addition with User input
// for the second variable (y)
void main()
{
scanf("%d", &y);
result = x + y;
//printf("%d", result);
}
; Arithmetic with user input from switches
; Assembly version
.data
x BYTE 2
y BYTE ?
result BYTE ?
.code
LOAD A, [x] ; Reg. A <- [x]
INPUTD [y] ; [y] <- Input
LOAD B, [y] ; Reg. B <- [y]
ADD A, B ; A <- A + B
STORE [result], A ; result <- Reg A

## Slide 28: C vs. Assembly
#include<stdio.h>
int x = 2;
int y;
int result;
// Addition with User input
// for the second variable (y)
void main()
{
scanf("%d", &y);
result = x + y;
//printf("%d", result);
}
; Arithmetic with user input from switches
; Assembly version
.data
x BYTE 2
y BYTE ?
result BYTE ?
.code
LOAD A, [x] ; Reg. A <- [x]
INPUTD [y] ; [y] <- Input
LOAD B, [y] ; Reg. B <- [y]
ADD A, B ; A <- A + B
STORE [result], A ; result <- Reg A
Read the current value from switches SW07 to SW01
and store this value in the DMEM cell with label y.

## Slide 29: Multiplication

## Slide 30: C Version
// Multiplication
//
// C version
int main()
{
int x=3;
int z;
z = x*5;
// printf("%d\n", z);
}

## Slide 31: Assembly Version
; Multiplication
.data
x BYTE 3
z BYTE ?
.code
LOAD A, [x]
MOVE C, A ; z=x;
MOVE B, A ; B=x;
SHIFTL B ; B=2x
SHIFTL B ; B=4x
ADD C, B ; C=4x+x
STORE [z], C ; update the memory for z
; Register allocation
;
; A: x
; B: temporary results for 2x and 4x
; C: z
; D: <not used>

## Slide 32: C vs. Assembly
// Multiplication
//
// C version
int main()
{
int x=2;
int z;
z = x*5;
// printf("%d\n", z);
}
; Multiplication
.data
x BYTE 3
z BYTE ?
.code
LOAD A, [x]
MOVE C, A ; z=x;
MOVE B, A ; B=x;
SHIFTL B ; B=2x
SHIFTL B ; B=4x
ADD C, B ; C=4x+x
STORE [z], C ; update the
; memory for z

## Slide 33: Multiplication (implemented with repeated addition)

## Slide 34: C Version
// Multiplication
//
// C version
int main()
{
int x=2;
int z;
z = x*5;
// printf("%d\n", z);
}

## Slide 35: C Version
// Multiplication
//
// C version
int main()
{
int x=3;
int z=0;
for(int i=0; i<5; i++){
z+=x;
}
// printf("%d\n", z);
}

## Slide 36: Assembly Version
; Assembly version
;
; The CPU does not have OPCODEs for multiplication.
; Therefore, it is emulated with repeated addition.
.data
x BYTE 3
z BYTE ?
.code
LOAD A, [x]
LOADI C, 0 ; z=0
LOADI B, 0 ; i=0
LOADI D, 5 ; sentinel value
For: CMP B, D ; i<5?
BRGE End ; if(i>=5), exit for loop
ADD C, A ; z+=x
ADDI B, 1 ; i++
JUMP For ; jump to For loop
End: STORE [z], C ; update the z value in memory

## Slide 37: Assembly Version
; Assembly version
;
; The CPU does not have OPCODEs for multiplication.
; Therefore, it is emulated with repeated addition.
.data
x BYTE 3
z BYTE ?
.code
LOAD A, [x]
LOADI C, 0 ; z=0
LOADI B, 0 ; i=0
LOADI D, 5 ; sentinel value
For: CMP B, D ; i<5?
BRGE End ; if(i>=5), exit for loop
ADD C, A ; z+=x
ADDI B, 1 ; i++
JUMP For ; jump to For loop
End: STORE [z], C ; update the z value in memory
; Register allocation
;
; A: x
; B: i (optimized to register)
; C: z
; D: 5

## Slide 38: C vs. Assembly
// Multiplication
//
// C version
int main()
{
int x=3;
int z=0;
for(int i=0; i<5; i++){
z+=x;
}
// printf("%d\n", z);
}
; Assembly version
.data
x BYTE 3
z BYTE ?
.code
LOAD A, [x]
LOADI C, 0 ; z=0
LOADI B, 0 ; i=0
LOADI D, 5 ; sentinel value
For: CMP B, D ; i<5?
BRGE End ; if(i>=5), exit loop
ADD C, A ; z+=x
ADDI B, 1 ; i++
JUMP For ; jump to For loop
End: STORE [z], C ; update the z
; value in memory

## Slide 39: If Statement: Comparison of Signed Numbers

## Slide 40: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal

## Slide 41: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal
These 6 are used to
implement comparisons

## Slide 42: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal
BRL BRanch if Less
BRLE BRanch if Less than or Equal
These two instructions
are NOT supported
by this CPU

## Slide 43: The i281 Assembly Instructions
NOOP NO OPeration
INPUTC INPUT into Code memory
INPUTCF INPUT into Code memory with oFfset
INPUTD INPUT into Data memory
INPUTDF INPUT into Data memory with oFfset
MOVE MOVE the contents of one register into another
LOADI LOAD Immediate value
LOADP LOAD Pointer address
ADD ADD two registers
ADDI ADD an Immediate value to a register
SUB SUBtract two registers
SUBI SUBtract an Immediate value from a register
LOAD LOAD from a data memory address into a register
LOADF LOAD with an oFfset specified by another register
STORE STORE a register into a data memory address
STOREF STORE with an oFfset specified by another register
SHIFTL SHIFT Left all bits in a register
SHIFTR SHIFT Right all bits in a register
CMP CoMPare the values in two registers
JUMP JUMP unconditionally to a specified address
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal
BRL BRanch if Less
BRLE BRanch if Less than or Equal
comparison
of signed
numbers
only

## Slide 44: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)

## Slide 45: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)
These two comparisons
are NOT supported
by this CPU.
But with the help of the compiler
we can still use these comparisons.

## Slide 46: If Equal

## Slide 47: C vs. Assembly
// If Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x==y)
z=x;
}
; If Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRE Assign
JUMP End
Assign: STORE [z], A
End: NOOP

## Slide 48: C vs. Assembly
// If Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x==y)
z=x;
}
; If Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRE Assign
JUMP End
Assign: STORE [z], A
End: NOOP
This code is inefficient.
It takes 3 instructions.

## Slide 49: C vs. Assembly
// If Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x==y)
z=x;
}
; If Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRNE End
STORE [z], A
End: NOOP
instead of x == y,
check if x != y
This version is better:

## Slide 50: C vs. Assembly
// If Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x==y)
z=x;
}
; If Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRNE End
STORE [z], A
End: NOOP

## Slide 51: If Not Equal

## Slide 52: C vs. Assembly
// If Not Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x != y)
z=x;
}
; If Not Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRE End
STORE [z], A
End: NOOP

## Slide 53: C vs. Assembly
// If Not Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x != y)
z=x;
}
; If Not Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRE End
STORE [z], A
End: NOOP
instead of x != y,
check if x == y

## Slide 54: If Less

## Slide 55: C vs. Assembly
// If Less
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x < y)
z=x;
}
; If Less
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRGE End
STORE [z], A
End: NOOP

## Slide 56: C vs. Assembly
// If Less
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x < y)
z=x;
}
; If Less
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRGE End
STORE [z], A
End: NOOP
instead of x < y,
check if x >= y and
skip the z=x part if true.

## Slide 57: If Less or Equal

## Slide 58: C vs. Assembly
// If Less or Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x <= y)
z=x;
}
; If Less or Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRG End
STORE [z], A
End: NOOP

## Slide 59: C vs. Assembly
// If Less or Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x <= y)
z=x;
}
; If Less or Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP A, B
BRG End
STORE [z], A
End: NOOP
instead of x <= y,
check if x > y

## Slide 60: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)
BRGE End BRG End BRNE End BRE End BRL End BRLE End
CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y
Where x and y are two registers.

## Slide 61: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)
BRGE End BRG End BRNE End BRE End BRL End BRLE End
CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y
These two instructions
are NOT supported
by this CPU.

## Slide 62: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)
BRGE End BRG End BRNE End BRE End BRL End BRLE End
CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y
Therefore, invert the order.
(y <= x) (y < x)

## Slide 63: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)
BRGE End BRG End BRNE End BRE End BRL End BRLE End
CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y
(y <= x) (y < x)
BRG End BRGE End
CMP y,x CMP y,x
Therefore, invert the order.

## Slide 64: If Greater or Equal

## Slide 65: C vs. Assembly
// If Greater or Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x >= y)
z=x;
}
; If Greater or Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRG End
STORE [z], A
End: NOOP

## Slide 66: C vs. Assembly
// If Greater or Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x >= y)
z=x;
}
; If Greater or Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRG End
STORE [z], A
End: NOOP
need to swap the direction

## Slide 67: C vs. Assembly
// If Greater or Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(y <= x)
z=x;
}
; If Greater or Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRG End ; B,A instead of A,B
STORE [z], A
End: NOOP

## Slide 68: C vs. Assembly
// If Greater or Equal
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(y <= x)
z=x;
}
; If Greater or Equal
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRG End
STORE [z], A
End: NOOP
instead of y <= x,
check if y > x

## Slide 69: If Greater

## Slide 70: C vs. Assembly
// If Greater
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(x > y)
z=x;
}
; If Greater
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRGE End
STORE [z], A
End: NOOP

## Slide 71: C vs. Assembly
// If Greater
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(y < x)
z=x;
}
; If Greater
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRGE End
STORE [z], A
End: NOOP

## Slide 72: C vs. Assembly
// If Greater
//
// C version
int main()
{
int x=3;
int y=5;
int z=0;
if(y < x)
z=x;
}
; If Greater
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE 0
.code
LOAD A, [x]
LOAD B, [y]
CMP B, A ; these are swapped
BRGE End
STORE [z], A
End: NOOP
instead of y < x,
check if y >= x

## Slide 73: Common Comparisons
(x < y) (x <= y) (x == y) (x!= y) (x >= y) (x > y)
BRGE End BRG End BRNE End BRE End BRL End BRLE End
CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y CMP x,y
(y <= x) (y < x)
BRG End BRGE End
CMP y,x CMP y,x

## Slide 74: If Statement: Comparison of Unsigned Numbers
(not supported by this CPU)

## Slide 75: Comparison of Signed Numbers
Equal ZF
Not equal ZF
Greater ZF • XNOR( NF, OF )
Greater or Equal XNOR( NF, OF )
Less XOR( NF, OF )
Less or Equal ZF + XOR( NF, OF )

## Slide 76: Comparison of Unsigned Numbers
Equal ZF
Not equal ZF
Above ZF • CF
Above or Equal CF
Below CF
Below or Equal ZF + CF

## Slide 77: Signed v.s. Unsigned

## Slide 78: Signed v.s. Unsigned
they overlap only here

## Slide 79: Signed v.s. Unsigned
BRE Ranch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRA BRanch if Above
BRAE BRanch if Above or Equal
BRB BRanch if Below
BRBE BRanch if Below or Equal
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal
BRL BRanch if Less
BRLE BRanch if Less than or Equal

## Slide 80: Signed v.s. Unsigned
BRE Ranch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRA BRanch if Above
BRAE BRanch if Above or Equal
BRB BRanch if Below
BRBE BRanch if Below or Equal
BRE BRanch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRG BRanch if Greater
BRGE BRanch if Greater than or Equal
BRL BRanch if Less
BRLE BRanch if Less than or Equal
The OPCODEs in blue
are NOT implemented
on this CPU

## Slide 81: Thus, comparing unsigned numbers requires adding new OPCODEs
BRE Ranch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRA BRanch if Above
BRAE BRanch if Above or Equal
BRB BRanch if Below
BRBE BRanch if Below or Equal

## Slide 82: Thus, comparing unsigned numbers requires adding new OPCODEs
BRE Ranch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRA BRanch if Above
BRAE BRanch if Above or Equal
BRB BRanch if Below
BRBE BRanch if Below or Equal
at a minimum
you need only
these two

## Slide 83: Thus, comparing unsigned numbers requires adding new OPCODEs
BRE Ranch if Equal
BRZ BRanch if Zero
BRNE BRanch if Not Equal
BRNZ BRanch if Not Zero
BRA BRanch if Above
BRAE BRanch if Above or Equal
BRB BRanch if Below
BRBE BRanch if Below or Equal
or these two

## Slide 84: OPCODEs that check the Flags

## Slide 85
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 86
The Flags Register
Clock
Write
Enable
D
Q
Q
0
1
Carry
Carry
Flag
D
Q
Q
0
1
Overflow
Overflow
Flag
D
Q
Q
0
1
Negative
Negative
Flag
D
Q
Q
0
1
Zero
Zero
Flag

## Slide 87: You could also add OPCODEs that just check a specific flag
BRC BRanch if Carry
BRNC BRanch if No Carry
BRO BRanch if Overflow
BRNO BRanch if No Overflow
BRN BRanch if Negative
BRNN BRanch if Not Negative
BRZ BRanch if Zero
BRNZ BRanch if Not Zero
only these two
are currently
supported

## Slide 88: You could also add OPCODEs that just check a specific flag
BRC BRanch if Carry
BRNC BRanch if No Carry
BRO BRanch if Overflow
BRNO BRanch if No Overflow
BRN BRanch if Negative
BRNN BRanch if Not Negative
BRZ BRanch if Zero
BRNZ BRanch if Not Zero
equivalent to
BRE
BRNE

## Slide 89: You could also add OPCODEs that just check a specific flag
BRC BRanch if Carry
BRNC BRanch if No Carry
BRO BRanch if Overflow
BRNO BRanch if No Overflow
BRN BRanch if Negative
BRNN BRanch if Not Negative
BRZ BRanch if Zero
BRNZ BRanch if Not Zero
equivalent to
BRAE
BRB

## Slide 90: Signed v.s. Unsigned

## Slide 91: How to add more BRanch OpCODEs
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
BRE/BRZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
BRNE/BRNZ
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
BRG
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
BRGE

## Slide 92: How to add more BRanch OpCODES
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
BRE/BRZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
BRNE/BRNZ
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
BRG
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
BRGE
could use this don’t’ care bit and
update the OpCODE decoder

## Slide 93: How to add more BRanch OpCODES
1 | 1 | 1 | 1 | d | d | 0 | 0 | P | C | O | F | F | S | E | T
BRE/BRZ
1 | 1 | 1 | 1 | d | d | 0 | 1 | P | C | O | F | F | S | E | T
BRNE/BRNZ
1 | 1 | 1 | 1 | d | d | 1 | 0 | P | C | O | F | F | S | E | T
BRG
1 | 1 | 1 | 1 | d | d | 1 | 1 | P | C | O | F | F | S | E | T
BRGE
could use these two don’t care bits and
update the OpCODE decoder

## Slide 94
c4
c5
A
B
C
D
00000000
A
00000000
B
00000000
C
00000000
D
c6
c7
A
B
C
D
Registers
c10
c8
c9
Control
c1 c2 c3 c4 c5 c6 c7 c8 c9 c10 c11 c12 c13 c14 c15 c16 c17 c18
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
c2
1
0
c18
0
1
c15
0
1
OpCode
Decoder
100000
PC
PC
Update
Logic
c3
c12
c13
ALU
i281 CPU
0000
0001
0010
0011
0100
0101
0110
0111
Data Memory
c17
00000101
00000000
00000000
00000000
00000000
00000000
00000000
00000000
c11
0
1
Switches
c16
0
1
100000
100001
100010
100011
100100
100101
100110
100111
101000
00110100 00000000
00110000 00000001
10001100 00000000
11010011 00000000
11110010 00000011
01000100 00000000
01010000 00000001
11100000 11111011
10100100 00000010
Code Memory
c1
6 low
6
6
16
16
8 high
8 low
4
27
4
4
4 low
8
8
8
8
8
6
6
6
6
6
8
4
8
8
6 low
4
8
8
8
8
8
8
8
8 low
16
16
8
8
0 0 0 0
c14
Flags

## Slide 95
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8 | I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0
8
2
2
ADDR/VAL/OFFSET
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1

## Slide 96
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8 | I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0
8
2
2
ADDR/VAL/OFFSET
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
change to
3-to-8 decoder
use 3 bits

## Slide 97
I15 | I14 | I13 | I12 | I11 | I10 | I9 | I8 | I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0
8
2
2
ADDR/VAL/OFFSET
RY
RX
En
1
4-to-16 decoder
w0
w3
w2
w1
y0
y1
y2
y3
y4
y5
y6
y7
y8
y9
y10
y11
y12
y13
y14
y15
NOOP
MOVE
LOADI/LOADP
ADD
ADDI
SUB
SUBI
LOAD
LOADF
STORE
STOREF
CMP
JUMP
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
INPUTC
INPUTCF
INPUTD
INPUTDF
BRE/BRZ
BRNE/BRNZ
BRG
BRGE
En
2-to-4 decoder
w0
w1
y0
y1
y2
y3
SHIFTL
SHIFTR
En
1-to-2 decoder
w0
y0
y1
change to
4-to-16 decoder
use 4 bits

## Slide 98: If-Else Statement

## Slide 99: C vs. Assembly
// If-Else Statement
//
// C version
int main()
{
int x=3;
int y=5;
int z;
if (x<y)
z=x;
else
z=y;
}
; If If-Else Statement
;
; Assembly version
.data
x BYTE 3
y BYTE 5
z BYTE ?
.code
LOAD A, [x]
LOAD B, [y]
If: CMP A, B
BRGE Else
STORE [z], A
JUMP End
Else: STORE [z], B
End: NOOP

## Slide 100: If with two conditions (OR)

## Slide 101: C vs. Assembly
// If with 2 conditions (OR)
//
// C version
int main()
{
int x=9;
int min=1;
int max=8;
int inRange=1;
if ( (x<min) || (x>max) )
inRange=0;
}
; Assembly version
.data
x BYTE 9
min BYTE 1
max BYTE 8
inRange BYTE 1
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
First: CMP A, B ; x < min ?
BRGE Second
Set: LOADI D, 0
STORE [inRange], D
JUMP End
Second: CMP C, A ; max < x ?
BRGE End
JUMP Set
End: NOOP

## Slide 102: C vs. Assembly
// If with 2 conditions (OR)
// this is closer to assembly
int main()
{
int x=9;
int min=1;
int max=8;
int inRange=1;
if(x < min) // First
{
Set:
inRange=0;
goto End;
}
else if(max < x) // Second
{
goto Set;
}
End:
}
; Assembly version
.data
x BYTE 9
min BYTE 1
max BYTE 8
inRange BYTE 1
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
First: CMP A, B ; x < min ?
BRGE Second
Set: LOADI D, 0
STORE [inRange], D
JUMP End
Second: CMP C, A ; max < x ?
BRGE End
JUMP Set
End: NOOP
// swapped condition

## Slide 103: C vs. Assembly
// If with 2 conditions (OR)
// this is closer to assembly
int main()
{
int x=9;
int min=1;
int max=8;
int inRange=1;
if(x < min) // First
{
Set:
inRange=0;
goto End;
}
else if(max < x) // Second
{
goto Set;
}
End:
}
; Assembly version
.data
x BYTE 9
min BYTE 1
max BYTE 8
inRange BYTE 1
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
First: CMP A, B
BRGE Second
Set: LOADI D, 0
STORE [inRange], D
JUMP End
Second: CMP C, A ; max < x ?
BRGE End
JUMP Set
End: NOOP
instead of x < min,
check if x >= min

## Slide 104: C vs. Assembly
// If with 2 conditions (OR)
// this is closer to assembly
int main()
{
int x=9;
int min=1;
int max=8;
int inRange=1;
if(x < min) // First
{
Set:
inRange=0;
goto End;
}
else if(max < x) // Second
{
goto Set;
}
End:
}
; Assembly version
.data
x BYTE 9
min BYTE 1
max BYTE 8
inRange BYTE 1
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
First: CMP A, B
BRGE Second
Set: LOADI D, 0
STORE [inRange], D
JUMP End
Second: CMP C, A
BRGE End
JUMP Set
End: NOOP
instead of max < x,
check if max >= x

## Slide 105: If with two conditions (AND)

## Slide 106: C vs. Assembly
// If with 2 conditions (AND)
//
// C version
int main()
{
int x=5;
int min=1;
int max=8;
int inRange=0;
if ( (x>=min) && (x<=max) )
inRange=1;
}
; Assembly version
.data
x BYTE 5
min BYTE 1
max BYTE 8
inRange BYTE 0
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
CMP B, A ; min <= x ?
BRG End
CMP A, C ; x <= max ?
BRG End
LOADI D, 1
STORE [inRange], D
End: NOOP

## Slide 107: C vs. Assembly
// If with 2 conditions (AND)
//
// C version
int main()
{
int x=5;
int min=1;
int max=8;
int inRange=0;
if(min<=x) // swapped dir.
{
if(x<=max)
{
inRange=1;
}
}
}
; Assembly version
.data
x BYTE 5
min BYTE 1
max BYTE 8
inRange BYTE 0
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
CMP B, A ; min <= x ?
BRG End
CMP A, C ; x <= max ?
BRG End
LOADI D, 1
STORE [inRange], D
End: NOOP

## Slide 108: C vs. Assembly
// If with 2 conditions (AND)
//
// C version
int main()
{
int x=5;
int min=1;
int max=8;
int inRange=0;
if(min<=x) // swapped dir.
{
if(x<=max)
{
inRange=1;
}
}
}
; Assembly version
.data
x BYTE 5
min BYTE 1
max BYTE 8
inRange BYTE 0
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
CMP B, A
BRG End
CMP A, C ; x <= max ?
BRG End
LOADI D, 1
STORE [inRange], D
End: NOOP
instead of min <= x,
check if min > x

## Slide 109: C vs. Assembly
// If with 2 conditions (AND)
//
// C version
int main()
{
int x=5;
int min=1;
int max=8;
int inRange=0;
if(min<=x) // swapped dir.
{
if(x<=max)
{
inRange=1;
}
}
}
; Assembly version
.data
x BYTE 5
min BYTE 1
max BYTE 8
inRange BYTE 0
.code
LOAD A, [x]
LOAD B, [min]
LOAD C, [max]
CMP B, A
BRG End
CMP A, C
BRG End
LOADI D, 1
STORE [inRange], D
End: NOOP
instead of x <= max,
check if x > max

## Slide 110: Switch Statement

## Slide 111: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 112: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 113: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 114: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 115: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 116: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 117: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP

## Slide 118: C vs. Assembly
// Switch Statement
//
// C version
int main()
{
int x=6;
int y;
switch(x)
{
case 0: y=2*x;
break;
case 1: y=x+3;
break;
case 2: y=x-1;
break;
default: y=x/2;
break;
}
}
; Assembly version
.data
x BYTE 6
y BYTE ?
.code
LOAD A, [x]
Zero: LOADI C, 0
CMP A, C
BRNE One
MOVE B, A
SHIFTL B
JUMP End
One: LOADI C, 1
CMP A, C
BRNE Two
MOVE B, A
ADDI B, 3
JUMP End
Two: LOADI C, 2
CMP A, C
BRNE Default
MOVE B, A
SUBI B, 1
JUMP End
Default: MOVE B, A
SHIFTR B
End: STORE [y], B
NOOP
not mapped to instruction;
just goes to next line

## Slide 119: Working with Arrays

## Slide 120: C vs. Assembly
// Array
//
// C version
int array[]={1, 2, 3, 4};
int main()
{
array[0] = 0;
array[1] += 5;
array[2] -= 1;
array[3] += array[2];
}
; Array
;
; Assembly version
.data
array BYTE 1, 2, 3, 4
.code
LOADI A, 0
STORE [array + 0], A
LOAD B, [array + 1]
ADDI B, 5
STORE [array + 1], B
LOAD C, [array + 2]
SUBI C, 1
STORE [array + 2], C
LOAD D, [array + 3]
ADD D, C
STORE [array + 3], D

## Slide 121: C vs. Assembly
// Array
//
// C version
int array[]={1, 2, 3, 4};
int main()
{
array[0] = 0;
array[1] += 5;
array[2] -= 1;
array[3] += array[2];
}
; Array
;
; Assembly version
.data
array BYTE 1, 2, 3, 4
.code
LOADI A, 0
STORE [array + 0], A
LOAD B, [array + 1]
ADDI B, 5
STORE [array + 1], B
LOAD C, [array + 2]
SUBI C, 1
STORE [array + 2], C
LOAD D, [array + 3]
ADD D, C
STORE [array + 3], D

## Slide 122: C vs. Assembly
// Array
//
// C version
int array[]={1, 2, 3, 4};
int main()
{
array[0] = 0;
array[1] += 5;
array[2] -= 1;
array[3] += array[2];
}
; Array
;
; Assembly version
.data
array BYTE 1, 2, 3, 4
.code
LOADI A, 0
STORE [array + 0], A
LOAD B, [array + 1]
ADDI B, 5
STORE [array + 1], B
LOAD C, [array + 2]
SUBI C, 1
STORE [array + 2], C
LOAD D, [array + 3]
ADD D, C
STORE [array + 3], D

## Slide 123: Machine Code vs. Assembly
// Machine Code
ADDR: DMEM
0000: 00000001
0001: 00000010
0010: 00000011
0011: 00000100
IMEM
0011_00_00_00000000
1010_00_00_00000000
1000_01_00_00000001
0101_01_00_00000101
1010_01_00_00000001
1000_10_00_00000010
0111_10_00_00000001
1010_10_00_00000010
1000_11_00_00000011
0100_11_10_00000000
1010_11_00_00000011
; Array
;
; Assembly version
.data
array BYTE 1, 2, 3, 4
.code
LOADI A, 0
STORE [array + 0], A
LOAD B, [array + 1]
ADDI B, 5
STORE [array + 1], B
LOAD C, [array + 2]
SUBI C, 1
STORE [array + 2], C
LOAD D, [array + 3]
ADD D, C
STORE [array + 3], D

## Slide 124: Machine Code vs. Assembly
// Machine Code
ADDR: DMEM
0000: 00000001
0001: 00000010
0010: 00000011
0011: 00000100
IMEM
0011_00_00_00000000
1010_00_00_00000000
1000_01_00_00000001
0101_01_00_00000101
1010_01_00_00000001
1000_10_00_00000010
0111_10_00_00000001
1010_10_00_00000010
1000_11_00_00000011
0100_11_10_00000000
1010_11_00_00000011
; Array
;
; Assembly version
.data
array BYTE 1, 2, 3, 4
.code
LOADI A, 0
STORE [array + 0], A
LOAD B, [array + 1]
ADDI B, 5
STORE [array + 1], B
LOAD C, [array + 2]
SUBI C, 1
STORE [array + 2], C
LOAD D, [array + 3]
ADD D, C
STORE [array + 3], D

## Slide 125: Machine Code vs. Assembly
// Machine Code
ADDR: DMEM
0000: 00000001
0001: 00000010
0010: 00000011
0011: 00000100
IMEM
0011_00_00_00000000
1010_00_00_00000000
1000_01_00_00000001
0101_01_00_00000101
1010_01_00_00000001
1000_10_00_00000010
0111_10_00_00000001
1010_10_00_00000010
1000_11_00_00000011
0100_11_10_00000000
1010_11_00_00000011
; Array
;
; Assembly version
.data
array BYTE 1, 2, 3, 4
.code
LOADI A, 0
STORE [array + 0], A
LOAD B, [array + 1]
ADDI B, 5
STORE [array + 1], B
LOAD C, [array + 2]
SUBI C, 1
STORE [array + 2], C
LOAD D, [array + 3]
ADD D, C
STORE [array + 3], D

## Slide 126: Working with Arrays And Looping Over Their Elements

## Slide 127: C vs. Assembly
// Array plus 5
// C version
int array[]={1, 2, 3, 4};
int N = 4;
int main()
{
int i;
// add 5 to all elements
for( i=0; i< N; i++)
{
array[i] += 5;
}
}
; Array plus 5
; Assembly version
.data
array BYTE 1, 2, 3, 4
N BYTE 4
.code
LOADI A, 0 ; i = 0
For: LOAD D, [N] ; D <- N
CMP A, D ; i < N ?
BRGE End ; if no, exit loop
LOADF C, [array + A] ; load array[i]
ADDI C, 5 ; add 5
STOREF [array + A], C ; store the result
Iinc: ADDI A, 1 ; i++
JUMP For ; next iteration
End: NOOP
; Register allocation:
; A: i
; B: <not used>
; C: temp variable for loading the array elements
; D: N

## Slide 128: C vs. Assembly
// Array plus 5
// C version
int array[]={1, 2, 3, 4};
int N = 4;
int main()
{
int i;
// add 5 to all elements
for( i=0; i< N; i++)
{
array[i] += 5;
}
}
; Array plus 5
; Assembly version
.data
array BYTE 1, 2, 3, 4
N BYTE 4
.code
LOADI A, 0 ; i = 0
For: LOAD D, [N] ; D <- N
CMP A, D ; i < N ?
BRGE End ; if no, exit loop
LOADF C, [array + A] ; load array[i]
ADDI C, 5 ; add 5
STOREF [array + A], C ; store the result
Iinc: ADDI A, 1 ; i++
JUMP For ; next iteration
End: NOOP
; Register allocation:
; A: i
; B: <not used>
; C: temp variable for loading the array elements
; D: N

## Slide 130
2nd iteration

## Slide 131
3rd iteration

## Slide 132
4th iteration

## Slide 133: C vs. Assembly
// Array plus 5
// C version
int array[]={1, 2, 3, 4};
int N = 4;
int main()
{
int i;
// add 5 to all elements
for( i=0; i< N; i++)
{
array[i] += 5;
}
}
; Array plus 5
; Assembly version
.data
array BYTE 1, 2, 3, 4
N BYTE 4
.code
LOADI A, 0 ; i = 0
For: LOAD D, [N] ; D <- N
CMP A, D ; i < N ?
BRGE End ; if no, exit loop
LOADF C, [array + A] ; load array[i]
ADDI C, 5 ; add 5
STOREF [array + A], C ; store the result
Iinc: ADDI A, 1 ; i++
JUMP For ; next iteration
End: NOOP
; Register allocation:
; A: i
; B: <not used>
; C: temp variable for loading the array elements
; D: N

## Slide 135
2nd iteration

## Slide 136
3rd iteration

## Slide 137
4th iteration

## Slide 138: C vs. Assembly
// Array plus 5
// C version
int array[]={1, 2, 3, 4};
int N = 4;
int main()
{
int i;
// add 5 to all elements
for( i=0; i< N; i++)
{
array[i] += 5;
}
}
; Array plus 5
; Assembly version
.data
array BYTE 1, 2, 3, 4
N BYTE 4
.code
LOADI A, 0 ; i = 0
For: LOAD D, [N] ; D <- N
CMP A, D ; i < N ?
BRGE End ; if no, exit loop
LOADF C, [array + A] ; load array[i]
ADDI C, 5 ; add 5
STOREF [array + A], C ; store the result
Iinc: ADDI A, 1 ; i++
JUMP For ; next iteration
End: NOOP
; Register allocation:
; A: i
; B: <not used>
; C: temp variable for loading the array elements
; D: N

## Slide 149: For Loop Example: Add the numbers from 1 to 5

## Slide 150: Add the numbers from 1 to 5
// C Version
// using a for loop
int main()
{
int N=5;
int i, sum;
sum=0;
for(i=1; i<=N; i++) {
sum+=i;
}
// printf("%d\n", sum);
}
; Assembly Version
.data
N BYTE 5
i BYTE ?
sum BYTE ?
.code
LOADI B, 0 ; sum=0
LOADI A, 1 ; i=1
LOAD D, [N] ; register_D=N
Loop: CMP A, D ; i<=N ?
BRG End ; exit if i>N
Add: ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP Loop ; next iteration
End: STORE [sum], B ; write B to sum
; Register allocation:
; A: i
; B: sum
; C: <not used>
; D: N
See the previous lectures for an animation of the program execution.

## Slide 151: Do Loop Example: Add the numbers from 1 to 5

## Slide 152: C Version
// Add the numbers from 1 to 5 using a do loop.
int N=5;
int main()
{
int i, sum;
i=0;
sum=0;
do
{
i++;
sum+=i;
}while( i < N );
}

## Slide 153: Assembly Version
; Add the numbers from 1 to 5 using a do loop.
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0 ; i = 0
LOADI B, 0 ; sum=0
LOAD D, [N] ; register D = N
Do: ADDI A, 1 ; i++
ADD B, A ; sum+=i
CMP D, A ; N > i ? (register ordering is swapped)
BRG Do ; if true, jump to Do
End: STORE [sum], B ; store sum to memory
; Register allocation:
; A: i (the variable i is optimized to register A)
; B: sum
; C: <not used>
; D: N

## Slide 154: Do Loop
// Add the numbers from
// 1 to 5 using a do loop
int N=5;
int main()
{
int i, sum;
i=0;
sum=0;
do
{
i++;
sum+=i;
}while( i < N );
}
; assembly version
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0 ; i = 0
LOADI B, 0 ; sum=0
LOAD D, [N] ; register D = N
Do: ADDI A, 1 ; i++
ADD B, A ; sum+=i
CMP D, A ; N > i ?
BRG Do ; if true, jump to Do
End: STORE [sum], B ; store sum to memory
; Register allocation:
; A: i (the variable i is optimized to register A)
; B: sum
; C: <not used>
; D: N

## Slide 155: Machine Code Version
Data Memory:
00000101
00000000
Code Memory:
0011000000000000
0011010000000000
1000110000000000
0101000000000001
0100010000000000
1101110000000000
1111001011111100
1010010000000001

## Slide 156: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011000000000000
0011010000000000
1000110000000000
0101000000000001
0100010000000000
1101110000000000
1111001011111100
1010010000000001

## Slide 157: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
00110000_00000000
00110100_00000000
10001100_00000000
01010000_00000001
01000100_00000000
11011100_00000000
11110010_11111100
10100100_00000001

## Slide 158: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 159: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 160: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 161: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 162: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 163: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 164: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 165: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_dd_00000000
0011_01_dd_00000000
1000_11_dd_00000000
0101_00_dd_00000001
0100_01_00_dddddddd
1101_11_00_dddddddd
1111_dd_10_11111100
1010_01_dd_00000001

## Slide 166: Assembly v.s. Machine Code
.data
N BYTE 5
sum BYTE ?
.code
LOADI A, 0
LOADI B, 0
LOAD D, [N]
Do: ADDI A, 1
ADD B, A
CMP D, A
BRG Do
End: STORE [sum], B
Data Memory:
00000101
00000000
Code Memory:
0011_00_00_00000000
0011_01_00_00000000
1000_11_00_00000000
0101_00_00_00000001
0100_01_00_00000000
1101_11_00_00000000
1111_00_10_11111100
1010_01_00_00000001

## Slide 167: While Loop Example: Add the numbers from 1 to 5

## Slide 168: While Loop
; assembly version
.data
N BYTE 5
sum BYTE ?
; i is optimized to register A
.code
LOADI A, 1 ; i = 1
LOADI B, 0 ; sum=0
LOAD D, [N] ; register D = N
While: CMP A, D ; i <= N ?
BRG End ; if no, exit the loop
ADD B, A ; sum+=i
ADDI A, 1 ; i++
JUMP While ; next iteration
End: STORE [sum], B ; store sum to memory
; Register allocation:
; A: i
; B: sum
; C: <not used>
; D: N
// Add the numbers from
// 1 to 5 using a while loop
int N=5;
int sum;
int i;
int main()
{
i=1;
sum=0;
while( i <= N )
{
sum+=i;
i++;
}
}

## Slide 169: Bubble Sort

## Slide 170: C Version
int array[] = {7, 3, 2, 1, 6, 4, 5, 8};
int last = 7; // last valid index in the array
int temp;
int i, j;
int main()
{
for (i = 0; i < last; i++)
for (j = 0; j < last-i; j++)
if (array[j] > array[j+1]){
temp = array[j];
array[j] = array[j+1];
array[j+1] = temp;
}
//for(i = 0; i < N; i++){
// printf("%d, ", array[i]);
//}
}

## Slide 171: Assembly Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0 ; i = 0;
Outer: LOAD D, [last] ; Load last into D
LOADI B, 0 ; j = 0;
CMP A, D ; i < last
BRGE End ; If i >= last break out of the outer loop
Inner: LOAD D, [last] ; Re-Load last into D (this register is shared)
SUB D, A ; D = D - A (i.e., D = last - i)
CMP B, D ; j < last - i
BRGE Iinc ; If j >= last-i branch to Iinc
If: LOADF C, [array+B] ; C = array[j]
LOADF D, [array+B+1] ; D = array[j+1] (compiler adds 1 to addr. of array)
CMP D, C ; if array[j+1] < array[j] (switched direction)
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1 ; j++
JUMP Inner
Iinc: ADDI A, 1 ; i++
JUMP Outer
End: NOOP ; Do nothing
; Register allocation:
; A: i
; B: j
; C: array[j]
; D: last, array[j+1]
; Notes: i and j are optimized away. They exist only in registers, not in the main memory.

## Slide 172: Assembly Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0 ; i = 0;
Outer: LOAD D, [last] ; Load last into D
LOADI B, 0 ; j = 0;
CMP A, D ; i < last
BRGE End ; If i >= last break out of the outer loop
Inner: LOAD D, [last] ; Re-Load last into D (this register is shared)
SUB D, A ; D = D - A (i.e., D = last - i)
CMP B, D ; j < last - i
BRGE Iinc ; If j >= last-i branch to Iinc
If: LOADF C, [array+B] ; C = array[j]
LOADF D, [array+B+1] ; D = array[j+1] (compiler adds 1 to addr. of array)
CMP D, C ; if array[j+1] < array[j] (switched direction)
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1 ; j++
JUMP Inner
Iinc: ADDI A, 1 ; i++
JUMP Outer
End: NOOP ; Do nothing
; Register allocation:
; A: i
; B: j
; C: array[j]
; D: last, array[j+1]
; Notes: i and j are optimized away. They exist only in registers, not in the main memory.

## Slide 173: Bubble Sort
int array[] = {7, 3, 2, 1, 6, 4, 5, 8};
int last = 7; // last valid index
int temp;
int i, j;
int main()
{
for (i = 0; i < last; i++)
for (j = 0; j < last-i; j++)
if (array[j] > array[j+1]){
temp = array[j];
array[j] = array[j+1];
array[j+1] = temp;
}
//for(i = 0; i < N; i++){
// printf("%d, ", array[i]);
//}
}
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0 ; i = 0;
Outer: LOAD D, [last] ; Load last into D
LOADI B, 0 ; j = 0;
CMP A, D ; i < last
BRGE End ; If i >= last
Inner: LOAD D, [last] ; Re-Load last into D
SUB D, A ; D=D-A, i.e., D=last-i
CMP B, D ; j < last - i
BRGE Iinc ; If j >= last-i
If: LOADF C, [array+B] ; C = array[j]
LOADF D, [array+B+1] ; D = array[j+1]
CMP D, C ; array[j+1] < array[j]
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1 ; j++
JUMP Inner
Iinc: ADDI A, 1 ; i++
JUMP Outer
End: NOOP
; Register allocation:
; A: i
; B: j
; C: array[j]
; D: last, array[j+1] (shared)
; Notes: i and j are optimized away to registers.

## Slide 175: Machine Code Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 176: Machine Code Version
Data Memory:
00000111
00000011
00000010
00000001
00000110
00000100
00000101
00001000
00000111
00000000
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 177: Machine Code Version
Data Memory:
00000111 //array[0]
00000011 //array[1]
00000010 //array[2]
00000001 //array[3]
00000110 //array[4]
00000100 //array[5]
00000101 //array[6]
00001000 //array[7]
00000111 //last
00000000 //temp
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 178: Machine Code Version
Data Memory:
00000111 //array[0]
00000011 //array[1]
00000010 //array[2]
00000001 //array[3]
00000110 //array[4]
00000100 //array[5]
00000101 //array[6]
00001000 //array[7]
00000111 //last
00000000 //temp
Address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 179: Machine Code Version
Data Memory:
00000111 //array[0]
00000011 //array[1]
00000010 //array[2]
00000001 //array[3]
00000110 //array[4]
00000100 //array[5]
00000101 //array[6]
00001000 //array[7]
00000111 //last
00000000 //temp
00000000
00000000
00000000
00000000
00000000
00000000
Address
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 180: Machine Code Version
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 181: Machine Code Version
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 182: Machine Code Version
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
Address
100000
100001
100010
100011
100100
100101
100110
100111
101000
101001
101010
101011
101100
101101
101110
101111
110000
110001
110010
110011
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 183: Machine Code Version
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
0000000000000000
. . .
0000000000000000
0000000000000000
Address
100000
100001
100010
100011
100100
100101
100110
100111
101000
101001
101010
101011
101100
101101
101110
101111
110000
110001
110010
110011
110100
. . .
111110
111111
.data
array BYTE 7, 3, 2, 1, 6, 4, 5, 8
last BYTE 7
temp BYTE ?
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 185: Assembly v.s. Machine Code
Code Memory:
0011000000000000
1000110000001000
0011010000000000
1101001100000000
1111001100001110
1000110000001000
0110110000000000
1101011100000000
1111001100001000
1001100100000000
1001110100000001
1101111000000000
1111001100000010
1011110100000000
1011100100000001
0101010000000001
1110000011110100
0101000000000001
1110000011101110
0000000000000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 186: Assembly v.s. Machine Code
Code Memory:
00110000_00000000
10001100_00001000
00110100_00000000
11010011_00000000
11110011_00001110
10001100_00001000
01101100_00000000
11010111_00000000
11110011_00001000
10011001_00000000
10011101_00000001
11011110_00000000
11110011_00000010
10111101_00000000
10111001_00000001
01010100_00000001
11100000_11110100
01010000_00000001
11100000_11101110
00000000_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 187: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 188: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 189: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 190: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 191: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 192: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 193: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 194: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 195: Assembly v.s. Machine Code
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 196: Assembly v.s. Machine Code
Code Memory:
0011_00_dd_00000000
1000_11_dd_00001000
0011_01_dd_00000000
1101_00_11_dddddddd
1111_dd_11_00001110
1000_11_dd_00001000
0110_11_00_dddddddd
1101_01_11_dddddddd
1111_dd_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_dddddddd
1111_dd_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_dd_00000001
1110_dd_dd_11110100
0101_00_dd_00000001
1110_dd_dd_11101110
0000_dd_dd_dddddddd
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP

## Slide 197: Assembly v.s. Machine Code
.code
LOADI A, 0
Outer: LOAD D, [last]
LOADI B, 0
CMP A, D
BRGE End
Inner: LOAD D, [last]
SUB D, A
CMP B, D
BRGE Iinc
If: LOADF C, [array+B]
LOADF D, [array+B+1]
CMP D, C
BRGE Jinc
Swap: STOREF [array+B], D
STOREF [array+B+1], C
Jinc: ADDI B, 1
JUMP Inner
Iinc: ADDI A, 1
JUMP Outer
End: NOOP
Code Memory:
0011_00_00_00000000
1000_11_00_00001000
0011_01_00_00000000
1101_00_11_00000000
1111_00_11_00001110
1000_11_00_00001000
0110_11_00_00000000
1101_01_11_00000000
1111_00_11_00001000
1001_10_01_00000000
1001_11_01_00000001
1101_11_10_00000000
1111_00_11_00000010
1011_11_01_00000000
1011_10_01_00000001
0101_01_00_00000001
1110_00_00_11110100
0101_00_00_00000001
1110_00_00_11101110
0000_00_00_00000000

## Slide 198: For more examples try the i281 simulator

## Slide 199: i281 Simulator
To try the simulator, go to the class web page and follow the link.

## Slide 200: Questions?

## Slide 201: THE END