## Slide 1: Water Quality Considerations for Treatment
Water sources
Pollution
Treatment needs

## Slide 2: Hydrological cycle

## Slide 3: Water retention in aquifers

## Slide 4: Atmospheric water
Volume of water in the atmosphere
(if condensed) ~ 3,100 mi3 or 12,900 km3
= 0.001 % of Earth's total water volume
= 0.035% of all fresh water
= 4.5% of all surface water
= 1 inch to cover all of Earth’s surface
Atmosphere: superhighway for fresh water cycle around the globe

## Slide 5
Rainfall distribution on Earth

## Slide 6: World climatic areas
World climatic areas

## Slide 7: Safe and reliable supplies of water

## Slide 8: Ensuring supplies
Not without environmental consequences

## Slide 9: Alternative water sources
Promising, yet elusive

## Slide 10: Water pollution

## Slide 11: Hypoxia

## Slide 12: Hypoxia Mississippi Delta

## Slide 13: Fertilizer and nitrogen cycle

## Slide 14: Effect of Salinity on Soils
Salinity: Sodium and Chloride
Good Salts: Calcium, Magnesium
Hold soil particles together
Problem Salts:
Sodium – soil dispersion
Chloride - toxicity
Ca++
Mg++
Na+
Sodium Absorption Ratio (SAR)

## Slide 15: Consequences of Soil Dispersion
Poor Drainage
Less infiltration of water
Increased water runoff
Less efficient leaching of salt
Loss of Soil Structure
Loss of soil pore space
Decreased oxygen
Increased soil erosion
Plant Effects
High soil bulk density
Decreased root growth
Anoxia and root death
Poor water infiltration leads to soil ponding: poor leaching,
salt accumulation, low soil oxygen, root death from
anoxia, and increased Phytophthora root rot.

## Slide 16: The effect of salinity on plants
Chloride 0.61%
Chloride 0.58%
Sodium 0.35%

## Slide 17: Environmental protection

## Slide 18: Typical water treatment process with lime softening

## Slide 19: Water reclamation

## Slide 20: Process units in water treatment
Pre-chlorination – for algae control and arresting any biological growth
Aeration – along with pre-chlorination for removal of dissolved iron and manganese and stripping volatiles
Coagulation – for flocculation
Coagulant aids, such as polyelectrolytes – to improve coagulation and for denser floc formation
Sedimentation – for initial solids separation, that is, removal of suspended solids trapped in the floc
Filtration – removing additional solids from water
Desalination – removing soluble inorganics from water
Softening – removing calcium from water
Disinfection – inactivating microbes
Adsorption – removing undesirable organic compounds

## Slide 21: Reflection
The general technologies are well developed and generalized designs are available which are used by many water utilities (public or private)
No unique solution (selection of unit processes) for any type of water
New technologies are still developed
Difficult to standardize unit processes for different water sources. Treatability studies for each source of water in different seasons required for appropriate processes.