## Slide 1: Po-Heng (Henry) Lee
SURVEY OF THE FOULING CHARACTERISTICS BETWEEN ATTACHED AND SUSPENDED SUBMERGED MEMBRANE BIOREACTOR

## Slide 2: Activated Sludge Process
Primary Clarifier
Aeration tank
Secondary Clarifier
Blower
The drawbacks of Activated Sludge Process (ASP)
Low volumetric loading rate
Large space
Slow growing bacteria (nitrifiers) are easily washed out
  At low operating temperature
  At short sludge age
Low SRT
  Foaming
  Bulking

## Slide 3: Attached Biofilm Process
Primary Clarifier
Aeration tank
Secondary Clarifier
Blower
Advantage of attached system
Achieves high biomass in the reactor through biomass attachment on the surface of media
Settling problem

## Slide 4: Carriers
Photo of (from left to right) Kaldnes type K1, K2 and K3 biofilm carriers. (Rusten et al, 2006)

## Slide 5: Membrane Bioreactor Process (MBR)
Primary Clarifier
Aeration tank
Secondary Clarifier
Blower
Characteristics of MBR
Maintains high SRT through complete retention of biomass (High SRT)
Short HRT
High quality effluent
Short footprint
Fouling

## Slide 6: Fouling formation in membrane surface

## Slide 7: Commercial Membrane
Electron micrographs of non-woven polypropylene (NWPP) and polysulphone (PS) membranes: (a) PS (0.3 mm); (b) NWPP (5 mm); (c) NWPP (3 mm); (d) NWPP (1.5 mm). (Chang, 2001)

## Slide 8: Attached MBR Process
Primary Clarifier
Aeration tank
Secondary Clarifier
Blower
Advantage of attached MBR system
Low HRT
High SRT
High quality effluent
Low fouling rate

## Slide 9: Typical attached MBR system (Lee et al., 2001)

## Slide 10: Summary of the attached membrane system operational conditions and performance
 | Lee et al., 2006 | Leiknes and Ødegaard 2007 | Melin et al., 2005 | Yang et al., 2006 | Basu and Huck 2005 | Lee et al., 2001
Influent | COD = 1,000 mg/L | COD = 7-24 gCOD/m2d (178-242 mg/L) | COD = 4.1-26.6 g COD/m2 d) | COD = 1310- 1810 mg/L | TOC =2.43-4.33 mg/L | COD = 250 mg/L
Effluent | COD < 20 mg/L | N.D. | COD < 50 mg/L | - | 1.0-2.05 mg/L | COD = 3-5 mg/L
HRT | 10 h | 45-180 min | 3.45-4 h | 7.2 | - | 8
SRT | 10 d | - | - | 50 | - | 
Flux (l/m2 h) | 25 | 20-60 | 3.3-5.6 | 4.5 | 38 | 25
TMP | < 30 kPa | 0.1-0.5 bar | 0.1-0.55 bar | 5-30kPa | 0-8 bar | 26 kPa
Medium volume fraction (%) | 5-20 | 60-70 | > 6 | 20 | 0-40 | -
Air flow rate | 5-9 L/min | - | - | 0.15 m3/h | - | 2.5 L/min
DO (mg/L) | 4.9-5.1 | - | - | - | - | 6.0-6.2
pH | 6.5-7.5 | - | - | - | - | 6.8-7.2
Working Volume (L) | 6 | - | 60 | 10 | - | 5
Suspended biomass (mg/L) | 4,500-5,500 | - | 200-800 | - | - | -
Attached biomass (mg/L) | 3,900-4,700 | - | - | - | - | -
Membrane porous size (m) | 0.1 (Polyethylene hollow fiber) | 30kD (hollow fiber) | 30kD (hollow fiber) | 0.1-0.2 polyethylene | Zenon ZW-1 membrane | 0.1 (Polyethylene hollow fiber)
Attached media | 1.3 cm Virgin polyurethane cubes coated with | 7-15 mm (Polyethylene Kaldnes K1 media) | 7-15 mm (Polyethylene Kaldnes K1 media) | 1.0 mm | - | Biomatrix (Looped cord media)
Attached media surface area (m2/m2) | 35,000 | 350 | 350 | Porosity = 90 % | 690 | 4.37m2 (Total surface area)
Temperature (oC) | 25 | - | - | - | - | 25
Surface Area (m2) | 0.1 | 0.8 | 0.8 | 0.4 | - | 0.1

## Slide 11: Case study (Lee et al., 2006)
TMP variation as a function of media volume fraction and flow rate

## Slide 12: Case study (Lee et al., 2006)
Comparison of TMP rise-up between membrane modules with and without the iron net
Comparison of cake layer formed on the membrane surface (A) with and (B) without the iron net

## Slide 13: Case study (Yang et al., 2006 and Lee et al., 2006)
SEM images of cake layers on external membrane surfaces after fouling
Analysis of bound EPS concentration in suspended flocs as a function of air flow rate and media volume fraction

## Slide 14: Conclusion
Capital cost of membrane and O & M cost
High effluent quality required to meet stringent discharge limits with the requirements of capacity treatment increase
An alternative process for shortage of land of upgrading existing water pollution control facility
Nutrient removal

## Slide 15
Questions?