## Slide 1: Environmental Biotechnology
CE421/521
Tim Ellis
October 25, 2007

## Slide 2: INDICATOR MICROORGANISMS
Need for indicator organisms
  Not possible to test for every pathogen
  Use indicator that will be easy to test routinely
  Early warning if there is a problem
  Used in regulations
    Water treatment and distribution
    Wastewater treatment discharges (NPDES permit)
    When to close beaches and lakes for recreational uses
      Beaches closed when FC is over 300 colony
      forming units per 100 mL or when monthly
      average is over 140 CFU per 100 mL

## Slide 3: INDICATOR MICROORGANISMS
Use of indicator organisms dates back to 1914 when U.S. Public Health Service adopted the c______________ test as an indication of fecal contamination
Ideal indicator should have the following characteristics:
  Found in i___________________ of warm blooded animals
  Should be present when p__________________ are present and absent when pathogens are absent
  Present in greater n___________________ than pathogens
  As r____________________ as (or more resistant than) pathogens
  It shouldn’t m__________________ in the environment
  Easily detectable by r___________, inexpensive method
  Non-p_____________________ itself
E.coli

## Slide 4: Total Coliforms
Characteristics:
  Aerobic and f___________________ anaerobic organisms
  gram n_________________
  non s_____________ forming
  r_______ shaped
  ferment l__________________ within 48 h at 35°C as evidenced by gas production
  includes E. coli, Enterobacter, Kleibsiella, and Citrobacter
  high levels in human and animal feces ______ per capita per day

## Slide 5: Fecal Coliforms
all coliforms that can ferment lactose at 44.5°C as evidenced by g________ production
includes groups such as E. coli and Kleibsiella
p________________ is an indication of human and animal contamination
human and animal contamination cannot be d_______________
s___________________ pattern is similar to bacterial pathogens
much l______ resistant to disinfection than protozoan pathogens

## Slide 6: Fecal Streptococci
includes groups such as Streptococcus faecalis, S. bovis, S. equinus, and Kleibsiella
inhabit i______________ of warm blooded animals and humans
Historically fecal coliform/fecal strep r_______ serves as useful indicator of origin of contamination
  ratios greater than 4 indicate h____________ origin
  ratios less than ________ indicate animal contamination
  In-between ratios indicate a m__________________ of human and animal contamination
  Currently there are probably better
  indicators of human contamination
  (pharmaceuticals and personal care
  products)

## Slide 7: Clostridium perfringens
Anaerobe
forms s______________ that are resistant to disinfection and environmental stress
possibly t_____ resistant to be useful as an indicator
good for tracking contamination in m__________ environments
http://chem.ch.huji.ac.il/~eugeniik/
biofuel/biofuel_cells_bacteria12.jpg

## Slide 8: Bacteriophages
Similar to enteric v___________ and found in higher numbers
Suggested as water quality indicators in e___________________, seawater, recreational waters, and drinking water
C________________ exhibit
best correlation to enteric
viruses

## Slide 9: Heterotrophic Plate Count (HPC)
Measure of aerobic and facultative anaerobic bacteria that derive their c______________ and e________________ from organic compounds
No known effects of high HPC on h____________ health
HPC in drinking water ranges from less than _____ CFU/mL to more than ____ CFU/mL
Good indicator of pathogens in r___________________ wastewater

## Slide 10: BULKING and FOAMING
Sludge settling can be the most important operational problem in an activated sludge plant
Ciliates
Nematodes
Rotifers

## Slide 11: FILAMENTOUS BULKING
Measurement of sludge settleability
Sludge v___________ index
Measure of s_____________ characteristics
Measured in a g_____________ cylinder after 30 min of settling
Units of mL/g
A d_____________ SVI is in the range of 75-150

## Slide 12: Bulking and Foaming

## Slide 13: Filamentous Bulking
Kinetic Selection Theory (Chodoba et al.

## Slide 14: Types of Filaments
filament s_________
size and shape within filament
b___________
motility (e.g. Beggiatoa move by g___________ )
presence of s_____________
presence of epiphytic b_____________ on filament surface
filament size and d__________________
presence of g_____________________

## Slide 15: Isolation of Filaments
m___________________ analysis
fluorescent-a___________________ techniques
RNA chemotaxonomy (g____________ p____________)

## Slide 16: Predominant Filaments

## Slide 17: CAUSES
Waste composition
  high c___________________
  v__________ a__________
  readily d__________________ substrates

## Slide 18: Causes
Substrate Concentration
  l_____ s__________ concentrations favor filaments due to their low KS values
Sludge Loading (Food to Microorganism Ratio)

## Slide 19: Photos of bulking organisms
Type 1701
Type 021N
Type 0041N
Thiothrix spp.
Microthrix parvicella

## Slide 20: Causes
pH
  l________ pH tends to favor filaments
Sulfide
  sulfide tends to encourage growth of s_______ f_______________ such as
    Thiothrix
    Beggiatoa
    021N
D.O.
  Sphaerotilus natans KS for oxygen is 0.01
  KS for oxygen for floc formers is 0.15

## Slide 21: BULKING CONTROL
C_________________ or O_____________________ of RAS
Biological Selector
  a______________ selector
  a______________ selector
  a_________________ selector

## Slide 22: FOAMING IN ACTIVATED SLUDGE
Types of activated sludge foams:
  s______________ a_______________ compounds
  d____________________
  s___________ (e.g., as a result of denitrification)
  actinomycetes f___________

## Slide 23: Foam Nuisance
a____________________ and safety hazard (e.g., slippery walkways)
increased levels of o_________________ c________________ in effluent
foaming in a____________________ digesters
nuisance o_______________
opportunistic p___________________ (e.g., Nocardia asteroides)

## Slide 24: Foam Microbiology
A_______________________ is the most predominant foam causing organism
N________________ is a predominant member of this classification (e.g., Gordona amarae, formerly Nocardia amarae, N. asteroides, N. pinensis, and Rhodococcus).
Gordona amarae and N. pinensis are usual suspects
foaming is problematic when Nocardia concentration exceeds ______ mg Nocardia per g VSS

## Slide 25: Mechanisms of Foam Production
Gas b__________ from aeration or denitrification assist in flotation
h_____________________ nature of cell wall assist in their transport to air-water interface
b_______________________ produced by microorganisms accelerate foaming
foaming is exacerbated by:
  l____________ SRTs (i.e., >9 d)
  w____________ temperatures (i.e., >18°C)
  wastewaters with high f_______ , o_______, and g_____________ (FOG)

## Slide 26: FOAM CONTROL
c_________________________ of foams
l____________ SRT
s________________
reduced a_______________
r__________ FOG, pH
recirculation of a_____________ d______________ supernatant
water s______________
a____________ agents
p___________________ modifications (e.g., overflow weirs)

## Slide 28
http://www.tcd.ie/Centre_for_the_Environment/watertechnology/images/17.2.jpg