## Slide 1
Matthew Fischels
Aerospace Engineering Department
Major Professor : Dr. R. Ganesh Rajagopalan
Reducing Runtime of Wind Turbine Simulation
Los Alamos National Lab
CD-adapco: STAR-CCM+

## Slide 2: CFD Intro
CFD = Computational Fluid Dynamics
Navier-Stokes Equations = Conservation of mass, momentum, & energy
Wind Turbines
  Assume incompressible (slow)
  Blade Modeling: geometry or as momentum source
Turbulence
  Directly simulate (DNS)
  Model (LES,RANS)
  Ignore (Laminar)

## Slide 3: Motivation
Current wind turbine CFD simulations require large time and computing resources

## Slide 4: Goal
Simulate a wind farm on limited computing resources in a reasonable time
  limited: a single machine or a small server?
  reasonable: a day or a week?
  How many wind turbines?

## Slide 5: How to reduce runtime?
Hardware Utilization
  Parallelization/GPU
Algorithm Development
  Develop more efficient methods for solving N-S
My goal is to reduce runtime while on limited computing resources -> Algorithm Development

## Slide 6: Algorithm Development
Runge-Kutta Methods
Multigrid Methods
Interface Flux Computations

## Slide 7: Runge-Kutta Methods
Runge-Kutta methods efficiently/accurately integrate momentum equations in time
  RK-SIMPLER Algorithm
  Explicit (computationally inexpensive)
  Implicit (stable for larger time steps)
For 2D flow over flat plate results
Method | Speedup Compared to SIMPLER (C-N)
Explicit | 5.4
Implicit | 14.0

## Slide 8: Runge-Kutta Methods
3D Isolated NREL Combined Experiment Rotor
Downwind turbine
No tower/nacelle
Uniform inflow
              SIMPLER & RK-SIMPLER results identical

## Slide 9: Runge-Kutta Methods
 | Max. Time Step | 
Wind Speed | ERK | IRK
5 m/s | 0.070 s | 0.100 s
10 m/s | 0.040 s | 0.060 s
15 m/s | 0.025 s | 0.040 s
20 m/s | 0.020 s | 0.030 s
25 m/s | 0.016 s | 0.024 s
Runtime (hours) for each wind speed and method
 | 5 m/s | 10 m/s | 15 m/s | 20 m/s | 25 m/s
ERK | 18.0 | 10.4 | 6.2 | 5.1 | 4.0
IRK | 24.4 | 16.0 | 9.4 | 7.4 | 5.9
Speedup compared to SIMPLER

## Slide 10: Runge-Kutta Methods

## Slide 11: Multigrid Methods
Iterate on multiple grid levels
  Removes errors of wave length ~ grid spacing
  Restrict to coarser grids, prolong errors to finer grids

## Slide 12: Multigrid Methods
Error (or residual) drops at a faster rate with multigrid
Multigrid speedup can be 14x or higher

## Slide 13: Interface Flux Computations
How to find a value between points?
  Linear Interpolation
  Upwind (1st Order, 2nd Order)
  Power Law
  QUICK
  Flux Corrected Method

## Slide 14: Interface Flux Computations
Power Law
QUICK

## Slide 15: Interface Flux Computations
Two ways to look at these improvements
  Can get greater accuracy on the same grid
  Can get the same accuracy on a coarser grid
Develop more accurate methods to further reduce grid requirements

## Slide 16: How will these methods interact?
Additive or Multiplicative?
  Example:
    Multigrid has speedup of 14
    RK has a speedup of 10
    Will the combination yield 24x speedup or 140x speedup?
  Probably somewhere in between
  Some combinations could be negative

## Slide 17: Questions?