## Slide 1: Increased Energy Efficiency of Permanent Magnet Generators for Wind Turbines
Helena Khazdozian
WESEP
Major Department: Electrical Engineering
Major Professor: Dr. David Jiles

## Slide 2: Outline
Problem Definition
Commercial Wind Turbines
Permanent Magnet Generators
Magnetic Materials
  Soft Magnet Materials
  Hard Magnet Materials
  Alternative Materials
Approach to Research

## Slide 3: Problem Definition
Broad Definition: Energy Crisis!
  U.S. relies on fossil fuels to generator power
  Contributes to climate change
Solution: Wind Energy
Source: O. Gutfleisc et al, Adv. Mater. 23, 2001, 821-842
Source: I. Kubiszewski, C. Cleveland, “Energy return on investment (EROI) for wind energy,” The Encyclopedia OF EARTH, 3/28/2013
Energy return on investment (EROI)
EROI =

## Slide 4: Commercial Wind Turbines
3 phase induction generators are industry standard
Require multistage gearboxes
  Gearboxes fail before designed lifetime of 20 years and account for majority of system losses
  High operation and maintenance costs
Variable speed operation is expensive
Direct drive permanent magnet generators present an efficient alternative
Need for Renewable Energy
Need for Alternative Generators
in Wind Turbines
Problem Definition

## Slide 5: Permanent Magnet Generators (PMG)
Synchronous operation
Direct drive
  Drive shaft coupled to turbine blade rotors
Rotor
  Generates field/excitation current
  Rotor disk
  Permanent magnet blocks
    Provides magnetic flux
Stator
  3 phase voltage induced in copper windings
Commercial efficiencies 85-98%

## Slide 6: Permanent Magnet Generators (PMG)
Advantages
  Elimination of gearbox
  Variable speed operation
  Higher energy yield
Disadvantages
  High torque, low speed operation
    Cogging torque
  More expensive
    Requires inverter for grid connection
    Increase in size and mass of generator with increase in output power
      Design challenge!
Need for Renewable Energy
Need for Alternative Generators
in Wind Turbines
Problem Definition
Need for Efficient PMG
with Reduced Size and Mass

## Slide 7
Efficiency Losses
  Cu losses
    I2R losses
  Fe losses
    Core losses, eddy current losses
  Rotational/mechanical losses
Can we reduce these with material choices?
Permanent Magnet Generators (PMG)

## Slide 8: Magnetic Materials
Soft magnetic materials
  High saturation magnetization, Ms
  High permeability
  Low coercivity, Hc
  Low core loss
Hard magnetic materials
  High remanence, Br
  High coercivity, Hc
  Energy Product = (BH)max

## Slide 9: Soft Magnetic Materials
Application
  Rotor disk
  Stator (steel laminations)
Types of Soft Materials
  Electrical steels
  FeNi and FeCo alloys
  Ferrites
  Amorphous metals
Reduce core loss through material choice

## Slide 10: Permanent Magnetic (PM) Materials
PMs are hard magnetic materials
Provides flux in PMG
Types of PM Materials
  Rare Earths
    Nd-Fe-B
    Sm-Co
  Non-Rare Earths
    Alnico
    Ceramics/hard ferrites

## Slide 11: Permanent Magnetic (PM) Materials
Need for Renewable Energy
Need for Alternative Generators
in Wind Turbines
Problem Definition
Need for Efficient PMG
with Reduced Size and Mass
Need to Reduce Critical
Materials in PMG
Nd-Fe-B is industry standard
  Considered a critical element by EPA
Rare earths
  China controls 97% of market
    Expensive!
  Hardrock mining results in potential environmental/human exposure to Al, As, Ba, Be, Cu, Mn, Sn, Pb
  Refining process:
    Dissolution of sulfide mineral deposits
    Dissolution of carbonate mineral deposits
    City of Boatou where 2/3 of Chinese rare earths are refined has resulted soil and groundwater contamination

## Slide 12: Permanent Magnetic (PM) Materials
Methods to reduce/eliminate critical materials
  Exchange spring magnets
  Alternative materials
Advanced Research Projects Agency – Energy (ARPA-E)
  Rare Earth Alternatives in Critical Technologies (REACT)
  Ames Laboratory
    Cerium based magnets
  Northeastern University
    Iron-nickel based supermagnets
    Manganese based magnets

## Slide 13: Approach
Choose Application:
HAWT or VAWT?
Design PMG
Magnetic Material Choice
Axial or radial?
Inner or outer rotor?
Magnet mounting?
Finite element analysis simulation using MagNet
Number of poles?
Optimize operating point and efficiency

## Slide 14: Questions?