## Slide 1: Wind Turbine NDE
Jeremy Van Dam

## Slide 2: Levelized Cost of Energy
LCOE = the average lifetime levelized cost of electricity generation
It = investment expenditures in the year t;
Mt = operations and maintenance expenditures in the year t;
Ft = fuel expenditures in the year t;
Et = electricity generation in the year t;
r = discount rate; and
n = economic life of the system.
(RENEWABLE ENERGY TECHNOLOGIES: COST ANALYSIS SERIES, 2012)

## Slide 3: Levelized Cost of Energy
(RENEWABLE ENERGY TECHNOLOGIES: COST ANALYSIS SERIES, 2012)

## Slide 4: Levelized Cost of Energy

## Slide 5: Reduce Operation and Maintenance Costs
Chart: U.S. Average levelized costs for plants entering service in 2018
| Conventional Coal | Advanced Coal with CCS | Natural Gas-Fired Conventional Combined Cycle | Natural Gas-Fired Advanced CC with CCS | Advanced Nuclear | Geothermal | Biomass | Wind | Wind-Offshore | Solar PV1 | Solar Thermal | Hydro2
Fixed O&M | 4.1 | 8.8 | 1.7 | 4.1 | 11.6 | 12 | 14.3 | 13.1 | 22.4 | 9.9 | 41.4 | 4.1
Table: (Levelized Cost of New Generation Resources in the Annual Energy Outlook 2013, 2013)

## Slide 6: Reduce Operation and Maintenance Costs
The fixed and variable operations and maintenance (O&M) costs are a significant part of the overall LCOE of wind power. O&M costs typically account for 20% to 25% of the total LCOE of current wind power systems.
                (EWEA, 2009)

## Slide 7: Turbines are Getting Bigger

## Slide 8: Turbines are Getting Bigger
Source: NREL. (Lantz, Hand, & Wiser, 2012)

## Slide 9: The state-of-the-art

## Slide 10: State-of-the-art
Nacelle Monitoring
  Displacement Monitoring
  Temperature Monitoring
  Vibration Censors
  Accelerometers
Ludeca, Inc
The green arrows indicate sensor (accelerometer) locations for standard wind turbines.

## Slide 11: State-of-the-art
Blade Monitoring
  Strain Gauges
  Fibre Bragg Grating
    Offer physical correlation between wavelength and strain
    Long term stability and no recalibration required
    Limited number of sensors
P.J. Schubel et al. / Renewable Energy 51 (2013) 113e123

## Slide 12: State-of-the-art
Blade Monitoring
  Strain Gauges
  Electrical Sensors
    Require Large Sensor arrays
    Stress Field is required
    Applicable in Operation
    Mature technology
P.J. Schubel et al. / Renewable Energy 51 (2013) 113e123

## Slide 13: State-of-the-art
Blade Monitoring
  Strain Gauges
  Acoustic Emissions
    Crack initiation
    Breaking of Fibers
    Few Sensors needed
    High levels of Noise
Integrity Diagnostics

## Slide 14: State-of-the-art
Blade Monitoring
  Strain Gauges
  Acoustic Emissions
  Ultrasonic
    Reveals certain flaws quickly
    Scattering effect has a negative impact
National Instruments

## Slide 15: State-of-the-art
Blade Monitoring
  Strain Gauges
  Acoustic Emissions
  Ultrasonic
  Thermography
    Record Temperature differences – identify flaws
Condition monitoring and fault detection of
wind turbines and related algorithms (Hameed)

## Slide 16: Turbine Blade
Windpower: Engineering & Development

## Slide 17: Turbine Blade
Cracking
  Typical blade damage
Study of fatigue failure damage
in wind turbine blades (Marin)

## Slide 18: Turbine Blade
Out-of-Plane Waviness
  Reduces Structural
  integrity
Iowa State University

## Slide 19: Turbine Blade
Custom created hole for testing
Joint Failure
  De-bonding
  Lack of Resin
  Cracking
Iowa State University

## Slide 20: Turbine Blade
Iowa State University

## Slide 21: Turbine Blade
Iowa State University

## Slide 22: Future Work
Determine Method of NDE
  What are the areas of need?
  Combine multiple methods?
Determine Failure Mode
  How to actively monitor for the Failure

## Slide 23: Related Work
Wind Turbine Reliability
  Keep the wind turbine functioning when the wind is blowing
  Avoid critical failures
Reduce Wind Turbine Costs
  Reduce the O & M costs
  Manage downtimes